## Slide 1: Analysing Dual Stack Behaviour and IPv6 Quality
Geoff Huston & George Michaelson
APNIC

## Slide 2: Dual Stack Behaviour
What does a browser do in a dual stack environment?
Is this behaviour better – or worse – than comparable behaviour in a IPv4-ony world?

## Slide 3: Dual Stack Behaviour: V1.0
Unconditional preference for IPv6 over IPv4
If the local client has an active IPv6 interface then:
  Perform two DNS queries: A and AAAA record queries
  Wait for both to complete
  If the AAAA query succeeds then initiate the browser connection using IPv6
  If there is no AAAA record then initiate the browser connection using IPv4

## Slide 4: Dual Stack Failure: V1.0
What if the IPv6 SYN does not elicit a response?
Then you fall back to use IPv4
How long will you wait before you fall back?
Windows: 3 SYN packets, 19 seconds
Mac OS X 6.8 and earlier: 11 SYN packets, 75 seconds
Linux: >= 11 SYN packets, between 75 to 180 seconds
Obviously, this sucks!

## Slide 5: Dual Stack Behaviour: V2.0
Add Local Preference Rules:
  unicast IPv6
  unicast IPv4
  6to4 tunneled IPv6
  Teredo IPv6
The effect of this preference table is that if the local IPv6 interface is an auto-tunneled interface than it will only be used when there is no local unicast IPv6 interface and the remote site is IPv6-only

## Slide 6: Dual Stack Failure: V2.0
What if the IPv6 SYN does not elicit a response?
Then you fall back to IPv4
How long will you wait before you fall back?
Windows: 3 SYN packets, 19 seconds
Mac OS X 6.8 and earlier: 11 SYN packets, 75 seconds
Linux: >= 11 SYN packets, between 75 to 180 seconds
i.e. no change – this still sucks.
If you are behind a broken V6 connection, your life is still abject misery!

## Slide 7: Dual Stack Behaviour: V2.5 Windows Vista and 7
While Vista and 7 has IPv6 on by default, if the system is behind a NAT the IPv6 interface is a auto-configured as a Teredo auto-tunnel interface
The modified behaviour is that these systems will not even query the DNS for a AAAA record if the only local IPv6 interface is a Teredo interface
  i.e. the Teredo interface is only used when there is no precursor DNS lookup (e.g. use of IPv6 address literal form of URL)

## Slide 8: Dual Stack Behaviour: V2.5
Add Local Preference Rules:
  unicast IPv6
  unicast IPv4
  6to4 tunneled IPv6
  Teredo IPv6
The effect of this is that if the Windows box is behind a NAT and does not have a unicast V6 connection then it shows IPv4-only behaviours

## Slide 9: All this is broken!
When the network sucks, this form of browser behaviour makes it suck even more!
These serialized approaches to dual stack connectivity really don’t work well when there is a connection failure.
The technique used to identify a failure falls back to a timeout – and this can be frustrating to the user if a default OS-provided timeout is used

## Slide 10: We need better failures!

## Slide 11: We need better failures!
Altering the local preference rules may alter the chances of encountering a failure, but does not alter the poor method of determining when you have failed
The fine print: The real problem here is that the assumption behind the TCP connection code in most operating systems was that there was no fallback – you either connected to a given address or you report failure. To provide a behaviour that was robust under adverse network conditions the OS connection code is incredibly persistent (up to 3 minutes In the case of Linux default). But to use this same code in the circumstance where you have alternate connection possibilities is just testing the user’s patience. So we need to rethink this and use a connection strategy that tests all possibilities in a far shorter elapsed time.

## Slide 12
Start with one horse
How to conduct a two horse race...

## Slide 13
Start with one horse
If it dies on way then
send off the other
horse!
How to conduct a two horse race...

## Slide 14
You can fire off both horses
at once and go with whichever is fastest...
How to conduct a two horse race...
Or...

## Slide 15: Dual Stack Behaviour: V3.0 Safari and Mac OSX 10.7 and later
Moderately Happy Eyeballs:
Determine the preference between IPv4 and IPv6 by maintaining a running performance metric of per-protocol average RTT to each cached destination address
When DNS queries return both A and AAAA records initiate a connection using the protocol with the lowest current average RTT

## Slide 16: Dual Stack Failure: V3.0 Safari and Mac OSX 10.7 and later
If the connection is not established within the RTT estimate time interval then fire off a connection attempt in the other protocol
  i.e. use a very aggressive timeout to trigger protocol fallback

## Slide 17: Dual Stack Failure: V3.0 Safari and Mac OSX 10.7 and later
If the connection is not established within the RTT estimate time interval then fire off a connection attempt in the other protocol
  i.e. use a very aggressive timeout to trigger protocol fallback

## Slide 18: Dual Stack Failure: V3.0 Safari and Mac OSX 10.7 and later
If the connection is not established within the RTT estimate time interval then fire off a connection attempt in the other protocol
Only when you have tried ALL the addresses in the first protocol family, then flip over to the other protocol

## Slide 19: Dual Stack Failure: V3.0 Safari and Mac OSX 10.7 and later
If the connection is not established within the RTT estimate time interval then fire off a connection attempt in the other protocol
Only when you have tried ALL the addresses in the first protocol family, then flip over to the other protocol
Multi-addressing a critical service point in dual stack situations can make it look worse to clients, not better!

## Slide 20: Dual Stack Behaviour: V3.1 Chrome Browser
Happyish Eyeballs:
Fire off the A and AAAA DNS queries in parallel
It’s a DNS race: Initiate a TCP connection with the first DNS response
If the TCP connection fails to complete in 300ms then start up a second connection on the other protocol

## Slide 21: Dual Stack Behaviour: V3.2 Firefox and Fast Failover
Happier Eyeballs:
Fire off the A and AAAA DNS Queries
Initiate a TCP connection as soon as the DNS response is received
It’s a SYN race: Use the first connection to complete the SYN-ACK handshake for data retrieval
Close off the other connection

## Slide 22: The bigger picture...
http://www.potaroo.net/ispcol/2011-12/esotropia.html
Failover Timer Values
Protocol Preference Setting

## Slide 23: The bigger picture...
http://www.potaroo.net/ispcol/2011-12/esotropia.html

## Slide 24: Why?
Why add all this parallel complexity to browser behaviour?
What was wrong with the initial concept of “prefer IPv6 if you can, use IPv4 otherwise”?
Is there really any difference in performance between IPv6 connections?
Lets see...

## Slide 25: Measuring Dual Stack Quality
Enlist a large set of dual stack clients to connect to an instrumented server using both IPv4 and IPv6
  Equip a number of web sites with a javascript module that poses a number of image-blot retrieval tests
  Extended this using Flash to embed the same tests in a Google Image Ad*
Thank you to Google,
RIPE NCC & ISC for
your assistance to conduct
this experiment!

## Slide 26
We are currently performing 400K – 500K connection tests per day
Web Scripts
Embedding tests in Ads
Test Volume – Number of unique tests performed per day
2010
2011
2012

## Slide 27: Measuring Dual Stack Quality
Enlist a large set of dual stack clients to connect to an instrumented server using both IPv4 and IPv6
  For each successful connection couplet gather the pair of RTT measurements on the SYN-ACK exchanges
  Gather connection failure statistics (where a “failure” is defined as a received SYN, but no followup ACK)

## Slide 28: Connection Failure
Outbound SYN
Busted SYN ACK
Return path

## Slide 29: Measuring Failure

## Slide 30: Relative Connection Failure Rates
Why is this failure rate for V6
so incredibly high?

## Slide 31: Relative Connection Failure Rates
And why is the V4 relative failure rate dropping over time?
What is this spike?

## Slide 32: What is going on with IPv4?

## Slide 33: What is going on with IPv4?
The failure rate for V4 decreases as the volume of experiments increases – which implies that the number of “naked SYNs” being sent to the servers is not related to the number of tests being performed.
Aside from residual IPv4 failures in the image fetch due to device resets, connection dropouts, etc, the bulk of the recorded failures here is probably attributable to bots doing address scanning on port 80

## Slide 34: What is going on with IPv4?
Syn Flood Attacks
bot scanning on port 80?

## Slide 35: What about IPv6?
Local Miredo Relay Failures
Why is the base failure rate
of all IPv6 connections sitting
at 40%? This is amazingly bad!

## Slide 36: V6 Failure Rate by Address Type
All V6 Average
Teredo
6 to 4
Unicast

## Slide 37: Teredo Failures
Teredo connections use a 2-step connection process:
  An ICMP exchange to establish the form of local NAT behaviour (full cone, port restricted cone, ...) and to set up the symmetric path
  A TCP 3-way handshake
There are 2 failure modes:
  ICMP seen, no SYN
  ICMP seen, SYN seen, no ACK

## Slide 38: Teredo Failure Rate
ICMP Exchange fails to complete
ICMP completed, but SYN Exchange fails to complete

## Slide 39: It’s NAT Traversal Failure
Teredo failure is around 40% of all connection attempts
  Obviously, this is unacceptably high!
  This is unlikely to be local filtering effects given that Teredo presents to the local NAT as conventional IPv4 UDP packets
  More likely is the failure of the Teredo protocol to correctly identify the behaviour mode of the local NAT device

## Slide 40: Working with Failure
A 40% connection failure is unworkable is almost all circumstances
But one particular application can thrive in this environment, and makes use of Teredo addresses: Torrents
  Not many DPI interceptors are sensitive to V6 in V4 UDP encap
  The massive redundancy of the data set across multiple sources reduces the sensitivity of individual session failures

## Slide 41: 6to4 Auto-tunnelling
6to4 Auto-tunnelling technique
  Cannot operate through IPv4 NATs
  Relies on third party relays in BOTH directions
  Asymmetric traffic paths
  Some of the performance problems can be mitigated by placing the reverse 6to4 relay into the V6 service point

## Slide 42: 6to4 Failure Rate
ASIA
US
EU

## Slide 43: 6to4 Failure is Local Failure
6to4 failure appears to be related to two factors:
  The client’s site has a protocol 41 firewall filter rule for incoming traffic (this is possibly more prevalent in AsiaPac than in Europe)
  Load / delay / reliability issues in the server’s chosen outbound 6to4 relay (noted in the data gathered at the US server)
Even so, the 10% to 20% connection failure rate for 6to4 is unacceptably high!

## Slide 44: V6 Unicast Failures
January – March 2012:
  110,761 successful V6 connecting endpoints
  6,227 failures
  That’s a failure rate of 5.3%!
  7 clients used fe80:: link local addresses
  7 clients used fc00:/7 ULA source addresses
  2 clients used fec0::/16 deprecated site local addresses
  16 clients used 1f02:d9fc::/16
  Nobody used 3ffe::/16 prefixes!
  What about the other 6,195 clients?

## Slide 45: Unicast IPv6 Failures
8 were using unallocated unicast V6 addresses
66 were using unadvertised unicast V6 addresses
6,116 were using V6 addresses drawn from conventional advertised V6 prefixes!
Local inbound filters appear to be a common problem in IPv6

## Slide 46: Where does V6 Fail?
Highest:
Spain – 18%
Vietnam – 16%
Indonesia – 13%
Hong Kong – 10%
Canada – 10%
Sweden – 10%
Brazil – 6%
United States – 6%
Lowest:
Norway – 0.2%
Australia – 0.7%
France – 0.8%
Russia – 1.7%
Italy – 2%
China – 3%
Germany – 3%
Japan – 4%
Average - 5.3% of unicast V6 connections fail to complete
However, we saw wide variance across countries:

## Slide 47: Measuring Dual Stack Quality
For each successful connection couplet gather the pair of RTT measurements on the SYN-ACK exchanges
  Use the server’s web logs to associate a couplet of IPv4 and IPv6 addresses
  Use the packet dumps to collect RTT information from the SYN-ACK Exchange

## Slide 49
IPv6 is slower
IPv6 is faster
RTT Difference (in fractions of a second)
Number of samples (log scale)
Teredo
6 to 4
Unicast

## Slide 50
This is unexpected!
Europe-located Server

## Slide 51: Why is Teredo slower?
The technique used here is to measure the interval between the first received SYN and the first received ACK
  But something is happening with Teredo
    we use inbuilt Teredo Relays, so the Teredo RTT should precisely match the IPv4 RTT
      But we are measuring the initial SYN exchange
      It appears that there are some major setup delays in Teredo that are occurring in the initial SYN ACK exchange
      The performance of CPE based NATs has a massive tail of delay, woe and abject misery!

## Slide 52
This is unexpected!
Europe-located Server

## Slide 53: Why is V6 faster in some cases?
We see some sessions that have faster V6 RTTs than their paired IPv4 counterpart
  Because IPv6 is faster?
    This is possible – there are some strange IPv4 paths out there
    But why would a Teredo SYN exchange be faster than a native IPv4 SYN exchange?
  Becuase IPv4 is slower?
    Is this related to the behaviour characteristics of some CPE based NATs and their handling of NAT bindings during a a SYN exchange?

## Slide 54
Australia-located Server
Huh?
Huh?
Huh?

## Slide 55
Australia-located Server
Huh?
The server’s V6 routing transit is not always optimal
And nor is V4 transit optimal in some cases
There are 6to4 delay peaks at 40ms and 150ms
And the long tail of Teredo slowness
Huh?
Huh?

## Slide 56
US-located Server
Remote outbound
6to4 relay

## Slide 57
Use of local outbound
6to4 relay has
reduced this skew
US-located Server

## Slide 58: Observations
Is IPv6 as fast as IPv4?
  If you are native in IPv6, then, yes!
  The use of tunnels and overlays can make this worse in some cases, but, in general, V6 is as fast as V4

## Slide 59: Observations
Is IPv6 as robust as IPv4?
  Sadly, No
  The base failure rate of V6 connection attempts at 5% of the total V6 unicast traffic volume is simply unacceptable as a service platform
  But its not in the core network. It appears that this is mainly self-inflicted with local edge firewall filter settings that trap V6 packets

## Slide 60: How Should Browsers Behave?
One view is to place both protocols on equal footing in a parallel connection environment, using a “SYN-ACK race” with parallel DNS and TCP session establishment
  E.g. Firefox with fast retransmit
Or reduce the server load by using a “DNS race” and take whichever answers first, but prepare for failover using a very aggressive timeout
  E.g. Chrome with 300ms failover timer
Or use local heuristics to estimate which is faster and failover within 1 RTT interval
  E.g. Safari + Mac OS X >= 10.7

## Slide 61: How Should Browsers Behave?
One view is to place both protocols on equal footing in a parallel connection environment, using a “SYN-ACK race” with parallel DNS and TCP session establishment
  E.g. Firefox with fast retransmit
Or reduce the server load by using a “DNS race” and take whichever answers first, but prepare for failover using a very aggressive timeout
  E.g. Chrome with 300ms failover timer
Or use local heuristics to estimate which is faster and failover within 1 RTT interval
  E.g. Safari + Mac OS X >= 10.7
None of these are that bad – they are all very fast. The trade off is slightly higher number of connections with the server against speed and robustness of the session

## Slide 62: But it’s still not enough!
Many access providers see their immediate future as having to
deploy IPv6 across their infrastructure, and at the same time field CGNs
But how $big$ does the CGN need to be?
  Generically, the CGN needs to be as big as the residual preference for using IPv4 in dual stack scenarios
So how can we help this story along?

## Slide 63: How Should Browsers Behave?
  Fire off the DNS queries in parallel
  If the DNS returns AAAA and A records, fire off a V6 connection attempt first
  Use a reasonably aggressive fallback timer to trigger V4 connection
    E.g. Chrome with 300ms failover timer
    E.g. Safari + Mac OS X with RTT-derived timer

## Slide 64: How Should Browsers Behave?
  Fire off the DNS queries in parallel
  If the DNS returns AAAA and A records, fire off a V6 connection attempt first
  Use a reasonably aggressive fallback timer
    E.g. Chrome with 300ms failover timer
    E.g. Safari + Mac OS X with RTT-derived timer
“Biased, but still Pleasantly Amused Eyeballs”!

## Slide 65
Thank You
Questions?
labs