## Slide 1: Open Life in a Post IPocalyptic Network
Scribblings by Geoff Huston. APNIC

## Slide 2
The mainstream telecommunications industry has a rich history
Time Switching
FDM
Submarine Cables

## Slide 3
The mainstream telecommunications industry has a rich history
…of making some really poor technology choices

## Slide 4
The mainstream telecommunications industry has a rich history
…of making very poor
technology guesses
and regularly being
taken by
surprise!

## Slide 5: The Internet...
Has been a runaway success that has transformed not just the telecommunications sector, but entire social structures are being altered by the Internet!

## Slide 6: The Internet...
Has been a runaway success that has transformed not just the telecommunications sector, but entire social structures are being altered by the Internet!
And now we’ve used up most of the original pool of IP addresses!

## Slide 7: The Internet...
And now we’ve used up most of the original pool of IP adresses!
Has been a runaway success that has transformed not just the telecommunications sector, but entire social structures are being altered by the Internet!
This is should not be news – we’ve known about
this looming IPocalypse for the past twenty years!

## Slide 9: IETF Meeting – August 1990

## Slide 10: IETF Meeting – August 1990

## Slide 11: What did we do back in 1992?

## Slide 12: What did we do back in 1992?
We bought some time by removing the CLASS A, B, C address structure from IP addresses

## Slide 13: What did we do back in 1992?
NSFNET
A&R networks
CIDR
Class-full
We bought some time by removing the CLASS A, B, C address structure from IP addresses
Which seemed to work
pretty well!

## Slide 14: What else did we do back in 1992?
And we started working on a new Internet Protocol – to become IPv6 - to replace IPv4

## Slide 15: What else did we do back in 1992?
And we started working on a new Internet Protocol – to become IPv6 - to replace IPv4
We left the task of transition until after we had figured out what this new protocol would look like

## Slide 16: What else did we do back in 1992?
We developed some new middleware – an address sharing protocol that worked for TCP and UDP: NAT (RFC 1631)
“It is possible that CIDR will not be adequate to maintain the IP
Internet until the long-term solutions are in place. This memo
proposes another short-term solution, address reuse, that complements
CIDR or even makes it unnecessary.”

## Slide 17: zzzzzz ...
For a long while this did not look to be an urgent problem...

## Slide 18: CIDR + NATs just worked!
NSFNET
A&R networks
CIDR + NAT
Class-full

## Slide 19: Meanwhile, we continued to build (IPv4) networks
NSFNET
A&R networks
CIDR
Boom & Bust
Broadband
Mobiles
NATs

## Slide 20: The rude awakening
Until all of a sudden the IPv4 address piggy bank was looking extremely empty...

## Slide 21: IPv4 Address Allocations
NSFNET
A&R networks
CIDR
Boom & Bust
Exhaustion!
Broadband
Mobiles

## Slide 22
Going...

## Slide 23
Going...
Going...

## Slide 24
Oh shit!

## Slide 25: Panic?

## Slide 26: AsiaPac: Panic.

## Slide 27: Europe: Distracted.

## Slide 28: America: Confused.

## Slide 29: Numerology
Lets look at the IPv4 allocation statistics

## Slide 30: IPv4 Allocations in APNIC
2010: 146 IPv4 allocations / week
2011: 168 IPv4 allocations / week
2012: 166 IPv4 allocations / week
The allocation rate has been pretty constant for the past 3 years!
Is this a work to rule at APNIC?
Or some underlying business dynamic?
Why is this production profile steady at 20 allocations per working day?

## Slide 31: All RIRs
Year
Allocated Addresses
IPv4 Allocated Addresses: 2005 - 2012
2010 – 248m
2012 – 114m

## Slide 32: Top 10 Countries, 2009-2012

## Slide 33: Largest Allocations in 2011
30% of the addresses
18 Carriers -->

## Slide 34: Choices, Choices
If you are in AsiaPac, and you need IP addresses...
what are you going to do?

## Slide 35: Choices, Choices
Apply for a FINAL allocation of 1,024 IPv4 addresses
Apply for an IPv6 allocation
Buy addresses someone who has some addresses to sell
Carrier IPv4 NATs

## Slide 36: Choices, Choices
Apply for a FINAL allocation of 1,024 IPv4 addresses
Apply for an IPv6 allocation
Buy addresses someone who has some addresses to sell
Carrier IPv4 NATs
That’s not a lot of addresses! It is only really useful for small end sites and/or NATs

## Slide 37: Choices, Choices
Apply for a FINAL allocation of 1,024 IPv4 addresses
Apply for an IPv6 allocation
Buy addresses someone who has some addresses to sell
Carrier IPv4 NATs
That’s not a lot of addresses!

## Slide 38: Measuring IPv6
That’s not a lot of IPv6!
% of the Internet’s systems
who are using IPv6

## Slide 39: Choices, Choices
Apply for a FINAL allocation of 1,024 IPv4 addresses
Apply for an IPv6 allocation
Buy addresses someone who has some addresses to sell
Carrier IPv4 NATs
That’s not a lot of addresses!
This won’t connect you to the IPv4 Internet.
An IPv6-only network without any form of IPv4
mapping or translation capability is a pretty
lonely and useless network today!

## Slide 40: Choices, Choices
Apply for a FINAL allocation of 1,024 IPv4 addresses
Apply for an IPv6 allocation
Buy addresses someone who has some addresses to sell
Carrier IPv4 NATs
That’s not a lot of addresses!
This won’t connect you to the IPv4 Internet

## Slide 41
Registry Address Exhaustion
Address Markets Stats
Number of Transfers/Sales per month

## Slide 42
Registry Address Exhaustion
Address Markets Stats
Number of Transfers
Volume of Transfers/Sales

## Slide 43: Choices, Choices
Apply for a FINAL allocation of 1,024 IPv4 addresses
Apply for an IPv6 allocation
Buy addresses someone who has some addresses to sell
Run up V4 more NATs
That’s not a lot of addresses!
This won’t connect you to the IPv4 Internet
This is not being widely used. It does not appear to be taken up by ISPs in the region. Supply is limited and costs are volatile

## Slide 44: Choices, Choices
Apply for a FINAL allocation of 1,024 IPv4 addresses
Apply for an IPv6 allocation
Buy addresses someone who has some addresses to sell
Carrier IPv4 NATs
That’s not a lot of addresses!
This won’t connect you to the IPv4 Internet
This is not being widely used
The Goldilocks Option!

## Slide 45
Edge NAT
Carrier NAT
Internet
Access Net
Edge Net

## Slide 46
Edge NAT
Carrier NAT
Internet
Access Net
Edge Net
Why is this CGN model so attractive?
Incrementally deployable
No coordination of actions
Applications are unaltered
Carrier infrastructure unaltered
Relatively low marginal cost

## Slide 47
Edge NAT
Carrier NAT
Internet
Access Net
Edge Net
Downsides of the CGN model?
HTTP will work
  But parallelism will not
UDP will work
  But UDP behaviour will be erratic
Not much else will work
Which places severe restrictions on how applications operate across the network
And impacts the current model of network service provision

## Slide 48
Back to networking basics....

## Slide 49
The historical vertically integrated service architecture
Telco nostalgia...

## Slide 50
Devolution of the integrated
service architecture through
an open IP service architecture
and deregulation

## Slide 51
Devolution of the integrated
service architecture
Where’s the money to invest
in new network services?

## Slide 52
Users
Services
Access Provider

## Slide 53
Users
Services
C
G
N
Access Provider
Gatekeeper

## Slide 54
Users
Services
G
L
A
CGNs and ALGs and similar IPv4 rationing middleware devices provide control points in the IPv4 network that allow monetary extraction from both consumers and content providers
Access Provider

## Slide 55: Where are we headed?

## Slide 56: Where are we headed?
The Internet pulled apart content from carriage, and enforced this with concepts of “network neutrality”
Content folk have thrived
Carriage folk are claiming otherwise

## Slide 57: Where are we headed?
The Internet pulled apart content from carriage, and enforced this with concepts of “network neutrality”
Content folk have thrived
Carriage folk are claiming otherwise
But now that we’ve exhausted V4 addresses this separation of carriage and content roles is being questioned by the ISP carriers

## Slide 58
New York Times: 15 January 2013

## Slide 59
Korea, February 2012

## Slide 60: So What?

## Slide 61: Why did the Internet Work?
Openness
Agility
Minimalism
Efficiency

## Slide 62: Why did the Internet Work?
Openness
Agility
Minimalism
Efficiency
Proprietary Systems
Inflexibility
Complexity
Cost
won’t

## Slide 63: What’s Left?
/etc/protocols:
TCP, bits of UDP,
and nothing else!

## Slide 64: What’s Left?
/etc/services:
HTTPs over TCP is the last remaining bastion of end-to-end coherency in today’s Natted net!

## Slide 65: What does this imply about open networking?
Openness is difficult to sustain in a restricted environment dominated by scarcity – the space for innovation is limited and open spaces are consumed by incumbents

## Slide 66: So we need to chose carefully!
We need to think about how to build a post-PC world where content, computation, storage and communications are sustainable abundant and openly available commodities.
This objective is basically incompatible with the current momentum of the Internet

## Slide 67: And its not yet clear which path the Internet will take!

## Slide 68: And its not yet clear which path the Internet will take!
market forces

## Slide 70: Thank You!