## Slide 1: That 512K Route Thing
Geoff Huston
APNIC

## Slide 2: 12 August 2014
Newborn Panda Triplets in China
Rosetta closes in on comet 67P/Churyumov-Gerasimenko
World Elephant Day

## Slide 3
The Internet apparently has a bad hair day

## Slide 4: What happened?

## Slide 5: Someone sneezed all over BGP!

## Slide 6: Who was that?
Verizon Route Leak (AS701)

## Slide 7: But route leaks happen all the time
Why was this one so different from the rest?

## Slide 8: But route leaks happen all the time
Firstly, its because the leaker was AS 701
  AS701 is a tier 1 ISP
  So very few networks (noone?) filters what they hear from AS701
  Which means that when AS701 leaks all non-default AS’s (and a few more besides) are likely to see the route leak
So everybody saw this route leak!

## Slide 9: But route leaks happen all the time
Secondly because it caused the routing table to exceed 512K entries for many networks
  It leaked 27,000 more specifics
  And most non-default BGP speakers were carrying between 490,000 and 510,000 entries in this table
  So many BGP environments exceeded 512K IPv4 entries for the first time
  And for some routers 512K is a magic number!

## Slide 10
http://www.cisco.com/c/en/us/support/docs/switches/catalyst-6500-series-switches/116132-problem-catalyst6500-00.html
http://www.brocade.com/downloads/documents/html_product_manuals/NI_05600_ADMIN/wwhelp/wwhimpl/common/html/wwhelp.htm#context=Admin_Guide&file=CAM_part.11.2.html
Cisco Cat 6500
Brocade NetIron XMR
512K is a default constant
in some of the more mature
Cisco and Brocade products

## Slide 11: Minute by Minute ANNces & WDLs

## Slide 12: Second by Second

## Slide 13: Second by Second
07:49.15 Table exceeds 512K
07:49:45 First set of withdrawals
07:49:58 Second set of announcements
07:50:20 Third set of announcements
07:52:04 Fourth set of announcements
07:52:46 Second wave of Withdrawals start
07:58:20: All done

## Slide 14: What happens then?
Crash and reboot?
Crash and die?
Push excess routes to slow path?
Discard excess routes
Did anyone crash and die?
Was there any evidence of dropped routes?

## Slide 15: Dropped Routes?
Net change of -450 routes

## Slide 16: Maybe there’s more…

## Slide 17: Collateral Damage
Outside of AS701, a further ~4,424 routes were withdrawn for some period of between 07:47 and 12:00
Some of these were probably part of the route leak as they appeared to be part of the Verizon enterprise structure.
But there were others who were clearly unrelated to Verizon…

## Slide 18: Collateral Damage
Up to 896 Origin ASes were possibly affected
AS Pfxs AS Name
9658 435 ETPI-IDS-AS-AP Eastern Telecoms Phils., Inc.,PH
7046 1 77 RFC2270-UUNET-CUSTOMER - MCI Communications Services, Inc. d/b/a Verizon Business,US
6648 132 BAYAN-TELECOMMUNICATIONS Bayan Telecommunications, Inc.,PH
23498 77 CDSI - COGECODATA,CA
21332 61 NTC-AS OJSC "Vimpelcom",RU
27882 60 Telefonica Celular de Bolivia S.A.,BO
131222 59 MTS-INDIA-IN 334,Udyog Vihar,IN
8402 56 CORBINA-AS OJSC "Vimpelcom",RU
30036 55 MEDIACOM-ENTERPRISE-BUSINESS - Mediacom Communications Corp,US
46805 54 CACHED - CachedNet LLC,US
6459 49 TRANSBEAM - I-2000, Inc.,US
18025 45 ACE-1-WIFI-AS-AP Ace-1 Wifi Network,PH
45664 42 LBNI Liberty Broadcasting Network Inc,PH
55465 41 TTT-AS-AP TT&T Co., Ltd., Bangkok.,TH
15085 38 IMMEDION - Immedion, LLC,US
16058 37 Gabon-Telecom,GA
27229 35 WEBHOST-ASN1 - Webhosting.Net, Inc.,US
21284 33 VIVODI-AS ON S.A.,GR
13188 33 BANKINFORM-AS CONTENT DELIVERY NETWORK LTD,UA
23606 33 BELLTELECOM-PH-AS-PH Bell Telecommunication Philippines,PH
35017 32 SWIFTWAY-AS Swiftway Sp. z o.o.,GB
7018 31 ATT-INTERNET4 - AT&T Services, Inc.,US
15467 31 ENTERNET-LIBERCOM-AS Enternet 2001 Ltd., Hungary,HU
50576 30 KRASNET-UA-AS Krasnet ltd.,UA

## Slide 19: But then it happened again!
BGP FIB Size
A second time!
Verizon Leak!

## Slide 20: But was this just me or everyone?
Was this general background level of routes passing 512 something that every BG{ speaker observed on the 12th August?
Or was this something unique to me (AS131072)?

## Slide 21: There is no Routing God!
There is no single objective “out of the system” view of the Internet’s Routing environment.
BGP distributes a routing view that is modified as it is distributed, so every eBGP speaker will see a slightly different set of prefixes, and each view is relative to a given location
When we look at some of the route collector sites we see a variance of ~20,000 routes across the routing peer set

## Slide 22: Route Views Peers
12 August
512K
10 October

## Slide 23: For most networks…
(probably including yours) the 12th August route leak pushed the network route count over 512K for a brief period
within an hour it all went back under again
But later on the IPv4 BGP table would pass over this threshold and not go back under again

## Slide 24: Passing 512K

## Slide 25: For most networks…
And what’s next?
How quickly is the routing table growing?

## Slide 26
1994: Introduction of CIDR
2001: The Great Internet Boom and Bust
2005: Broadband to the Masses
2009: The GFC hits the Internet
2011: Address Exhaustion
20 years of Routing the Internet

## Slide 27: IPv4 BGP Prefix Count 2010 - 2014

## Slide 28: How can the IPv4 network continue to grow when we are running out of IPv4 addresses?
We are now recycling old addresses back into the routing system

## Slide 29: IPv4 Address Reuse
50% of new addresses in 2014 were more than 1 year old
20% of new addresses in 2010 were more than 1 year old
18% of new addresses in 2014 were more than 20 years old

## Slide 30: IPv4 in 2014 – Growth is Slowing (slightly)
Overall IPv4 Internet growth in terms of BGP is at a rate of some ~9%-10% p.a.
Address span growing far more slowly than the table size (although the LACNIC runout in May caused a visible blip in the address rate)
The rate of growth of the IPv4 Internet is slowing down (slightly)
  Address shortages
  Masking by NAT deployments
  Saturation of critical market sectors
  Transition uncertainty

## Slide 31: IPv6 BGP Prefix Count
World IPv6 Day

## Slide 32: IPv6 in 2013
Overall IPv6 Internet growth in terms of BGP is 20% - 40 % p.a.
  2012 growth rate was ~ 90%.
If these relative growth rates persist then the IPv6 network would span the same network domain as IPv4 in ~16 years time

## Slide 33: What to expect

## Slide 34: BGP Size Projections
For IPv4 this is a time of extreme uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of any after-market in IPv4 on the routing table
  which makes this projection even more
  speculative than normal!

## Slide 35: V4 - Daily Growth Rates

## Slide 36: V4 - Relative Daily Growth Rates

## Slide 37: V4 - Relative Daily Growth Rates

## Slide 38: IPv4 BGP Table Size predictions
Jan 2013 441,172 entries
2014 488,011
2015 529,806
2016 580,000
2017 620,000
2018 670,000
2019 710,000
2020 760,000
These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.

## Slide 39: IPv6 Table Size

## Slide 40: V6 - Daily Growth Rates

## Slide 41: V6 - Relative Growth Rates

## Slide 42: V6 - Relative Growth Rates

## Slide 43: V6 - Relative Growth Rates

## Slide 44: IPv6 BGP Table Size predictions
Jan 2013 11,600 entries
2014 16,200 entries
2015 21,000 entries
2016 30,000 entries 25,000
2017 42,000 entries 29,000
2018 58,000 entries 34,000
2019 82,000 entries 38,000
2019 113,000 entries 43,000
Exponential Model
Linear Model

## Slide 45
Moore’s Law
BGP Table Size Predictions
IPv4 BGP Table size and Moore’s Law

## Slide 46: IPv6 Projections and Moore’s Law
Moore’s Law
BGP Table Size Predictions

## Slide 47: BGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing rapidly, is still relatively small in size in absolute terms
As long as we are prepared to live within the technical constraints of the current routing paradigm it will continue to be viable for some time yet

## Slide 48: BGP Updates
What about the level of updates in BGP?
Let’s look at the update load from a single eBGP feed in a DFZ context

## Slide 49: Announcements and Withdrawals

## Slide 50: Convergence Performance

## Slide 51: IPv4 Average AS Path Length
Data from Route Views

## Slide 52: Updates in IPv4 BGP
Nothing in these figures is cause for any great level of concern …
  The number of updates per instability event has been constant, due to the damping effect of the MRAI interval, and the relatively constant AS Path length over this interval
What about IPv6?

## Slide 53: V6 Announcements and Withdrawals

## Slide 54: V6 Convergence Performance

## Slide 55: V6 Average AS Path Length
Data from Route Views

## Slide 56: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention
But whether this is a problem or not depends on the way in which routers handle the routing table.
So lets take a quick look at routers…

## Slide 57: Inside a router
Backplane
Line Interface Card
Switch Fabric Card
Management Card
Thanks to Greg Hankins

## Slide 58: Inside a line card
CPU
PHY
Network
Packet Manager
DRAM
TCAM
*DRAM
Media
Backplane
FIB Lookup Bank
Packet Buffer
Thanks to Greg Hankins

## Slide 59: Inside a line card
CPU
PHY
Network
Packet Manager
DRAM
TCAM
*DRAM
Media
Backplane
FIB Lookup Bank
Packet Buffer
Thanks to Greg Hankins

## Slide 60: FIB Lookup Memory
The interface card’s network processor passes the packet’s destination address to the FIB module.
The FIB module returns with an outbound interface index

## Slide 61: FIB Lookup
This can be achieved by:
  Loading the entire routing table into a Ternary Content Addressable Memory bank (TCAM)
or
  Using an ASIC implementation of a TRIE representation of the routing table with DRAM memory to hold the routing table
Either way, this needs fast memory

## Slide 62: TCAM Memory
Address
Outbound Interface identifier
192.0.2.1
I/F 3/1
192.0.0.0/16 11000000 00000000 xxxxxxxx xxxxxxxx 3/0
192.0.2.0/24 11000000 00000000 00000010 xxxxxxxx 3/1
11000000 00000000 00000010 00000001
Longest Match
The entire FIB is loaded into TCAM. Every destination address is passed through the TCAM, and within one TCAM cycle the TCAM returns the interface index of the longest match. Each TCAM bank needs to be large enough to hold the entire FIB. TTCAM cycle time needs to be fast enough to support the max packet rate of the line card.
TCAM width depends on the chip set in use. One popular TCAM config is 72 bits wide. IPv4 addresses consume a single 72 bit slot, IPv6 consumes two 72 bit slots. If instead you use TCAM with a slot width of 32 bits then IPv6 entries consume 4 times the equivalent slot count of IPv4 entries.

## Slide 63: TRIE Lookup
Address
Outbound Interface identifier
192.0.2.1
I/F 3/1
11000000 00000000 00000010 00000001
1/0
1/0
1/0
1/0
1/0
x/0000
?
?
?
?
?
…
?
The entire FIB is converted into a serial decision tree. The size of decision tree depends on the distribution of prefix values in the FIB. The performance of the TRIE depends on the algorithm used in the ASIC and the number of serial decisions used to reach a decision
ASIC
DRAM

## Slide 64: Memory Tradeoffs
TCAM
Lower
Higher
Higher
Higher
Larger
80Mbit
ASIC +
RLDRAM 3
Higher
Lower
Lower
Lower
Smaller
1Gbit
Thanks to Greg Hankins
Access Speed
$ per bit
Power
Density
Physical Size
Capacity

## Slide 65: Memory Tradeoffs
TCAMs are higher cost, but operate with a fixed search latency and a fixed add/delete time. TCAMs scale linearly with the size of the FIB
ASICs implement a TRIE in memory. The cost is lower, but the search and add/delete times are variable. The performance of the lookup depends on the chosen algorithm. The memory efficiency of the TRIE depends on the prefix distribution and the particular algorithm used to manage the data structure

## Slide 66: Size
What memory size do we need for 10 years of FIB growth from today?
TCAM
V4: 2M entries (1Gt)
plus
V6: 1M entries (2Gt)
2014
2019
2024
512K
25K
125K
1M
768K
512K
V6 FIB
V4 FIB
Trie
V4: 100Mbit memory (500Mt)
plus
V6: 200Mbit memory (1Gt)
“The Impact of Address Allocation and Routing on the Structure and
Implementation of Routing Tables”, Narayn, Govindan & Varghese, SIGCOMM ‘03

## Slide 67: Scaling the FIB
BGP table growth is slow enough that we can continue to use simple FIB lookup in linecards without straining the state of the art in memory capacity
However, if it all turns horrible, there are alternatives to using a complete FIB in memory, which are at the moment variously robust and variously viable:
  FIB compression
  MPLS
  Locator/ID Separation (LISP)
  OpenFlow/Software Defined Networking (SDN)

## Slide 68: But it’s not just size
It’s speed as well.
10Mb Ethernet had a 64 byte min packet size, plus preamble plus inter-packet spacing
=14,880 pps
=1 packet every 67usec
We’ve increased speed of circuits, but left the Ethernet framing and packet size limits largely unaltered. What does this imply for router memory?

## Slide 69: Wireline Speed – Ethernet
1980
1990
2000
2010
2020
1Tb
10Mb
100Mb
1Gb
10Gb
100Gb
10Mb 1982/15Kpps
100Mb 1995 / 150Kpps
1Gb 1999 / 1.5Mpps
10Gb 2002 / 15Mpps
40Gb/100Gb 2010 / 150Mpps
400Gb/1Tb 2017?
1.5Gpps

## Slide 70: Clock Speed – Processors
1980
1990
2000
2010
2020
100Ghz
1Mhz
10Mhz
100Mhz
1GHz
10GHz
8080 2Mhz 1981
Dec Alpha 100Mz 1992
AMD 1GHz 2000
P4 3Ghz 2002
zEC12 5.5Ghz 2012

## Slide 71: Clock Speed – Processors

## Slide 72: CPU vs Memory Speed

## Slide 73: Speed, Speed, Speed
What memory speeds are necessary to sustain a maximal packet rate?
100GE 150Mpps 6.7ns per packet
400Ge 600Mpps 1.6ns per packet
1Te 1.5Gpps 0.67ns per packet
0ns
10ns
20ns
30ns
40ns
50ns
100Ge
400Ge
1Te

## Slide 74: Speed, Speed, Speed
What memory speeds do we have today?
0ns
10ns
20ns
30ns
40ns
50ns
Commodity DRAM
DDR3DRAM= 9ns -15ns
RLDRAM = 1.9ns - 12ns
Thanks to Greg Hankins
100Ge = 6.7ns
400Ge =1.67ns
1Te = 0.67ns

## Slide 75: Scaling Speed
Scaling size is not a dramatic problem today
Scaling speed is going to be tougher over time
Moore’s Law talks about the number of gates per circuit, but not circuit clocking speeds
Speed and capacity could be the major design challenge for network equipment in the coming years
If we can’t route the max packet rate for a terrabit wire then:
If we want to exploit parallelism as an alternative to wireline speed for terrabit networks, then is the use of best path routing protocols, coupled with destination-based hop-based forwarding going to scale?
Or are we going to need to look at path-pinned routing architectures to provide stable flow-level parallelism within the network to limit aggregate flow volumes?
Or should we reduce the max packet rate by moving away from a 64byte min packet size?
http://www.startupinnovation.org/research/moores-law/

## Slide 76
Thank You
Questions?