## Slide 1: Addressing and Routing in 2014
Geoff Huston
APNIC

## Slide 2: The Addressing View

## Slide 3: Addressing V4 Exhaustion
We have been predicting that the exhaustion of the free pool of IPv4 addresses would eventually happen for the past 25 years
And, we’ve now hit bottom!
  APNIC, RIPE NCC and LACNIC are now empty of general use IPv4 addresses
  We now have just ARIN and AFRINIC to go – ARIN is expected to run out in the coming weeks

## Slide 4: Allocations in the Last Years of IPv4
Chart: Year
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
APNIC | 53.6 | 51.4 | 69.6 | 87.8 | 86.9 | 120.2 | 105.2 | 1 | 1.3 | 3.7
RIPE NCC | 61.2 | 55 | 60.7 | 44 | 43.4 | 56 | 43.1 | 40 | 2 | 2.5
ARIN | 47.2 | 46.5 | 53 | 57.1 | 41.1 | 45.2 | 23.5 | 45 | 26.5 | 26
LACNIC | 10.4 | 10.7 | 14.2 | 12 | 10.5 | 13 | 24.4 | 21 | 28.5 | 19.1
AFRINIC | 0.9 | 2.6 | 5.5 | 1.6 | 5.9 | 8.5 | 9.2 | 7.9 | 6.8 | 12.5

## Slide 5: Allocations in the Last Years of IPv4
Chart: Year
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
APNIC | 53.6 | 51.4 | 69.6 | 87.8 | 86.9 | 120.2 | 105.2 | 1 | 1.3 | 3.7
RIPE NCC | 61.2 | 55 | 60.7 | 44 | 43.4 | 56 | 43.1 | 40 | 2 | 2.5
ARIN | 47.2 | 46.5 | 53 | 57.1 | 41.1 | 45.2 | 23.5 | 45 | 26.5 | 26
LACNIC | 10.4 | 10.7 | 14.2 | 12 | 10.5 | 13 | 24.4 | 21 | 28.5 | 19.1
AFRINIC | 0.9 | 2.6 | 5.5 | 1.6 | 5.9 | 8.5 | 9.2 | 7.9 | 6.8 | 12.5
Pre Exhaustion
Global Financial
Crisis
Exhaustion
Profile

## Slide 6: Where did the Addresses Go?
APNIC runs out
RIPE NCC runs out
LACNIC runs out
Volume of Allocated IPv4 Addresses (using units of millions of /32s) per year

## Slide 7: The IPv4 After-Market: Address Transfers
There is a considerable residual demand for IPv4 addresses following exhaustion
  IPv6 is not a direct substitute for the lack of IPv4
Some of this demand is pushed into using middleware that imposes address sharing (Carrier Grade NATS, Virtual Hosting, etc)
Where there is no substitute then we turn to the aftermarket
Some address transfers are “sale” transactions, and they are entered into the address registries
Some transfers take the form of “leases” where the lease holder’s details are not necessarily entered into the address registry

## Slide 8: Address Transfers
Number of registered
Address transfers per year
Volume of addresses transferred
per year (millions of /32s p.a.)

## Slide 9: How old are transferred addresses?
2014 transferred addresses are predominately between 2 and 9 years old
10% of addresses are >15 years old
6% of addresses are >20 years old

## Slide 10: IPv6 Allocations
Chart: 
| 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0
RIPE NCC | 89 | 158 | 427 | 622 | 1042 | 1647 | 1756 | 2149 | 2218
ARIN | 69 | 210 | 227 | 378 | 623 | 1038 | 611 | 560 | 512
APNIC | 43 | 63 | 161 | 190 | 666 | 641 | 599 | 540 | 528
LACNIC | 12 | 42 | 48 | 96 | 220 | 463 | 573 | 698 | 1208
AFRINIC | 17 | 19 | 16 | 13 | 55 | 129 | 83 | 73 | 62
Number of individual IPv6
address allocations per year

## Slide 11: IPv6 Allocated Addresses
Chart: 
| 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0
RIPE NCC | 6515 | 1440 | 856 | 883 | 2236 | 2293 | 3857 | 6301 | 8565
ARIN | 53 | 48 | 14489 | 237 | 547 | 6336 | 1663 | 12569 | 5232
APNIC | 3225 | 5236 | 139 | 171 | 1341 | 9493 | 3788 | 4449 | 2663
LACNIC | 12 | 55 | 40 | 89 | 205 | 970 | 4633 | 609 | 1363
AFRINIC | 15 | 13 | 10 | 9 | 101 | 149 | 4196 | 67 | 51
Volume of Allocated IPv6 Addresses (using units of /32s) per year

## Slide 12: Where did the IPv6 addresses go?
Volume of Allocated IPv6 Addresses (using units of /32s) per country, per year

## Slide 13: The Routing View

## Slide 14: Routing Indicators for IPv4
Routing prefixes – growing by some 45,000 prefixes per year
AS Numbers– growing by some 3,000 ASNs per year

## Slide 15: Routing Indicators for IPv4
The average size of a routing advertisement is getting smaller
Address Exhaustion is now visible in the extent of advertised address space

## Slide 16: Routing Indicators for IPv4
More Specifics are still taking up one half of the routing table
The “shape” of inter-AS interconnection appears to be steady, as the Average AS Path length has been held steady through the year

## Slide 17: How can the IPv4 network continue to grow when we are running out of IPv4 addresses?
We are now recycling old addresses back into the routing system

## Slide 18: IPv4 Address Reuse
50% of new addresses in 2014 were more than 1 year old
20% of new addresses in 2010 were more than 1 year old
18% of new addresses in 2014 were more than 20 years old
The age distribution of new addresses announced into the
‘routing system each year
It appears that this collection of “old” addresses includes space that has been leased rather than transferred
i.e. the current address user is not listed in the address registry

## Slide 19: IPv4 in 2014 – Growth is Slowing
Overall IPv4 Internet growth in terms of BGP is at a rate of some ~9%-10% p.a.
Address span growing far more slowly than the table size
The rate of growth of the IPv4 Internet is slowing down
  Address shortages
  Masking by NAT deployments and transfers
  Saturation of critical market sectors
  Transition uncertainty

## Slide 20: The Route Views view of IPv6
World IPv6 Day
IANA IPv4 Exhaustion

## Slide 21: Routing Indicators for IPv6
Routing prefixes – growing by some 6,000 prefixes per year
AS Numbers– growing by some 1,600 prefixes per year (which is half the V4 growth)

## Slide 22: Routing Indicators for IPv6
The average size of a routing advertisement is getting smaller
Address consumption is happening at a constant rate, and not growing year by year

## Slide 23: Routing Indicators for IPv6
More Specifics now take up one third of the routing table
The “shape” of inter-AS interconnection appears to be steady, as the Average AS Path length has been held steady through the year

## Slide 24: IPv6 in 2013
Overall IPv6 Internet growth in terms of BGP is 20% - 40 % p.a.
  2012 growth rate was ~ 90%.
If these relative growth rates persist then the IPv6 network would span the same network domain as IPv4 in ~16 years time

## Slide 25: Are we all now using V6?

## Slide 26: IPv6: How Many Can?

## Slide 27: IPv6: How Many Can?
Weekend numbers are 0.4% higher then weekday numbers
0.2% of users prefer to use V4 in dual stack scenarios
IPv6 use has doubled across 2014

## Slide 28: Forward Guesstimates
Best Case: IPv6 uptake doubles every year:
2019
Worst Case: IPv6 update constant 2% every year:
2067

## Slide 29: IPv6: Who Can?
IPv6 use by Country – February 2015

## Slide 30: IPv6: Who Can?
IPv6 use by Country – February 2015
World Average

## Slide 31: The Local View: Japan

## Slide 32: The Local View: Japan

## Slide 33: The Internet’s IPv6 Top 30
Est. V6 Users
V6 Takeup

## Slide 34: The Internet’s IPv6 Top 30
Est. V6 Users
V6 Takeup
Cumulative Sum

## Slide 35: The Internet’s IPv6 Top 30
Est. V6 Users
V6 Takeup
Cumulative Sum
It’s a very uneven takeup of IPv6 – 86% of the world’s IPv6 users sit behind just 30 ISPs

## Slide 36: Some Observations
If you allow the customer to own and maintain their own CPE then the CPE upgrade path is a critical issue – old CPE drags the IPv6 numbers down
Mobile providers should see higher penetration numbers … but legacy handsets seem to pull the numbers down
There are some high penetration numbers on “greenfield” deployments, but its rare to see:
49,AS16591,"GOOGLE-FIBER - Google Fiber Inc.",US,155096,87.3%

## Slide 37: The Internet’s 30 Largest ISPs

## Slide 38: Some Further Observations
IPv6 support is still very patchy:
  While most of the V6 activity in terms of user counts is confined to 30 ISPs, just 6 of the top 30 largest ISPs have any significant IPv6 deployments
The Internet is heavily skewed
  The 30 largest ISPs service 40% of the entire Internet user population
  If these 30 providers were to achieve an average 50% IPv6 uptake in their customer base, then the total IPv6 capability level would be 20% rather than 3.6%

## Slide 39
Thank You