## Slide 1: BGP in 2021
Geoff Huston
APNIC Labs

## Slide 2: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 3
1994: Introduction of CIDR
2001: The Great Internet
Boom and Bust
2005: Consumer Market
2011: Address Exhaustion
28 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route-Views

## Slide 4: 2021 in detail

## Slide 5: 2021 in detail
Slight downtick?
Slight uptick?

## Slide 6: 2021: Assigned vs Recovered
Change in UnAdvertised Addresses
Change in the Advertised Address Pool
RIR Allocations
218M advertised
24M allocated
186M recovered

## Slide 7: What happened in 2021 in V4?
  From the look of the routing growth plots, the growth of the size of the IPv4 network is slowing down
  The number of entries in the IPv4 default-free zone reached 906,000 by the end of 2021
  The pace of growth of the routing table was slightly lower than the rolling 5-year average, with 40,000 new entries in 2021 (was 52,000 in 2020)
  The AS position was slightly lower with 2,400 new AS’s advertised in 2021 (was 3,400 in 2020)
  Transit relationships have not changed materially over 2021 for most networks
  The overall growth trends are slowing down in 2021

## Slide 8: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 9: The Route-Views View of IPv6
IANA IPv4 Exhaustion

## Slide 10: 2021 in Detail

## Slide 11: 2021 in Detail
Route deaggregation events
CERN Future Net Research Platform

## Slide 12: V6 in 2021
Overall IPv6 Internet growth in terms of BGP is still increasing, and is currently at some 41,000 route entries p.a.
  With a couple of deaggregation leaks along the way!
It’s a case of increasing growth, not just constant growth
  More use of /48 more specifics
  More networks advertising IPv6 prefixes

## Slide 13: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 14: V4 BGP Table Size Predictions
Date RIB Size Prediction
Jan 2018 699,000
2019 760,000
2020 814,000
2021 866,000
2022 906,000 908,000
2023 956,000
2024 1,004,000
2025 1,052,000
2026 1,100,000
2027 1,148,000

## Slide 15: V6 BGP Table Size Predictions
Jan 2018 45,000
2019 62,000
2020 79,000
2021 104,000
2022 147,000 152,000
2023 185,000 214,000
2024 233,000 302,000
2025 261,000 426,000
2026 299,000 601,000
2027 366,000 847,000
Linear Exponential
Note that the IPv6 tables are 128bits wide – i.e. 4x the size of the IPv4 tables!

## Slide 16: BGP Table Growth
The absolute size of the IPv6 routing table is growing much faster than the IPv4 table
  These two tables will require the same storage/lookup size in around 2 years time, given that each IPv6 entry is 4 times the bit size of an IPv4 entry
The good news …
  As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet

## Slide 17: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 18: IPv4 BGP Updates

## Slide 19: IPv4 BGP Convergence Performance

## Slide 20: Updates in IPv4 BGP
The IPv4 inter-domain routing system is still highly stable …
The number of updates per instability event and the time to converge to a stable forwarding state has been relatively constant for many years - it rose in 2019 - 2020 and has declined again in 2021
20% of prefixes generate 80% of all updates. Less than 5% of all origin networks are linked to 80% of all updates. Instability is concentrated in a small number of highly unstable cases.

## Slide 21: V6 BGP Updates

## Slide 22: V6 Unstable Prefixes

## Slide 23: V6 Convergence Performance

## Slide 24: Updates in IPv6 BGP
It’s improving …
Compared to IPv4, the IPv6 network has exhibited a high level of routing instability, which is unexpected as the old overlay approaches are disappearing and the topology of IPv6 is now converging to the same topology as IPv4. The V6 network was more stable than ever in the last half of 2021
Just 2 AS’s generated 70% of the BGP update load in the last 2 weeks of 2021. Instability is still concentrated in a small number of pathological cases.

## Slide 25: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 26: Routing Futures
There is still little in the way of scaling pressure from BGP as a routing protocol – the relatively compressed inter-AS topology and stability of the infrastructure links tend to ensure that BGP remains effective in routing the internet. Instability levels are rising, generally driven by a small set of highly unstable “super generators”
The issues of FIB size, line speeds and equipment cost of line cards represent a more significant issue for hardware suppliers – we can expect cheaper line cards to to use far smaller LRU cache local FIBs in the high-speed switches and push lesser-used routes to a slower / cheaper lookup path. This approach may also become common in very high-capacity line cards

## Slide 27: Some Practical Suggestions
Know your network’s limits
Understand your routing hardware’s line card FIB capacity in the default-free parts of your network

## Slide 28: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Review your IPv4 / IPv6 portioning in the FIB tables - a dual-stack eBGP router will need 1M 32-bit IPv4 slots and 233K 128-bit IPv6 slots for a full eBGP routing table in line cards in 2 years time if they are using a full eBGP FIB load (plus internal routes of course). That’s the same memory footprint for IPv4 and IPv6!

## Slide 29: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Judicious use of default routes in your internal network may allow you drop this requirement significantly

## Slide 30: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Time for hot caching in line card FIBs?
Using a hot cache for line card FIB cache would reduce the high-speed TCAM memory requirement significantly without visible performance cost

## Slide 31: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Time for hot caching in line card FIBs?

## Slide 32: That’s it!
Questions?

## Slide 33: The Complete Pack

## Slide 34
1994: Introduction of CIDR
2001: The Great Internet
Boom and Bust
2005: Consumer Market
2011: Address Exhaustion
27 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route-Views

## Slide 35: 2017-2022 in detail
average growth trend

## Slide 36: 2021 in detail

## Slide 37: Routing Indicators for IPv4
Routing prefixes – growing by some 40,000 prefixes per year
AS Numbers– growing by some 2,400 prefixes per year

## Slide 38: Routing Indicators for IPv4
More Specifics are still taking up slightly more than one half of the routing table
But the average size of an IPv4 routing advertisement continues to shrink

## Slide 39: Routing Indicators for IPv4
The US DoD advertised its collection of legacy /8 prefixes in 2021
The “shape” of inter-AS interconnection appears to be trending to a more compact topology

## Slide 40: AS Adjacencies (as seen by AS131072)
6,059 AS6939 HURRICANE - Hurricane Electric, Inc., US
4,977 AS3356 LEVEL3 - Level 3 Communications, Inc., US
3,743 AS174 COGENT-174 - Cogent Communications, US
2,015 AS6461 ZAYO Bandwidth, US
1,776 AS3257 GTT-Backbone, DE
1,742 AS7018 ATT-INTERNET4 - AT&T Services, Inc., US
1,372 AS1299 TWELVE99 Arelion (fka Telia Carrier), SE
1,243 AS2914 NTT America, US
1,023 AS12389 ROSTELECOM, RU
59,044 out of 72,930 ASNs have 1 or 2 AS Adjacencies (82%)
2,425 ASNs have 10 or more adjacencies
9 ASNs have >1,000 adjacencies
Most networks are stub AS’s
A small number of major connectors

## Slide 41: What happened in 2021 in V4?
  From the look of the routing growth plots, the growth of the size of the IPv4 network is slowing down
  The number of entries in the IPv4 default-free zone reached 906,000 by the end of 2021
  The pace of growth of the routing table was slightly lower than the rolling 5-year average, with 40,000 new entries in 2021 (was 52,000 in 2020)
  The AS position was slightly lower with 2,400 new AS’s advertised in 2021 (was 3,400 in 2020)
  Transit relationships have not changed materially over 2021 for most networks
  The overall growth trends are slowing down in 2021

## Slide 42: Post-Exhaustion Routing Growth
What’s driving this post-exhaustion growth?
  Transfers?
  Last /8 policies in RIPE and APNIC?
  Leasing and address recovery?

## Slide 43: Advertised Address “Age”
80% of all new addresses announced in 2010 were allocated or assigned within the past 12 months
2% of all new addresses announced in 2010 were >= 20 years ‘old’ (legacy)
2010

## Slide 44: Advertised Address “Age”
Advertisment of legacy addresses

## Slide 45: IPv4 Advertised vs Unadvertised

## Slide 46: 2010 – 2021: Unadvertised Addresses

## Slide 47: 2021: Assigned vs Recovered
Change in Advertised Addresses
Change in the Unadvertised Address Pool
RIR Allocations

## Slide 48: V4 in 2021
199.6M addresses were added to the routing table across 2020
1.1M addresses were assigned by RIRs in 2019
And a net of 198.5M addresses were drawn from the pool of unadvertised addresses
The major shift in 2021 was the advertisement of the previously dormant legacy /8s that were assigned to the US DoD in the early days of the ARPANET/Internet

## Slide 49: The Route-Views View of IPv6
IANA IPv4 Exhaustion

## Slide 50: 2020-2022 in Detail

## Slide 51: Routing Indicators for IPv6
Routing prefixes – growing by some 46,000 prefixes per year
AS Numbers– growing by some 2,400 ASNs per year – with 6,740 added in 2021

## Slide 52: Routing Indicators for IPv6
More Specifics now take up 60% of the routing table
The average size of a routing advertisement is getting smaller

## Slide 53: Routing Indicators for IPv6
Advertised Address span is growing at an exponential rate
The “shape” of inter-AS interconnection in IPv6 is rising slightly. Local connections appear to be replacing overlay trunk transits

## Slide 54: AS Adjacencies (vantage point: AS131072)
23,243 out of 28,328 ASNs have 1 or 2 AS Adjacencies (82%)
914 ASNs have 10 or more adjacencies
5 ASNs have >1,000 adjacencies
5,734 AS6939 HURRICANE - Hurricane Electric, Inc., US
3,970 AS38255 FITI, China Education and Research Network CN
1,472 AS3356 LEVEL3 - Level 3 Communications, Inc., US
1,325 AS1299 TWELVE99 Arelion, (fka Telia Carrier), SE
1,232 AS174 COGENT-174 - Cogent Communications, US

## Slide 55: V6 in 2021
Overall IPv6 Internet growth in terms of BGP is still increasing, and is currently growing at some 41,000 route entries p.a.
It’s a case of increasing growth, not just constant growth
  More use of /48 more specifics
  More networks advertising IPv6 prefixes

## Slide 56: What to expect

## Slide 57: BGP Size Projections
How quickly is the routing space growing?
What are the projections of future BGP FIB size?

## Slide 58: V4 - Daily Growth Rates
Growth in the V4 network appears to be constant at a long-term average of 150 additional routes per day, or some 54,000 additional routes per year. Recent growth rates are lower

## Slide 59: V4 BGP Table Size Predictions
Date RIB Size Prediction
Jan 2018 699,000
2019 760,000
2020 814,000
2021 866,000
2022 906,000 908,000
2023 956,000
2024 1,004,000
2025 1,052,000
2026 1,100,000
2027 1,148,000

## Slide 60: V6 - Daily Growth Rates

## Slide 61: V6 BGP Table Size Predictions
Jan 2018 45,000
2019 62,000
2020 79,000
2021 104,000
2022 147,000 152,000
2023 185,000 214,000
2024 233,000 302,000
2025 261,000 426,000
2026 299,000 601,000
2027 366,000 847,000
Linear Exponential
Note that the IPv6 tables are 128bits wide – i.e. 4x the size of the IPv4 tables!

## Slide 62: BGP Table Growth
The absolute size of the IPv6 routing table is growing much faster than the IPv4 table
  These two tables will require the same storage/lookup size in around 2 years time, given that each IPv6 entry is 4 times the bit size of an IPv4 entry
The good news …
  As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet

## Slide 63: BGP Updates
What about the rate of updates in BGP?

## Slide 64: IPv4 BGP Updates

## Slide 65: IPv4 BGP Convergence Performance

## Slide 66: Updates in IPv4 BGP
The IPv4 inter-domain routing system is still highly stable …
The number of updates per instability event and the time to converge to a stable forwarding state has been relatively constant for many years - it rose in 2019 - 2020 and has declined again in 2021
20% of prefixes generate 80% of all updates. Less than 5% of all origin networks are linked to 80% of all updates. Instability is concentrated in a small number of highly unstable cases.

## Slide 67: V6 BGP Updates

## Slide 68: V6 Unstable Prefixes

## Slide 69: V6 Convergence Performance

## Slide 70: Updates in IPv6 BGP
It’s improving …
Compared to IPv4, the IPv6 network has exhibited a high level of routing instability, which is unexpected as the old overlay approaches are disappearing and the topology of IPv6 is now converging to the same topology as IPv4. The V6 network was more stable than ever in the last half of 2021
Just 2 AS’s generated 70% of the BGP update load in the last 2 weeks of 2021. Instability is still concentrated in a small number of pathological cases.

## Slide 71: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 72: Routing Futures
There is still little in the way of scaling pressure from BGP as a routing protocol – the relatively compressed inter-AS topology and stability of the infrastructure links tend to ensure that BGP remains effective in routing the internet. Instability levels are rising, generally driven by a small set of highly unstable “super generators”
The issues of FIB size, line speeds and equipment cost of line cards represent a more significant issue for hardware suppliers – we can expect cheaper line cards to to use far smaller LRU cache local FIBs in the high-speed switches and push lesser-used routes to a slower / cheaper lookup path. This approach may also become common in very high-capacity line cards

## Slide 73: Some Practical Suggestions
Know your network’s limits
Understand your routing hardware’s line card FIB capacity in the default-free parts of your network

## Slide 74: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Review your IPv4 / IPv6 portioning in the FIB tables - a dual-stack eBGP router will need 1M 32-bit IPv4 slots and 233K 128-bit IPv6 slots for a full eBGP routing table in line cards in 2 years time if they are using a full eBGP FIB load (plus internal routes of course). That’s the same memory footprint for IPv4 and IPv6!

## Slide 75: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Judicious use of default routes in your internal network may allow you drop this requirement significantly

## Slide 76: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Time for hot caching in line card FIBs?
Using a hot cache for line card FIB cache would reduce the high-speed TCAM memory requirement significantly without visible performance cost

## Slide 77: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Time for hot caching in line card FIBs?