## Slide 1: Dagstuhl Workshop Presentation: Learnings from Failure
Geoff Huston, APNIC

## Slide 2: The 40 year Scorecard for the Internet
Stacked Protocol Architecture
Stateless Packet Switching
ACK-paced Transport
End-to-End
Network Management
Names and Referential Frameworks
Security

## Slide 3: The 40 year Scorecard for the Internet
None of these areas are unqualified “successes” for the Internet Protocol:
  Layer violations proliferate
  MPLS is a widely used circuit-based overlay for many IP service platforms
  Ack-paced transport is slow and clumsy
  The proliferation of network middleware shows a moderated view of “pure” end-to-end
  The relationship between networks and hosts has never been made to work
    (The saga of failed QoS efforts, for example)
  UDP is a glaring vulnerability in the DOS world

## Slide 4: Learning from our Failures
IPv6
  What happened?
  Why didn’t the industry take a low risk path and avoid IPv4 address depletion completely by adopting IPv6 earlier?
  Is IPv6 too complex for a simple-minded industry?
    Fragmentation and Extension headers
    SLAAC / DHCP / etc
    Chaotic address plan
  Is the lack of backwards compatibility a fatal flaw in any transition?
  Do we understand the economics of transition in a heterogenous market-driven environment?

## Slide 5: Learning from our Failures
DNSSEC
  Why doesn’t anyone validate what they learn from the DNS?
  Why don’t zone admins DNSSEC-sign everything?
  The DNSSEC design parameters looked good:
    Backward compatible, incremental extension, no protocol change to the DNS
  But its just not happening
    Resistance to signing
    Resistance to validating at the edge
  Is this a case of technical failure or economic failure? (or both!)

## Slide 6: Learning from our Failures
Security and Robustness
  Obviously what we are doing is nowhere near enough - we are engaging in a spiral process of escalation of the sophistication of the attacks and a response of greater complexity
  Some commentary has suggested we would have been in a better place if we had ”integrated” security into the basic protocol design at the outset
  Other commentary suggests that we really never knew how to do that and a bolt-on approach allows for greater agility in our response
  Have we largely given up on network level security and just relying on applications to fend for themselves?
  Is this enough?

## Slide 7: A Case Study – Routing Security
The Internet took the novel approach of self-orchestration in building the routing system
Routing is a distributed algorithm operating across a collection of diverse mutually trusting entities
Routing is easily abused:
  Deliberately by manipulation of the routing exchange
  Deliberately by a rouge entity abusing the trust model
  Inadvertently through operational mishap
We assume(d) that if we addressed a packet to the “right” IP address, then we could trust any response we received as “authentic”
  Corrupting the routing system undermined this assumption

## Slide 8: Routing Security is a Hard Problem
The problem space includes:
The integrity of the routing information
The proper operation of the routing protocol to propagate this information
A definition of points of “absolute trust”
It’s taken more than 30 years and we’ve achieved little

## Slide 9: RPKI and BGPSEC Efforts
The RPKI is a poor fit to the routing application space
  Routing needs to bring “all” of the PKI to every relying party – this is a scaling flooding problem
  Routing is not transactional – the information in a routing update is trusted until it is withdrawn or updated
  Omissions (deliberate or otherwise) in routing propagation are unverifiable
  Routing security works best when everybody signs and everybody validates
BGPSEC is over-burdened
  AS path validation is implemented by signing chains which impose a high crypto burden on routers - BGP session resets become a problem
  Loading keys into routers and maintaining this framework is operationally brittle

## Slide 10: Does anyone care any more?
After 30 years with no workable secure routing framework applications have resigned themselves not to trust the underlying network
TLS is the general “solution” to this problem
  Irrespective of where the packet may have been delivered, if the remote end cannot demonstrate that it is a genuine instance of the named service then its an untrusted transaction
  This shifts authenticity function up from the IP address layer to the session/application layer
  This devalues the incremental benefit from a secure routing system, and reduces the motivation to deploy this technology

## Slide 11: Why deploy BGPSEC?
High cost, fragile framework
The consequences of operational lapses tend towards enforced disconnection – often a far more damaging outcome than the problem that these measures they they are attempting to detect
The network operators incur a high cost in deployment. Where is the incremental benefit? Who accrues value from this benefit?
Partial deployments are very challenging for AS Path protection, and validating origination without propagation protection does not mitigate the security risks of malfeasance
Is TLS doing an adequate job for the purposes we need to use it for?

## Slide 12: Learning from Successes
TCP
  Are we talking about TCP per se or about the use of a sliding window protocol to implement reliable packet flows in a datagram substrate?
  TCP’s model of ACK-based sender clocking with AIMD-based sender governance is not ideal in any individual scenario, but is adequately good in most scenarios we’ve come across
  TCP’s use of sender-based controls allows servers to innovate without forcing change on clients

## Slide 13: Learning from Successes
BGP - The Border Gateway Protocol
  This is a venerable protocol and continues to operate efficiently in spite of considerable scaling demands
  What can we learn from BGP:
    Don’t try to solve everything all at once – work with a limited set of objectives
    Avoid flag days and forced change - use negotiation to add capabilities

## Slide 14: Lessons for Protocol Utility
Design for the general case, not a specific scenario
But focus on a single function
Keep it simple
Every needless exposure of data can and will be used against the user!
Avoid inter-dependencies on third parties wherever possible
Backward compatibility and tolerance for piecemeal deployment are essential
Adopters need to be able to realise benefits of adoption from the outset – if benefits are realizable only when everyone deploys then adoption will stall

## Slide 15: Transitional Considerations
Backward Compatibility?
Piecemeal uncoordinated adoption?
Early adopter advantages?
Late adopter penalties?
Risk reduction?
Alignment of cost and benefit?
Reduce dependencies?

## Slide 16: Lessons?
IPv6, DNSSEC, BGPSEC are all technology adoption failures in economic terms
Economic considerations are ultimately more important than just “good” technology
In a deregulated space, technology adoption is a function of markets, not an outcome of regulatory fiat or imposed orchestration
Technology adoption is not based on relative merit – adoption is based on cost efficiencies, alignment of cost and benefit, and market dynamics
The larger the system the greater the resistance to change - incumbent technologies have a strong advantage
Displacement occurs only when the relative cost advantages are massive (10x, 100x, …)