## Slide 1: Quality of Service in the Internet Theory and Practice
Geoff Huston
Notes: 1

## Slide 2: Acknowledgment and thanks
2
to Fred Baker and Paul Ferguson, both of Cisco Systems,
for some of the material used in this slide set
Notes: 2

## Slide 3: Agenda
3
Definition of the Problem
Service Quality and the Application Environment
Approaches to Quality Management
Considerations
Mechanisms
Measuring QoS
Marketing QoS
Summary
Notes: 3

## Slide 4: Quality of Service Definition of the Problem
4
Notes: 4

## Slide 5: What is the problem?
5
Today’s Internet is plagued by sporadic poor performance.
  This is getting worse, not better!
Methods are needed to differentiate traffic and provide “services”
Notes: 5

## Slide 6: What is the problem?
6
“Poor Performance” of the Internet service environment
  more specifically:
    routing instability
    high packet loss in critical NAPs/Exchange Points
    server congestion
    high variation of transaction times
    poor protocol performance due to loss and round trip time variation
Notes: 6

## Slide 7: The QoS challenge
Internet network infrastructure is under stress due to:
  robust demand models
  engineering the network to use all available resources, on the edge of instability and capacity saturation

## Slide 8: What is the problem?
7
Applications are more demanding
  end systems are getting faster
  end systems use faster network connections
  emerging ubiquity of access breeds diversity of application requirements
  end systems applications wish to negotiate performance from the network
Notes: 7

## Slide 9: It would be good if…
8
When the user wished to access a priority service:
  the network could honor the request
The application could forecast its network load requirements so that:
  the network could commit to meet them
When there isn't sufficient bandwidth on one network path to meet the application’s requirements:
  The network could find another path
Notes: 8

## Slide 10: Quality of Service
9
Customers want access to an Internet service which can provide a range of consistent & predictable high quality service levels
  in addition to normal best effort service levels
Notes: 9

## Slide 11: Quality of Service
Network mechanisms intended to meet this demand for various levels of service are categorized within the broad domain of Quality of Service

## Slide 12: Rationale for providing QoS
10
The Internet is commercial & competitive.
    No major revelation here
Internet Service Providers are looking for ways to generate new sources of revenue.
    Again, nothing new
Creation of new services creates new sources of revenue.
Notes: 10

## Slide 13: Rationale for providing QoS
11
Preferential treatment is an attractive service which customers are indicating they desire to purchase.
Notes: 11

## Slide 14: Rationale for providing QoS
12
Service Providers would like offer differential services where:
  the customer is charged at a rate comparable to service level expectations
  where the marginal service revenue reflects the marginal network engineering and support costs for the service
Notes: 12

## Slide 15: Non-Rationale for QoS
13
QoS is not a tool to compensate for inadequacies elsewhere in the network.
It will not fix:
  Massive over-subscription
  Horrible congestion situations
  Sloppy network design
No magic here™
Notes: 13

## Slide 16: What is the expectation?
14
A requirement for a premium differentiated services within the network that will provide predictable and consistent service response for selected customers and traffic flows:
  provision of guarantees on bandwidth & delay
  provision of absolute service level agreements
  provision of average service level agreements
But can the Internet deliver?
Notes: 14

## Slide 17: QoS
15
QoS is the provision of control mechanisms within the network which are intended to manage congestion events.
Notes: 15

## Slide 18: Aside...
16
The Congestion Problem as we see it --
  Chaos theory:
    Congestion is non-linear behavior
    Think in terms of pipes and water
    Turbulence produces mixing and increases drag
  QoS is akin to solving non-linear fluid dynamics:
    Enforcing linearity, or
    Convincing big flows to behave nicely
Notes: 16

## Slide 19: Expectation setting
17
QoS is not magic
  QoS cannot offer cures for a poorly performing network
  QoS does not create nonexistent bandwidth.
    Elevating the amount of resources available to one class of traffic decreases the amount available for other traffic classes
    Total goodput will be reduced in a differentiated environment
  QoS will not alter the speed of light
    On an unloaded network, QoS mechanisms will not make the network any faster
      Indeed, it could make it slightly worse!
Notes: 17

## Slide 20: Expectation setting
18
QoS is unfair damage control
  QoS mechanisms attempt to preferentially allocate resources to predetermined classes of traffic, when the resource itself is under contention
  The preferential allocation can be wasteful, making the cumulative damage worse
  Resource management only comes into play when the resource is under contention by multiple customers or traffic flows
    Resource management is irrelevant when the resource is idle or not an object of contention
Notes: 18

## Slide 21: Expectation setting
19
QoS is relative, not absolute
  QoS actively discriminates between preferred and non-preferred classes of traffic at those times when the network is under load (congested)
  Qos is the relative difference in service quality between the two generic traffic classes
    If every client used QoS, then the net result is a zero sum gain
Notes: 19

## Slide 22: Expectation setting
20
QoS is intentionally elitist and unfair
  The QoS relative difference will be greatest when the preferred traffic class is a small volume compared to the non-preferred class
  QoS preferential services will probably be offered at a considerable price premium to ensure that quality differentiation is highly visible
Notes: 20

## Slide 23: Quality of Service
21
Definition of Quality
Notes: 21

## Slide 24: What is Quality?
22
Quality cannot be measured on an entire network
  Flow bandwidth is dependant on the chosen transit path
  Congestion conditions are a localized event
  Quality metrics degrade for those flows which transit the congested location
Quality can be only be measured on an end-to-end traffic flow, at a particular time
Notes: 22

## Slide 25: Quality metrics
23
The network quality metrics for a flow are:
  Delay - the elapsed time for a packet to transit the network
  Jitter - the variation in delay for each packet
  Bandwidth - the maximal data rate that is available for the flow
  Reliability - the rate of packet loss, corruption, and re-ordering within the flow
Notes: 23

## Slide 26: Quality metrics
24
Quality metrics are amplified by network load
  Delay increases due to increased queue holding times
  Jitter increases due to chaotic load patterns
  Bandwidth decreases due to increased competition for access
  Reliability decreases due to queue overflow, causing packet loss
Notes: 24

## Slide 27: QoS and the Internet
The Internet transmission model is a set of self-adjusting traffic flows that cooperate to efficiently load the network transmission circuits
  session performance is variable
  network efficiency is optimised

## Slide 28: QoS and the Internet
QoS is a requirement for the network to bias the flow self-adjustment to allow some flows to consume greater levels of the network resource
  this is not easy...

## Slide 29: Quality metrics
25
Quality differentiation is only highly visible under heavy network load
  differentiation is relative to normal best effort
  On unloaded networks queues are held short, reducing queue holding time, propagation delay is held constant and the network service quality is at peak attainable level
Notes: 25

## Slide 30: The Internet QoS Margin is small
Network Load
Quality traffic efficiency
Best Effort traffic efficiency
QoS differential
for a given load
1
You must be joking
Network Carriage Efficiency

## Slide 31: Service Quality
26
Not every network is designed with quality in mind…
Adherence to fundamental networking engineering principals.
Operate the network to deliver Consistency, Stability, Availability, and Predictability.
Cutting corners is not necessarily a good idea.
Notes: 26

## Slide 32: Service Quality
27
Without Service Quality, QoS is unachievable
Notes: 27

## Slide 33: Quality of Service Service Quality and the Application Environment Application Performance Issues
28
Notes: 28

## Slide 34: Today’s Internet Load
29
Two IP protocol families
  TCP
  UDP
Three common application elements
  WWW page fetches (TCP)
  bulk data transfer (TCP)
  audio & video transfer (UDP)
consume some 90% of today’s Internets
Notes: 29

## Slide 35: UDP-based applications
30
sender transmits according to external signal source timing, such as:
  audio encoder
  video encoder
one (unicast) or more (multicast) receivers
no retransmission in response to network loss
      need to maintain integrity of external clocking of signal
no rate modification due to network congestion effects
      no feedback path from network to encoder
Notes: 30

## Slide 36: UDP and Quality
31
QoS: reduce loss, delay and jitter
  RSVP approach
    ‘reserve’ resource allocation across intended network path
    guaranteed load for constant traffic rate encoder
    controlled load for burst rate managed encoder
  application-based approach
    introduce feedback path from receiver(s) to encoder to allow for some rate adjustment within the encoder
  diff-serv approach
    mark packets within a flow to trigger weighted preferential treatment
Notes: 31

## Slide 37: TCP behavior
32
Large volume TCP transfers
  allow the data rate to adjust to the network conditions
  establish point of network efficiency, then probe it
  variable rate continually adjusted to optimize network load at the point of maximal transfer without loss
  uses dynamic adjustment of sending window to vary the amount of data held ‘in flight’ within the network
Notes: 32

## Slide 38: TCP performance
33
use the Principle of Network Efficiency:
  only inject more data into a loaded network when you believe that the receiver has removed the same amount of data from the network
  TCP uses ACKs as the sender’s timer
ACK packets
Data packets
R
S
Notes: 33

## Slide 39: TCP rate control (1)
34
Slow Start
  inject one segment into the network, wait for ACK
  for each ACK received inject ACK’ed data quantity, plus an additional segment (exponential rate growth)
  continue until fast packet loss, then switch to Congestion Avoidance
Under slow start TCP window
growth is exponential
Notes: 34

## Slide 40: TCP rate control (2)
35
Congestion Avoidance
  halve current window size
  for each ACK received inject ACK’d data quantity plus message_segment / RTT additional data (linear rate growth of 1 segment per RTT)
  on fast loss, halve current window size
Under Congestion Avoidance
TCP window size is a linear
sawtooth
Notes: 35

## Slide 41: TCP session behaviour
36
Network congestion level
Slow Start Behaviour
Congestion Avoidance Behaviour
Notes: 36

## Slide 42: TCP and Quality
37
For long held sessions an optimal transfer rate is dependant on:
  avoiding sequenced packet drop, to allow TCP fast retransmit algorithm to trigger
      i.e., tail drop is a Bad Thing ™
  avoiding false network load signals, to allow slow start to reach peak point of path load (ATM folk please take careful note!)
      congestion avoidance has (slow) linear growth while slow start uses (faster) exponential growth
  avoiding resonating cyclical queue pressure
      packets tend to cluster at RTT epoch intervals, needing large queues to even out load at bottleneck spots
Notes: 37

## Slide 43: Short TCP sessions
38
average WWW session is 15 packets
15 packets are 4 RTTs under slow start
average current network load is 70% WWW traffic
performance management for short TCP sessions is important today
Notes: 38

## Slide 44: Short TCP and Quality
39
Increase initial slow start TCP window from 1 to 4 segments
    decrease transfer time by 1 RTT for 15 packet flows
avoid loss for small packet sequences
    retransmission has proportionately high impact on transfer time
use T/TCP to avoid 3-way handshake delay
    reduce transfer time from 6 RTT to 4 RTT
use HTTP/1.1 to avoid multiple short TCP sessions
Notes: 39

## Slide 45: TCP and QoS
40
TCP performance is based on round trip path
Partial QoS measures may not improve TCP performance
  QoS symmetry
  End-to-end QoS
Notes: 40

## Slide 46: QoS Symmetry
41
Forward (data) precedence without reverse (ACK) precedence may not be enough for TCP
    data transmission is based on integrity of reverse ACK timing
    unidirectional QoS setting is not necessarily enough for TCP
      ACKs should mirror the QoS of the data it acknowledges to ensure optimal performance differential
      will the network admit such ‘remote setting’ QoS?
        How?
      will the QoS tariff mechanism support remote triggered QoS?
        How?
Notes: 41

## Slide 47: End-to-End QoS
42
Precedence on only part of the end-to-end path may not be enough
    data loss and jitter introduced on non-QoS path component may dominate end-to-end protocol behavior
Notes: 42

## Slide 48: End-To-End QoS
43
Partial provider QoS is not good enough
  inter-provider QoS agreements an essential precondition for Internet-wide QoS
  inter-provider QoS agreements must cover uniform semantics of QoS indicators
  inter-provider agreements are not adequately robust today to encompass QoS
Notes: 43

## Slide 49: What is End-to-End?
44
Notes: 44

## Slide 50: QoS Discovery protocol
45
Will we require QoS discovery probes to ‘uncover’ QoS capability on a path to drive around the non-uniform deployment environment?
  similar to MTU discovery mechanism used to uncover end-to-end MTU
  use probe mechanism to uncover maximal attainable QoS setting on end-to-end path
    even if we need it, we haven’t got one of these tools yet!
Notes: 45

## Slide 51: End-To-End QoS
46
BUT --
  link-based QoS on critical bottleneck paths may produce useful QoS outcomes without complete end-to-end QoS structures
  Potential hop-based QoS deployment scenarios:
    queuing precedence on heavily congested high delay link
      place mechanism on critical common bottleneck point
    satellite vs cable QoS path selection
      use policy-based forwarding for path selection
Notes: 46

## Slide 52: Quality of Service Service Quality and the Application Environment Delay Management
47
Notes: 47

## Slide 53: Operational definition
48
Application perspective:
  A link or network over which an application is less useful due to the effects of delay
User Perspective:
  the World Wide Wait
Notes: 48

## Slide 54: TCP measures delay
49
Mean Round Trip Time (RTT)
  elapsed time for a data packet to be sent and a corresponding ACK packet to be received
One window of data per RTT
Mean variance in RTT
Retransmit after
  Mean RTT + (constant x Mean Variance)
Delay affects performance
Notes: 49

## Slide 55: What is delay?
50
Packet propagation times
  LAN - less than 1 millisecond
  campus - 1 millisecond
  trans-US - 12 milliseconds
  trans-Pacific cable - 60 milliseconds
  AU to US - 120 milliseconds
  AU to FI - 220 milliseconds
  LEO - variable - 100 - 200 milliseconds
  GEO - 280 milliseconds
Notes: 50

## Slide 56: Delay and applications
51
One window transaction per RTT
Small transmission windows
  TCP Slow Start gets slower!
Limited Throughput
  32K per RTT protocol limitation
Slow reaction to congestion levels
Notes: 51

## Slide 57: Delay mitigation strategies
52
Avoid it in the first place
Mitigate the delay source
Notes: 52

## Slide 58: Avoid delay in the first place
53
Bring the data source closer to the consumer
Local caches
  FTP “mirror sites”
  Web caches
Local services
  Local computation
Notes: 53

## Slide 59: Obvious sources of delay
54
Router Queuing delay
Transmission Propagation delay
“Window depleted” period
  where sender is blocked by receiver
Notes: 54

## Slide 60: Mitigate queuing delays
55
Queuing algorithms
  FIFO Queuing
  Class-based Queuing
  Weighted Fair Queuing
Line disciplines
  PPP fragmentation
  Multiplexed ATM VCs
Notes: 55

## Slide 61: Mitigate propagation delays
56
These result from physics
  Which mere mortals can't readily change
Can we parallelize the system?
  Long windows + Selective Acknowledge
  Parallel file transfers
Can we make good use of recent history?
  HTTP 1.1 persistent TCP connections
Notes: 56

## Slide 62: Mitigate “window depleted” intervals
57
TCP behavior
Traffic rate controls
Overlapping windows with rate-based controls
Notes: 57

## Slide 63: TCP behavior
58
Slow start
Fast retransmission
Traffic drops seen as indications of congestion
Notes: 58

## Slide 64: Traffic rate controls
59
Sliding window controls
  Constant data outstanding
Rate based controls
  Constant transmission rate
Notes: 59

## Slide 65: Subdivide the TCP connection
60
TCP at each end
Reliable link between points
  Could be TCP, not required
  Limit each connection to rate supported by next connection
  Large effective window
Notes: 60

## Slide 66: Net effect:
61
Throughput governed by slowest connection
  High delay connection has pseudo-rate based control governed by slow start at endpoints
Duration of data transfer:
  Duration of transfer disregarding propagation delay
  Plus 1-2 round trip delays
Notes: 61

## Slide 67: Quality of Service Approaches to Quality Management
62
Notes: 62

## Slide 68: What are the Q variables?
63
A network is composed of a set of
  routers
  switches
  other network attached devices
Connected by
  transmission links
Notes: 63

## Slide 69: Router Service Components
64
INPUT BUFFER
IP SWITCH
OUTPUT QUEUE STRUCTURE
IP SWITCH
OUTPUT DRIVER
Notes: 64

## Slide 70: Router Q variables?
65
Routers can:
  fragment
  delay
  discard
  forward
packets through manipulation of ingress & queue management and forwarding mechanisms
Notes: 65

## Slide 71: Router Q variables
66
INPUT BUFFER
IP SWITCH
OUTPUT QUEUE STRUCTURE
IP SWITCH
OUTPUT DRIVER
DELAY / DROP / FORWARD
DROP
DELAY / JITTER / DROP
DELAY
Notes: 66

## Slide 72: Transmission Q variables
67
Constant flow point-to-point bit pipes
  constant delay
  packet loss probability related to transmission error rate and link MTU
No intrinsic differentiation on loss and delay is possible
Notes: 67

## Slide 73: Transmission Q variables
68
Switched L2 services:
  ATM, Frame Relay, SMDS
  create virtual end to end circuits with specific carriage characteristics
Variable delay and loss probability is possible
Notes: 68

## Slide 74: Transmission Q variables
69
Multiple access LANs
  variable delay and loss probability based on access algorithm, which is effected by imposed load
No predetermined differentiation on loss and delay is possible
  although some efforts are underway to change this for LAN technologies
Notes: 69

## Slide 75: How to differentiate flows
70
Use state-based mechanisms to identify flows of traffic which require per-flow differentiation
Use stateless mechanisms that react to marked packets with differentiated servicing
Notes: 70

## Slide 76: Integrated Services
1
Per flow traffic management to undertake one of more of the following service commitments:
  Place a preset bound on jitter.
  Limits delay to a maximal queuing threshold.
  Limit packet loss to a preset threshold.
  Delivers a service guarantee to a preset bandwidth rate.
  Deliver a service commitment to a controlled load profile.
Challenging to implement in a large network.
Relatively easy to measure success in meeting the objective.
Notes: 1

## Slide 77: IntServ and the Internet
2
RSVP approach
Integrated Services requires the imposition of flow-based dynamic state onto network routers in order to meet the stringent requirements of a service guarantee for a flow.
Such mechanisms do not readily scale to the size of the Internet.
Notes: 2

## Slide 78: Differentiated Services
3
Active differentiation of packet-based network traffic to provide a better than best effort performance for a defined traffic flow, as measured by one of more of:
  Packet jitter
  Packet loss
  Packet delay
  Available peak flow rate
Implementable within a large network.
Relatively difficult to measure success is providing service differentiation.
Notes: 3

## Slide 79: DiffServ and the Internet
4
Approach being considered within IETF
Differentiated Services can be implemented through the deployment of differentiation router mechanisms triggered by per-packet flags, preserving a stateless network architecture within the network core.
Such mechanisms offer some confidence to scale to hundreds of millions of flows per second within the core of a large Internet
Notes: 4

## Slide 80: Stateless QoS
Per Hop Behaviour
determined by packet
header attribute values

## Slide 81: Diffserv currently discussing use of TOS byte
5
Notes: 5

## Slide 82: Quality of Service Considerations
6
Notes: 6

## Slide 83: “Managed Expectations Internet”
7
Solve congestion problems with
  TCP implementation improvements
  Weighted Random Early Detection
Manage users to a contracted rate
Permit use of excess when available
Notes: 7

## Slide 84: Service contracts in the “new” Internet ?
8
Tiered cost structure
    Low cost for contracted service
    Additional cost for excess service
    Additional cost for specialized calls
QoS Routing could support “specialized calls”
Notes: 8

## Slide 85: End-to-End QoS
9
Reliance on a particular link-layer technology to deliver QoS is fundamentally flawed.
TCP/IP is the “common bearer service,” the most common denominator in today’s Internet.
Partial-path QoS mechanisms introduce distortion of the data flow and are ineffectual.
Must scale to hundreds of thousands of active flows, perhaps millions.
Notes: 9
It is also unrealistic to attempt to provide end-to-end QoS in the Internet with any particular link-layer technology, such as ATM, since a packet in flight between a source and destination may traverse any number of link-layer transport media types (e.g. Ethernet, point-to-point serial links).
This is where the “most common denominator” philosophy comes into play. Since the “common bearer service” in the Internet is the TCP/IP protocol suite, this is the natural place to do traffic differentiation.

## Slide 86: Again: What is End-to-End?
10
Notes: 10

## Slide 87: Pervasive homogeneity - Not!
11
Reliance on link-layer mechanisms to provide QoS assumes pervasive end-to-end, desktop-to-desktop, homogenous link-layer connectivity.
  This is simply not realistic.
QoS as a differentiation mechanism will be operated in an variable load environment
  differentiation will be non-repeatable
Notes: 11

## Slide 88: State and Scale
12
To undertake firm commitments in the form of per-flow carriage guarantees requires network-level state to be maintained in the routers.
State becomes a scaling issue.
Wide-scale RSVP deployment will not scale in the Internet (See: RFC2208, RSVP Applicability Statement).
Notes: 12

## Slide 89: Network Layer Tools
13
  Traffic shaping and admission control.
  IP packet marking for both delay indication & discard preference.
  Weighted Preferential Scheduling algorithms.
  Preferential packet discard algorithms (e.g. Weighted RED, RIO).
End result: Varying levels of best effort under load.
No congestion, no problem. (Well, almost.)
Notes: 13
Various IP packet marking schemes have been proposed in the IETF. See:
  http://diffserv.lcs.mit.edu/
  http://www.employees.org:80/~ferguson/QoS.html
  http://cio.cisco.com/warp/public/732/net_enabled/qos_wp.htm
For more information on RED (Random Early Detection), see:
  http://www-nrg.ee.lbl.gov/floyd/red.html
If there is no congestion in the network, everyone’s packets get delivered and everyone is happy.

## Slide 90: Quality of Service Mechanisms
14
Notes: 14

## Slide 91: Router Mechanisms
A router has a limited set of QoS responses:
  Fragmentation
    fragment the packet (if permitted)
  Forwarding
    route the packet to a particular interface
  Scheduling
    schedule the packet at a certain queuing priority, or
    discard the packet

## Slide 92: QoS Service Element
15
What is the service element for QoS services?
  Network ingress element
Client Network
Provider Network
Ingress Filter
Notes: 15

## Slide 93: QoS Service mechanism
16
Admission traffic profile filter
  In-Profile traffic has elevated QoS, out-of-profile uses non-QoS
Client Network
Provider Network
Ingress Filter
Input stream
QoS marked stream
Notes: 16

## Slide 94: QoS Service by Application
17
  Application-based differentiation at ingress:
    TCP or UDP port number
    For example:
      set elevated priority for interactive services
        ports 80, 23, 523
      set background priority for bulk batch services
        port 119
Notes: 17

## Slide 95: QoS Service by Host
18
Selected sender’s traffic has elevated QoS:
    Source IP address filter
      If source address matches a.b.c.d set precedence to p
Traffic to selected receiver has elevated QoS
    Destination IP address filter
      if destination address matches a.b.c.d set precedence to p
Traffic between selected sender and receiver has elevated QoS
    Flow based QoS, using dynamic selection of an individual flow
    flow-class based QoS, triggered by source, receiver and port mask
Notes: 18

## Slide 96: QoS Service by profile
19
profile based on token bucket for constant rate profile
T
T
T
T
Constant Rate Token Stream
Data stream
Output Stream of marked packets
Notes: 19

## Slide 97: QoS Service by profile
20
profile based on leaky bucket for controlled burst profile
Data stream
Output Stream of marked packets
Rate overflow
mark path
Leaky bucket with max output rate
and QoS output mark
Notes: 20

## Slide 98: QoS Admission model
21
Network defined and determined
  user QoS indicators are cleared at ingress, replaced by network defined QoS indicators
User selected, network filters
  User QoS tags are compared against contracted profile of admitted traffic
    within contract packets are admitted unchanged
    other packets have cleared QoS indication
Notes: 21

## Slide 99: Precedence selection based on contract
22
Network enforces precedence value
  Source or Destination Address
  ingress interface
Might have two or three precedence values
  such as
    1 - RSVP traffic
    2 - Best effort traffic within some token bucket
    3 - All other traffic
Notes: 22

## Slide 100: QoS per packet indicators
23
Explicit per packet signaling of:
  Precedence indication (delay)
  Discard indication (reliability)
As an indication of preference for varying levels of best effort.
This is deployable - today.
Notes: 23

## Slide 101: QoS Indicators
24
How to ingress mark a QoS packet?
  Precedence marking
    use a precedence value field in the packet header
    field value triggers QoS mechanisms within the interior of the network
  Drop Preference marking
    use a drop preference value filed in the packet header
    interior switches discard packets in order of drop preference
Notes: 24

## Slide 102: QoS Indicators
25
both precedence and drop preference require uniform responses from the interior of the network, which in turn requires:
  uniform deployment of QoS-sensitive mechanisms within routers
  uniform inter-provider mechanisms (where agreed)
Notes: 25

## Slide 103: Virtual Circuits
26
Segmented bandwidth resource for QoS states:
  Ingress traffic shaping (token or leaky bucket)
  Virtual circuits & statistical muxing (e.g. ATM, Frame Relay)
  RSVP admission control & reservation state
Circuit segmentation mechanisms by themselves are unrealistic in a large scale heterogeneous Internet which uses end-to-end flow control.
Notes: 26

## Slide 104: QoS Paths
27
Alternate path selection
  Alternative physical paths
    E.g., cable and satellite paths
  QoS Routing v. administrative path selection
Must be managed with care.
Can lead to performance instability.
Prone to inefficient use of transmission.
May not support end-to-end path selection
Notes: 27

## Slide 105: Alternate paths
28
Notes: 28

## Slide 106: Quality of Service
29
Queuing Disciplines
FIFO queuing
Notes: 29

## Slide 107: FIFO queuing
30
Strict Round-Robin queuing discipline
4
3
1
6
2
5
1
2
3
4
5
6
Notes: 30

## Slide 108: Effects of FIFO queuing
31
Packet trains:
  Delay
  Jitter
4
3
1
6
2
5
1
2
3
4
5
6
Queuing-induced jitter component
Input timing
Output timing
Notes: 31

## Slide 109: Effects of FIFO queuing
32
Tail drop yields performance collapse
  FIFO queuing causes queue pressure, resulting in queue exhaustion and tail drop
  tail drop causes packet trains to have trailing packets discarded
  Without following packets the receiver will not send duplicate ACKs for the missing packets
  The sender may then have to timeout to re-transmit
  The timeout causes the congestion window to close back to a value of 1, and restart with Slow Start rate control
Notes: 32

## Slide 110: Interactive Traffic Timing
33
Milliseconds
0
500
1000
1500
2000
2500
3000
3500
0
50
100
150
200
250
300
350
400
450
500
550
600
FIFO Queuing
Notes: 33

## Slide 111: Quality of Service
34
Queuing Disciplines
Precedence queuing
Notes: 34

## Slide 112: Precedence Queuing
35
multiple queues, each served in FIFO order
2
4
1
7
3
6
1
2
4
5
6
3
1
2
3
4
5
7
Input arrival timing
Stream
precedence
Queue Output
Notes: 35

## Slide 113: Precedence Queuing
36
Jitter and delay for high precedence queues still present at short time intervals
Precedence algorithm denies any service to lower level queues until all higher level queues are exhausted
  This allows high precedence TCP sessions to open up sending window to full transmission capacity
  this causes protocol collapse for lower layer queues
Notes: 36

## Slide 114: Quality of Service
37
Queuing Disciplines
Class-based queuing
Notes: 37

## Slide 115: Class-based Queuing
38
multiple queues, serviced in proportionate levels
2
4
1
7
3
6
2
5
4
8
6
50%
20%
20%
10%
5
7
8
1
3
Notes: 38

## Slide 116: Class-based queuing
39
Divide service among traffic classes
Divide service among delay classes
Notes: 39

## Slide 117: Class-based Queuing
40
Class-based queues attempt to allocate fixed proportion of resource to each service queue
Address denial of service by attempt to guarantee some level of service is provided to each queue
Class-based queues are an instance of a more general proportionate sharing model
Class-based queues are fair only for time intervals greater than number of service classes multiplied by link MTU transmission time
Notes: 40

## Slide 118: Example of Class-based Queuing
41
Left
Right
34
Left router
  Queue-list by incoming interface
  Bytes per MTU rotation proportional to fiscal input
Right router
  Queue-list by destination CIDR prefix
  Bytes per MTU rotation proportional to fiscal input
Notes: 41

## Slide 119: Quality of Service
42
Queuing Disciplines
Weighted Fair Queuing
Notes: 42

## Slide 120: Weighted Fair Queuing
43
Attempts to schedule packets to closely match a theoretical bit-wise weighted min-max allocation mechanism
The mechanism attempts to adhere to the resource allocation policies at time scales which are finer than class-based queuing
Notes: 43

## Slide 121: Min-Max weighted fairness
44
Allocate resources to each stream in accordance with its relative weight, and interatively redistribute excess allocation in accordance with relative weight
Initial Weighting
Re-allocation following stream termination,
where 25% is redistributed to the remaining streams in the ration 5:3:1
Notes: 44

## Slide 122: Bit-wise Round Robin Fair Queuing
45
Time Division Multiplexer
Fair Queuing Objectives:
  Simulates a TDM
  One flow per TDM virtual channel
Notes: 45

## Slide 123: Bit-wise Scheduling
46
2
4
1
7
3
6
5
8
Bits from each class are serviced in strict rotation
This is equivalent to Time Division Multiplexing
Round-robin bit-wise service interval
Notes: 46

## Slide 124: Weighted Bit-wise Scheduling
47
2
4
1
7
3
6
5
8
50%
20%
20%
10%
bit service interval
bits from each class are serviced in rotation, weighted by relative service weight
Notes: 47

## Slide 125: Weighted Fair Queuing
48
1
4
2
7
3
6
2
5
4
8
6
50%
20%
20%
10%
5
7
8
1
3
Schedule traffic in the sequence such that a equivalent weighted bit-wise scheduling would deliver the same order of trailing bits of each packet
Notes: 48

## Slide 126: Weighted Fair Queuing
49
As a result, be as fair as weighted bit-wise scheduling, modulo packet quantization
Weighted fair queuing is min-max fair
Weighted fair queuing does require extensive processing to determine the weighted TDM finish time of each packet
Weighted fair queuing scales per precedence level, and not necessarily on a per flow basis.
Notes: 49

## Slide 127: Weighted Fair Queuing
50
Low queue occupancy flows
  All the bandwidth they can use
  Minimal delay
High queue occupancy flows
  Enforce traffic interleaving
  Fair throughput rates
Notes: 50

## Slide 128: Interactive Traffic Timing
51
Milliseconds
Fair Queuing
0
500
1000
1500
2000
2500
3000
3500
0
50
100
150
200
250
300
350
400
450
500
550
600
Notes: 51

## Slide 129: Interactive Traffic Timing
52
Milliseconds
Fair Queuing (Magnified)
0
50
100
150
200
250
300
0
50
100
150
200
250
300
350
400
450
500
550
600
Notes: 52

## Slide 130: Weighted Fair Queuing
53
Appropriate when
  Important flows have significant amounts of data in queue
Can be used for various administrative models
Traffic classification based on
  Source/destination information
  per data flow
  Artifacts of network engineering
  packet indication (precedence value)
Notes: 53

## Slide 131: Quality of Service
54
Queue Management
Weighted Random Early Deletion
Notes: 54

## Slide 132: Weighted Random Early Deletion - W-RED
55
Stated requirement
  “Avoid congestion in the first place”
  “Statistically give some traffic better service than others”
Congestion avoidance, rather than congestion management
Notes: 55

## Slide 133: Behavior of a TCP Sender
56
Sends as much as credit (TCP window) allows
Starts credit small (initial cwnd = 1)
  Avoid overloading network queues
Increases credit exponentially (slow start) per RTT
  To gauge network capability via packet loss signal
Notes: 56

## Slide 134
ACK packets
Data packets
R
S
ACK packets
Data packets
R
S
ACK packets
Data packets
R
S

## Slide 135: Behavior of a TCP Receiver
57
When in receipt of “next message,” schedules an ACK for this data
When in receipt of something else, acknowledges all received in-sequence data immediately
  i.e. send duplicate ACK in response to out of sequence data received
Notes: 57

## Slide 136
ACK packets
Data packets
R
S
ACK packets
Data packets
R
S
Dropped Packet
Duplicate ACKs

## Slide 137: Sender Response to ACK
58
If ACK advances sender’s window
  Update window and send new data
If not then it’s a duplicate ACK
  Presume it indicates a lost packet
  Send first unacknowledged data immediately
  Halve current sending window
  shift to congestion avoidance mode
  Increase linearly to gauge network throughput
Notes: 58

## Slide 138: Implications for Routers
59
Dropping a data packet within a data sequence is an efficient way of indicating to the sender to slow down
  Dropping a data packet prior to queue exhaustion increases the probability of successive packets in the same flow sequence being delivered, allowing the receiver to generate duplicate ACKs, in turn allowing the sender to adjust cwnd and reducing sending rate using fast retransmit response
  Allowing the queue to fill causes the queue to tail drop, which in turn causes sender timeout, which in turn causes window collapse, followed by a flow restart with a single transmitted segment
Notes: 59

## Slide 139: RED Algorithm
60
Attempt to maintain mean queue depth
Drop traffic at a rate proportional to mean queue depth and time since last discard
Probability
of packet
drop
1
0
Onset of
RED
Queue
exhaustion
tail
drop
Average queue depth
RED
discard
Notes: 60

## Slide 140: Weighted RED
61
Alter RED-drop profile according to QoS indicator
  precedence and/or drop preference
1
0
Discard Probability
Weighted Queue Length
High priority traffic
Low priority traffic
1
0
Notes: 61

## Slide 141: Outcomes of RED
62
Increase overall efficiency of the network
  ensure that packet loss occurs prior to tail drop
  allowing senders to back off without need to resort to retransmit time-outs and window collapse
  ensure that network load signaling continues under load stress conditions
Notes: 62

## Slide 142: Outcomes of W-RED
63
High precedence and short duration TCP flows will operate without major impact
  RED’s statistical selection is biased towards large packet trains for selection of deletion
Low precedence long held TCP flows will back off transfer rate
  by how much depends on RED profile
W-RED provides differentiation of TCP-based traffic profiles
  but without deterministic level of differentiation
Notes: 63

## Slide 143: Pitfalls of RED
64
No effect on UDP
Packet drop uses random selection
  Depends on host behavior for effectiveness
  Not deterministic outcome
Specifically dependent on
  bulk of traffic being TCP
  TCP using RTT-epoch packet train clustering
    ACK spacing will reduce RED effectiveness
  TCP responding to RED drop - but not all TCPs are created equal
Notes: 64

## Slide 144: Weighted RED
65
Appropriate when
  Any given flow has low probability of having data in queue
Stochastic model
Reduces turbulent inputs
Traffic classification based on IP precedence
  Different min_threshold values per IP precedence value
Notes: 65

## Slide 145: Quality of Service
66
Link Management
Fragmentation
Notes: 66

## Slide 146: PPP with fragmentation
67
Jumbogram
Voice 2
Voice 1
Fragment 4
Fragment 3
Fragment 2
Fragment 1
Voice 2
Voice 1
Fragment large packets
Let small packets interleave with fragmented traffic
Delay
Delay
Notes: 67

## Slide 147: PPP with fragmentation
68
You COULD define different MTU sizes per traffic QoS profile
  lower precedence traffic has lower associated link MTU
This is a future
  performance impact through increased packet switching load is not well established
  MTU discovery and subsequent alteration of QoS will cause IP fragmentation within the flow
Notes: 68

## Slide 148: Quality of Service
69
Link Management
ATM Virtual Circuits
Notes: 69

## Slide 149: Separate VCs
70
Appropriate to ATM only
Linear behavior between VCs
Notes: 70

## Slide 150: ATM with Separate VCs
1
One VC per
  Set of flows through given set of neighbors with matching QoS requirements
Edge device routes traffic on VC with appropriate set of characteristics
Normal Traffic
QoS Traffic
Notes: 1

## Slide 151: ATM with per-precedence VCs
2
One VC per precedence level
Edge device routes traffic on VC with appropriate set of characteristics
Traffic classification based on IP precedence(!)
  High precedence traffic gets predictable service
  Low precedence traffic can get better service from ATM network than high precedence traffic
  Potential re-ordering within transport layer flow
Precedence 0
Precedence >0
Notes: 2

## Slide 152: Quality of Service
3
Routing Management
QoS Routing
Notes: 3

## Slide 153: Type of Service (TOS) Routing
4
“low delay”
“high throughput”
Intra-domain
  OSPF
  Dual IS-IS
Inter-domain
  IDRP
Notes: 4

## Slide 154: Circuit Switch QoS Routing
5
Sequential Alternate Routing
Notes: 5

## Slide 155: Sequential Alternate Routing
6
Hop by hop
Advertises
  Available bandwidth on path
  Hop count
Tries to route call:
  Successively less direct paths
  That have enough bandwidth
If cannot route a call
  Tells upstream switch to try next potential path
Notes: 6

## Slide 156: Sequential Alternate Routing
7
Observations
  Improves the throughput when traffic load is relatively light,
  Adversely affects the performance when traffic load is heavy.
Harmful in a heavily utilized network,
  Circuits tend to be routed along longer paths
  Use more capacity.
Notes: 7

## Slide 157: IP QoS routing experiments
8
Original ARPANET routing (1977)
IBM SNA COS routing
QOSPF
Integrated PNNI
Notes: 8

## Slide 158: Original ARPANET routing (circa 1977)
9
Ping your neighbor
  Link metric is ping RTT
Seek to minimize path delay
Subject to route oscillation:
  selected minimize delay path saturates
  RTT rises due to queue length increase on selected path
  alternate minimum delay path chosen
Notes: 9

## Slide 159: IBM SNA COS routing
10
Historically, heavy manual configuration
APPN High Performance Routing
  Dynamic routing reduces configuration
  Adds predictive methods to improve behavior
Notes: 10

## Slide 160: QOSPF
11
QoS extensions to OSPF
  Add link resource and utilization records
  Calculate call path at each node
  Use global state to direct this
  Issues of simultaneity
Notes: 11

## Slide 161: Simulation results in QOSPF
12
“Thus far we have found the target environment is fully able to break any naive simulation we try.”
Notes: 12

## Slide 162: Integrated PNNI
13
Extends ATM PNNI to support IP
Adaptive alternate path routing with crankback
Notes: 13

## Slide 163: PNNI algorithm combines:
14
Link State (SPF)
  Ingress node calculates full path
Source Routing
  Successive nodes merely accept or reject ingress node’s choice
Notes: 14

## Slide 164: PNNI does not address...
15
Multicast routing
Policy routing
Alternate routing control
Notes: 15

## Slide 165: QoS routing constraints
16
Security issues
Policy issues
Scaling
Notes: 16

## Slide 166: Flow Priorities and Preemption
17
Some flows are more equal than others
  Flow routing
  Data forwarding
How do we:
  Identify these securely?
  Bill for them?
  Preempt existing flows in a secure fashion?
Notes: 17

## Slide 167: Resource Control
18
Resources applied to differing QoS requirements
Enable traffic engineering
Notes: 18

## Slide 168: Scale is the technical problem
19
Per-flow state can be huge -- unrealistic.
Less than per-flow routing forces unnatural engineering choices
  All calls from A to B take same path?
  All calls require different VCs?
Notes: 19

## Slide 169: Routing overheads
20
State distribution
State storage
Route calculation
Notes: 20

## Slide 170: Inter-domain policy issues
21
Need to handle call accounting well
  Inter-ISP settlements...
If route metric is path delay of a call, then a competitive service provider:
  Possesses path data
  Could publish the data for marketing purposes
  Could engineer networks adversely
Notes: 21

## Slide 171: Now that you think you understand the problem...
22
Repeat the sentence using the word ‘multicast’
Notes: 22

## Slide 172: The QoSR plan for the moment
23
Develop a framework for research
Test protocols that appear promising
Notes: 23

## Slide 173: Quality of Service RSVP
24
Notes: 24

## Slide 174: RSVP
25
RFC2205, “Resource ReSerVation Protocol (RSVP) – Version 1 Functional Specification”
RFC2208, “Resource ReSerVation Protocol (RSVP) Version 1 Applicability Statement, Some Guidelines on Deployment”
Requires hop-by-hop, per-flow, path & reservation state
Scaling implications are enormous in the Internet
Notes: 25

## Slide 175: RSVP Path messages
26
Notes: 26

## Slide 176: RSVP Resv messages
27
Notes: 27

## Slide 177: RSVP Data Flow

## Slide 178: RSVP-based QoS
RSVP can implement service commitments:
  Delivers a service guarantee to a preset bandwidth rate.
  Deliver a service commitment to a controlled load profile.
  Limit packet loss to a preset threshold.
  Limits delay to a maximal queuing threshold.
  Place a preset bound on jitter.
Challenging to implement in a large network
Relatively easy to measure success in meeting the objective

## Slide 179: RSVP and the Internet
RSVP requires the imposition of flow state onto network routers in order to meet the stringent requirements of a service guarantee for a flow
Such state mechanisms do not readily scale to the size of the Internet
  unless you want to pay the price of higher unit switching costs

## Slide 180: RSVP Observations
28
May enjoy some limited success in smaller, private networks
May enjoy success in networks peripherally attached to global Internet
Unrealistic as QoS tool in the Internet
Notes: 28

## Slide 181: Quality of Service LAN Considerations
29
Notes: 29

## Slide 182: QoS and LANs
30
Subnet Bandwidth Manager (SBM)
IEEE 802.1p
Notes: 30

## Slide 183: Subnet Bandwidth Manager (SBM)
31
IETF Internet Draft, “SBM (Subnet Bandwidth Manager): A Proposal for Admission Control over IEEE 802-style networks,” draft-ietf-issll-is802-bm-5.txt
Integrates RSVP into traditional link-layer devices for IEEE 802 LANs
Effectiveness is questionable without IEEE 802.1p support/integration
Notes: 31

## Slide 184: SBM message flow
32
Notes: 32

## Slide 185: IEEE 802.1p
33
“Supplement to MAC Bridges: Traffic Class Expediting and Dynamic Multicast Filtering,” IEEE P802.1p/D6.
Extended encapsulation (802.1Q).
Method to define relative priority of frames (user_priority).
IEEE 802.1p support in LAN switches would provide transmission servicing based on relative priority indicated in each frame (delay indication).
Notes: 33

## Slide 186: Quality of Service Dial Access
34
Notes: 34

## Slide 187: QoS and Dial Access
35
Most of the Internet’s users connect to the Internet via dial access
Dial access has very few built-in QoS mechanisms today
If there is to be widespread deployment of QoS then its reasonable to expect robust and effective QoS mechanisms to be available to dial access clients
Notes: 35

## Slide 188: QoS and Dial Access
36
Service Quality First: Port availability, no busy signals
Differentiation Second: Determine methods to differentiate traffic
Conventional thinking: Provide differentiation at upstream aggregation point (next hop)
Notes: 36

## Slide 189: QoS and Dial Access
37
Port pool management
Differentiation of port availability
  separate port pools for each service level
    ensure premium pool meets peak call demand levels
  multiple logical pools using a single physical pool
    allow incoming calls for premium access callers when total pool usage exceeds threshold level
Notes: 37

## Slide 190: QoS and Dial Access
38
QoS with a twist:
  A low bandwidth line requires decisions on priorities
  QoS differentiation between simultaneous applications on the same access line
    ie: www traffic has precedence over pop traffic
  QoS differentiation is NOT at the host
  QoS differentiation is at the dial access server
Queue bottleneck point
Internet
Dial Access Server
Notes: 38

## Slide 191: QoS and Dial Access
39
The problem here is how to load service management rules into the dial access server to implement the user’s desired service profile
Radius profiles
  per-user profiles are loaded in the dial access server as part of session initiation
  use radius extensions to load service profile
  no changes required to host environment
Notes: 39

## Slide 192: QoS and Dial Access
40
Radius service profile
Internet
Dial Access Server
Radius
Server
Radius Profile
loaded at session start
Loaded Service Management Profile
Notes: 40

## Slide 193: Quality of Service Measuring QoS
41
Notes: 41

## Slide 194: QoS Measurement Tools
42
QoS measurement tools available today:
Notes: 42

## Slide 195: QoS Measurement Tools
43
We can instrument tools to measure network
  delay
  jitter
  bandwidth
  reliability
on a specific path, at a specific times
But we cannot measure network-wide QoS
  its not a concept which translates into an artifact which is directly measureable
Notes: 43

## Slide 196: QoS Measurement Tools
44
SNMP monitoring of routers
real time monitoring of ‘network component health’ by measuring for each link:
  link occupancy
  packet throughput
  mean queue depth
  queue drop levels
Use these metrics to create a link congestion metric
Notes: 44

## Slide 197: QoS Measurement Tools
45
Host-based probes to measure path state
  ping
    measures end-to-end delay & jitter
  bing
    provides per-hop total bandwidth estimate by differential timing across a single hop
  traceroute
    delay, and reliability measurement through path trace
  treno
    measures available bandwidth through TCP reno simulation with ping packets
Notes: 45

## Slide 198: QoS Measurement
46
SNMP and host probes
  What the user wants to measure
    the difference in performance between QoS differentiated and ‘normal’ service transactions
  What the tools provide
    a view of the performance of the components of the network, not a view of the performance of a network transaction
Notes: 46

## Slide 199: Host Measurement of QoS
47
Measure the TCP transaction at the sender
  stability of RTT estimate
  stability of congestion point (available bandwidth)
  incidence of tail drop congestion
  incidence of timeout
Sustainable TCP transfer rate
Notes: 47

## Slide 200: Host Measurement of QoS
48
Measure the TCP transaction at the receiver
  incidence of single packet drop
  incidence of tail drop congestion
  duplicate packets
  out of order packet
Sustainable TCP transfer rate
Notes: 48

## Slide 201: Host Measurement of QoS
49
Measure the UDP service at the reciever
  measure signal distortion components
    loss, jitter, delay, peak received rate
Notes: 49

## Slide 202: QoS Measurement
50
Internet performance metrics are still immature
We have
  tools to measure individual artifacts of performance
  Tools to measure individual session performance
Notes: 50

## Slide 203: QoS Measurements
51
We don’t have
  tools to measure quality potential
    “As a client, if I were to initiate a session with elevated priority how much faster would the resultant transaction be?”
  tools to measure quality delivery
    “As a provider, am I providing sufficient resources to provide discernable differentiation for elevated quality services?”
Notes: 51

## Slide 204: Quality of Service Host Considerations
52
Notes: 52

## Slide 205: QoS in the network is fine, BUT...
53
performance of an application is dependant on
  the state of the network
  the sender and the receiver
poor performance is often the outcome of poor or outdated protocol stacks
Notes: 53

## Slide 206: Performance Issues
54
Major benefits can be gained by using protocol stacks which support:
  large buffers and window scaling options
  selective acknowledgement (SACK)
  correct RTT estimate maintenance
  correct operation of window management algorithms
  MTU discovery
  initial cwnd value of 4
and use hosts with
  enough memory and CPU to drive the protocol
Notes: 54

## Slide 207: Network or Host
55
QoS in the network is not always the right answer to the question of poor performance.
Often the problem is the box behind your screen!
Notes: 55

## Slide 208: Quality of Service Marketing QoS
56
Notes: 56

## Slide 209: Marketing
57
What is being marketed?
  current base is variable best effort
  better than best effort?
    PREMIUM SERVICE
  worse than best effort ?
    BUDGET SERVICE
  constant effort ?
    DEDICATED SERVICE
Notes: 57

## Slide 210: Marketing
58
Pricing and QoS
  sender pays for premium / discount service
  service level set at packet ingress based on source admission policy
    at ingress?
    at egress ?
  receiver pays for premium / discount service
  service level set at packet ingress based on destination admission policy
    at egress
Notes: 58

## Slide 211: Marketing QoS is not easy...
59
Premium / Discount services are relative to best effort Base
Base level service quality varies on current load and path
Differentiated service levels difficult to quantify to customer
How are Service Level Agreements phrased for differentiated service environments?
Notes: 59

## Slide 212: Marketing
60
High variability of base level service is an impediment to marketing QoS
Marketing QoS will also require
  service level agreements
  dissemination of robust measurement tools able to measure differential quality
  accurate expectation setting
Notes: 60

## Slide 213: Quality of Service Summary
61
Notes: 61

## Slide 214: Current QoS Mechanisms
62
Rate Control
  token bucket
  leaky bucket
      admission mechanisms
Queuing control
  weighted Fair Queuing
  weighted RED
      internal resource management mechanisms
Notes: 62

## Slide 215: Current QoS Mechanisms
63
Link control
  Parallel Virtual Circuits
  MTU management
      Data Link layer differentiation
RSVP
  guaranteed load service
  controlled load service
      limited environment of deployment
Notes: 63

## Slide 216: Current QoS Mechanisms
64
Routing
  QoS Routing
      experimentation proceeds!
Notes: 64

## Slide 217: QoS Implementation Considerations
65
Complexity:
  If your support staff can’t figure it out, it is arguably self-defeating
Delicate balance between quality of network design & architecture and QoS differentiation mechanisms
Notes: 65
Building a network is only a small percentage of solving the overall problem -- once the network is built, someone has to provide ongoing management, maintenance, and troubleshooting support. If the network is excessively complex to the point where your support staff cannot figure it out, or has trouble pinpointing problems due to the complex nature of the network, then this is an important liability.
Remember Occam’s Razor, “All things being equal, choose the solution which is simpler.”
There is a delicate balance between the design & architecture of the network, and the ability to provide ongoing Quality of Service. If the network is designed poorly, then one might suggest that the ability to provide QoS is diminished significantly.

## Slide 218: Yet to be Resolved
66
Only long-held adaptive flows are highly susceptible to network layer shaping
  Symmetric handling of TCP QoS service requests
  Short held flows (WWW transactions) are not very susceptible to network layer shaping
UDP flow management
  Unicast flow model (ingress filter or sender moderation?)
  Multicast flow model (multi-layering of the signal?)
Inter-Provider semantics & agreements for differentiated services
Notes: 66
Some other unanswered questions still are being examined, such as non-adaptive flows and bit semantics interpretation between different administrative domains.
The IETF Integrated Services working group has begun examining these issues in an effort dubbed “Differential Services” (diffserv). More information can be found on diffserv efforts at:
http://diffserv.lcs.mit.edu/

## Slide 219: Unanswered Questions
67
How does the provider measure QoS?
How does the customer measure QoS?
How do you tariff, account, and bill for QoS?
How will QoS work in a heterogeneous Internet?
  QoS across transit administrative domains which may not participate or use different QoS mechanisms?
Notes: 67
Unanswered questions still exist in several areas with regard to QoS, such as how to measure and bill for QoS services, as well as how to provide end-to-end QoS when an administrative domain within the traffic path does not participate (or honor) the QoS mechanisms and semantics.
A couple of groups are looking a traffic measurement in the Internet, and perhaps in the future, may also begin to look at how to measure QoS:
The IETF IP Performance Metrics (ippm) working group:
  http://www.ietf.org/html.charters/ippm-charter.html
  Cooperative Association for Internet Data Analysis (CAIDA):
  http://www.caida.org/

## Slide 220: Summary
There are no absolute guarantees in the Internet. Sorry.
Notes: 68

## Slide 221: Summary
There is no magic QoS bullet. Sorry.
Notes: 69

## Slide 222: Summary
70
There is possibly a “middle ground” somewhere between traditional single level best effort and guaranteed customized services.
Notes: 70

## Slide 223: References
71
Quality of Service: Delivering QoS in the Internet and the Corporate Network http://www.wiley.com/compbooks/ferguson/
Differential Services in the Internet http://diffserv.lcs.mit.edu/
Notes: 71

## Slide 224: Questions? Thank you.
72
Geoff Huston
Technology Manager
Telstra Internet
gih@telstra.net
Notes: 72