## Slide 1: Unique Local IPv6 Unicast Addresses
A review from an RIR perspective
Geoff Huston
August 2003

## Slide 2: Background
IPv6 address architecture includes the requirement for local use addresses that are:
  Useable in a local (non-connected context)
  Span more than a link
  Are not components of a provider aggregate address block
  Not intended to be globally routed
  Unique (no NATS!)
  Unicast addresses

## Slide 3: Local Use Addresses
The IETF IPv6 Working Group is considering alternatives to Site-Local Addresses
  (This presentation is not intended to be a repeat of the Site-Local debate!)
One proposal is to use a block of the Global Unicast Address space for “local” use
  Where “local” implies “not anticipated to be globally routed”
  See “draft-hunden-ipv6-global-local-addr-02.txt” for the complete text of the proposal

## Slide 4: Questions Raised by the Proposal
What are the desireable characteristics of Local Use addresses?
What distribution mechanisms are called for?
Is there a role for the RIRs here?
If so what issues would this raise for the RIRs to consider?

## Slide 5: Characteristics of Local Use Addresses
Exclusive use of a common prefix drawn from the global unicast address space for all local use addresses (FC00::/7)
Unique assignment of a fixed size local use address block (/48) from within the pool of addresses defined by this prefix, using a Global ID as the block prefix.
There is no internal structure within the global ID, and these global IDs cannot be aggregated in a routing context.
The assignment information must be recorded and stored in a reliable manner.
Local Use Addresses are not intended to be passed within the global routing environment

## Slide 6: The Proposal
Use /48 blocks drawn from FC00::/7
An End user may either:
use a random number pick to draw a /48 block from FC00::/8
or:
obtain a unique /48 block from a registry that manages FD00::/8

## Slide 7: A Local Use Registry System
A Local Use Registry system should be:
  Readily accessible for anybody
  Highly automated
  No justification required
  Limited identity requirement
  Rapid turnaround
  Inexpensive
  Allocate randomly from the block
  Transparency of charges
  Allow for once-and-forever allocation services
  Allow for agency structures
  Reliable and enduring records of unique allocations
  Limited publication of allocations

## Slide 8: RIR Considerations
Service model (renewable, non-renewable)
Transaction model rather then membership based
Service fees to be cost-based
Record management
High volume low value transaction model
Preserve Local Use Address Characteristics (non-aggregatable, no public per-allocation records, stable allocations, non-hoardable)
Regulatory issues (competition, fee setting, equal access)

## Slide 9: RIR Considerations
This can be seen as a distinct service activity, not a seamless adjunct to existing activities:
  Transactions, not membership
  High volume, low value
  Automated applications without evaluation
  Limited publication of allocations
Considerations:
  Local agency activities?
  Wholesaling?
  Transfers?
  ?