## Slide 1: Today’s Mobile Internet
Geoff Huston,
APNIC

## Slide 2
The most profound technologies are those that disappear. They weave themselves into the fabric of everyday life until they are indistinguishable from it...
- Mark Weiser 1991

## Slide 3
So how should we look at mobile devices and the Internet?
Are these merely a temporary consumer fad, destined to be replaced by the next cool technology item?
Or is this an instance of a profound technology change that will bed down to be a part of our everyday life for many years to come?

## Slide 4
To try and answer this, lets try and put this question into some broader context of the evolution the computer and communications enterprise

## Slide 5: The Computing Evolutionary Path
1946 – Eniac – a numeric calculator

## Slide 6: The Computing Evolutionary Path
1946 – Eniac – a numeric calculator
1954 SAGE – a programmable computer

## Slide 7: The Computing Evolutionary Path
1964: IBM 360
1964 IBM 360 – commercial computing

## Slide 8: The Computing Evolutionary Path
The Computing Evolutionary Path
1976 CRAY-1 – “super” computing

## Slide 9: The Computing Evolutionary Path
1976: Apple I
The Computing Evolutionary Path
A fork in the road:
1976 – Apple-1 “personal” computing

## Slide 10
The Computing Evolutionary Path
1984 – Mac - visual computing

## Slide 11
The Computing Evolutionary Path
1993 – Intel - Pentium processor

## Slide 12
The Computing Evolutionary Path
2007 – Apple’s iPhone

## Slide 13
** Depending on whether you buy into Apple’s denial of Flash for iOS or not!
* Yes, WAP was a hideous mistake. Hopefully we’re over it now!
Today’s mobile device is a digital device that has the computing capability of a laptop device, with the form function of a mobile phone or small tablet.
It is an Internet-connected device with a general purpose browser* and a full** set of media capabilities

## Slide 14
** Depending on whether you buy into Apple’s denial of Flash for iOS or not!
* Yes, WAP was a hideous mistake. Hopefully we’re over it now!
Today’s mobile device is a digital device that has the computing capability of a laptop device, with the form function of a mobile phone or small tablet.
It is an Internet-connected device with a general purpose browser* and a full** set of media capabilities
And they are transforming the Internet!

## Slide 16
With desktop devices the Internet was a dedicated activity
dedicated chair
lighting
wired bandwidth
large view screens
privacy
dedicated worktop
reliable power

## Slide 17
The Internet is now anywhere and everywhere
Its trivial, commonplace and blends into all our activities
radio connectivity
battery power
hand sized
Thumb
operated

## Slide 18: Counting Users...
Chart: Internet users per 100 inhabitants, 2000-2010
| 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
Developed | 24.5969 | 29.3705 | 37.6501 | 41.4505 | 46.3356 | 51.3 | 53.5 | 59.1 | 61.3 | 64.7 | 68.8
World | 6.4126 | 7.9548 | 10.7038 | 12.2859 | 14.0958 | 15.7 | 17.5 | 20.6 | 23.4 | 26.5 | 29.7
Developing | 2.0154 | 2.8363 | 4.3359 | 5.4691 | 6.6409 | 7.7 | 9.4 | 12 | 15 | 18.5 | 21.1
http://www.itu.int/ITU-D/ict/statistics/
There are 2 billion Internet users today

## Slide 19: Counting Users...
Chart: Per 100 inhabitants
| 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
Developed | 39.242 | 47.0996 | 52.5002 | 59.5246 | 69.8202 | 82.1 | 92.9 | 102 | 108.5 | 113.2 | 114.2
World | 12.034 | 15.4644 | 18.3827 | 22.2211 | 27.311 | 33.9 | 41.8 | 50.6 | 59.9 | 68.3 | 78
Developing | 5.4547 | 7.9034 | 10.3201 | 13.5019 | 17.4815 | 23 | 30.2 | 39.1 | 49.1 | 58.4 | 70.1
There are 2 billion Internet users today
And 5 billion mobile phone users!
http://www.itu.int/ITU-D/ict/statistics/

## Slide 20: Counting Users...
Chart: Per 100 inhabitants
| 2007.0 | 2008.0 | 2009.0 | 2010.0
Developed | 18.5 | 27.4 | 34 | 46.2
World | 4 | 6.3 | 7.8 | 12.6
Developing | 0.8 | 1.6 | 2 | 5.3
There are 2 billion Internet users today
And 5 billion mobile phones!
And 630 million mobile Internet users!
Source: Generator Research

## Slide 21: Counting Bytes
http://statcounter.com/
8.5%
4.3%
Mobiles consume one tenth of the data than wired devices

## Slide 22: Production Numbers
  2011: 270 million units shipped
  Factors:
    Production volumes are bringing down component unit cost
    Android is bringing down software unit cost
    No need for new content - leverage off the the existing web universe of content
    Shift away from the desktop and the laptop by the production industry seeking new markets for their production capability

## Slide 23: Who is playing
Android
  19% of all smartphone shipments in 2011 – projected to reach 25% in 2015
  Multi-vendor adoption
  Android also extending into tablets and large screens
Apple iPhone / iPad
  18% of all smartphone shipments in 2011 – projected to remain steady through to 2015
  High revenue margins for Apple: $27B in 2011 to (proj.) $39B in 2015
RIM Blackberry
  highest revenue margin product (44%)
  Likely not to keep pace with market growth in the next 4 years
  2011 service disruptions have accelerated decline in market share
Nokia
  35% of all smartphones in 2011 – likely to drop to 30% in 2015
  Open question whether the Windows Phone OS will turn around Nokia’s fortunes

## Slide 24: Sales Projections by OS
 | Units Shipped (M) |  |  |  | 
 | 2011 | 2012 | 2013 | 2014 | 2015
Android | 50 | 68 | 88 | 108 | 125
Apple iOS | 47 | 60 | 72 | 83 | 92
RIM | 43 | 49 | 55 | 58 | 60
Symbian | 94 | 100 | 97 | 85 | 67
Windows | 14 | 32 | 54 | 81 | 110
Other | 21 | 26 | 30 | 34 | 36
 | 269 | 335 | 396 | 449 | 490
Source: Generator Research

## Slide 26: Apple’s Numbers
iPhones:
Q3 2010 : Apple shipped 8.4M iPhones
Q3 2011 : Apple shipped 20.3M iPhones
  Added 42 carriers and 15 countries in the quarter!
iPads:
Q3 2010 : Apple shipped 3.3M iPads
Q3 2011 : Apple shipped 9.2M iPads
  “every iPad we could make has been sold”
Q3 2011 profit: $US 7.3B

## Slide 27: Apple’s Numbers
iPhones:
Q3 2010 : Apple shipped 8.4M iPhones
Q3 2011 : Apple shipped 20.3M iPhones
  Added 42 carriers and 15 countries in the quarter!
iPads:
Q3 2010 : Apple shipped 3.3M iPads
Q3 2011 : Apple shipped 9.2M iPads
  “every iPad we could make has been sold”
Q3 2011 profit: $US 7.3B
And Q4 2011 was even bigger!

## Slide 28: Apple’s Numbers
iPhones:
Q3 2010 : Apple shipped 8.4M iPhones
Q3 2011 : Apple shipped 20.3M iPhones
  Added 42 carriers and 15 countries in the quarter!
iPads:
Q3 2010 : Apple shipped 3.3M iPads
Q3 2011 : Apple shipped 9.2M iPads
  “every iPad we could make has been sold”
Q3 2011 profit: $US 7.3B
And Q4 2011 was even bigger!
37M iPhones
15M iPads
$13.1B profit!

## Slide 29: Mobiles by Money
Source: Generator Research

## Slide 30: Technology for Mobility

## Slide 31: 2G: GSM
Groupe Spécial Mobile standards, developed by ETSI for second generation digital cellular networks, replacing the earlier analogue system (AMPS)
Data Services Provided by a General Packet Radio Service (GPRS) sub-system
  Data rates: typically 16 – 32kbps, with latency of ~600ms
  Higher speeds require more timeslots from the Base Transceiver Station

## Slide 32: 2G: GSM
Groupe Spécial Mobile standards, developed by ETSI for second generation digital cellular networks, replacing the earlier analogue system (AMPS)
Data Services Provided by a General Packet Radio Service (GPRS) sub-system
  Data rates: typically 32 – 40kbps, with latency of ~600ms
  Higher speeds require more timeslots from the Base Transceiver Station
Kbps – suitable for WAP – just!

## Slide 33: 3G: HSPA
High Speed Packet Access – an evolution of W-CDMA
  Peak data rates 20Mbps downlink, 5.8Mbps Uplink
  Shared channels, shorter Transmission Time Intervals, adaptive use of 16QAM and 64QAM access to increase spectrum efficiency

## Slide 34: 3G: HSPA
High Speed Packet Access – an evolution of W-CDMA
  Peak data rates 20Mbps downlink, 5.8Mbps Uplink
  Shared channels, shorter Transmission Time Intervals, adaptive use of 16QAM and 64QAM access to increase spectrum efficiency
Mbps – acceptable performance – but nothing special

## Slide 35: 3G: HSPA+
Evolved HSPA
  Theoretical peak of 84Mbps downlink, 22Mbps uplink
  Obtained by MIMO (multiple antenna technique) plus 64QAM

## Slide 36: 3G: HSPA+
Evolved HSPA
  Theoretical peak of 84Mbps downlink, 22Mbps uplink
  Obtained by MIMO (multiple antenna technique) plus 64QAM
10s of Mbps – decent broadband performance

## Slide 37: 4G: LTE
Theoretical maximum peak speed* 326Mbps
Practical achievable speeds of 4 – 12 Mbps
All IP internal architecture
* Probably assuming the absence of many of the laws of physics as we understand them 
Now it gets interesting!

## Slide 38: By The Numbers
Lets look at the allocation statistics to examine how mobiles have impacted overall network growth

## Slide 39: Internet Growth
2010 – 248m

## Slide 40: Top 10 Countries, 2009-2011

## Slide 41: Largest Allocations in 2011
30% of the addresses
18 Carriers -->

## Slide 42: Where are we headed?

## Slide 43: Where are we headed?
So far the mobile Internet has been constructed exclusively using IPv4 infrastructure
The Asia Pacific region region has an aggregate demand for 100M addresses p.a. to support network service growth
The global demand for V4 addresses is now approaching 300M addresses p.a.
Today’s mobile internet continues to grow by consuming accumulated address stockpiles and extensive use of NATs
But what about tomorrow?

## Slide 44: V4 Demand Projection
Global IPv4 supply shortfall is predicted to reach 800m addresses by 2014

## Slide 45: V6 and Mobile Devices
Android
IPv6 Support in 2.2 (in the radio module for some)
Dual Stack support in some apps
Apple
IPv6 has been added to iOS (wlan, not radio)
Dual Stack support added to browser
Windows Phone
still not yet (coming in Apollo release?)

## Slide 46: V6 and Radio Access Providers
Public details are scant:
  In the US:
    Some pilots by T-Mobile in the US
    Some early announcements by Verizon about future intent for its LTE network and IPv6
  Elsewhere:
    Slovenia: Mobitel
    Norway: NWN (?)
    ???
What about everyone else?

## Slide 49: Thank You!
Questions?