## Slide 1: The eBGP DFZ in 2011
Geoff Huston
APNIC

## Slide 2
“The rapid and sustained growth of the Internet over the past
several decades has resulted in large state requirements for
IP routers. In recent years, these requirements are continuing
to worsen, due to increased deaggregation (advertising more specific
routes) arising from load balancing and security concerns..”
“Conventional “wisdom” about routing:
Quoted from a 2012 research paper on routing

## Slide 3
“The rapid and sustained growth of the Internet over the past
several decades has resulted in large state requirements for
IP routers. In recent years, these requirements are continuing
to worsen, due to increased deaggregation (advertising more specific
routes) arising from load balancing and security concerns..”
“Conventional “wisdom” about routing:
quote from a 2012 research paper on routing
Is this really true, or do we accept it as true without actually looking at the real behaviours of the Internet’s routing system???

## Slide 4: Agenda
In this presentation we will explore the space of inter-domain routing (the Border Gateway Protocol – BGP
  We will look at the growth of the eBGP routing table over time and some projections for future growth
  Then we’ll look at the extent to which more specifics are dominating routing table growth ... or not

## Slide 5: The Big Picture of BGP Growth

## Slide 6: The Big Picture of the v4 Routing Table

## Slide 7: The Big Picture of the v4 Routing Table
Introduction of
CIDR – March 1994
The Great Internet Boom
and Bust of 2000/2001
Broadband to the Masses
The GFC hits the Internet
Address Exhaustion

## Slide 8: The Routing Table in 2010-2011
Lets look at the recent past in a little more detail...

## Slide 9: IPv4 BGP Prefix Count 2010 - 2011
Jan
2010
Jan
2011
320,000
350,000
380,000
Jul
2010
Jul
2011
Jan
2012

## Slide 10: IPv4 BGP Prefix Count 2010 - 2011
Jan
2010
Jan
2011
320,000
350,000
380,000
Jul
2010
Jul
2011
Jan
2012
Route Aggregation events
APNIC IPv4 runout day

## Slide 11: IPv4 Routed Address Span
2010
2011
Jan
2010
Jan
2011
Jul
2010
Jul
2011
130/8s
140/8s
150/8s
Jan
2012

## Slide 12: IPv4 Routed Address Span
2010
2011
Jan
2010
Jan
2011
Jul
2010
Jul
2011
130/8s
140/8s
150/8s
Jan
2012
/8 advertisements (by RIRs)

## Slide 13: IPv4 Routed AS Count
36,000
39,000
2010
2011
Jan
2010
Jan
2011
Jul
2010
Jul
2011
Jan
2012
33,000

## Slide 14: IPv4 2011 BGP Vital Statistics
Jan-11 Jan-12
Prefix Count 341,000 390,000 +14%
Roots 168,000 190,000 +13%
More Specifics 173,000 200,000 +15%
Address Span 140/8s 149/8s + 6%
AS Count 36,400 39,800 + 9%
Transit 5,000 5,700 +14%
Stub 31,400 34,100 + 9%

## Slide 15: IPv4 in 2011
Overall Internet growth in terms of BGP is at a rate of some ~12% p.a.
  This is much the same as 2009 and 2010.
Table growth has slowed since 20 April 2011, following APINC’s IPv4 address run out
Address span growing more slowly than the table size (address consumption pressures evident?)
  But its picked up again in the first few months of 2012

## Slide 16: IPv6 BGP Prefix Count
2,000
4,000
6,000
Jan
2010
Jan
2011
Jul
2010
Jul
2011
8,000
Jan
2012

## Slide 17: IPv6 BGP Prefix Count
2,000
4,000
6,000
Jan
2010
Jan
2011
Jul
2010
Jul
2011
8,000
Jan
2012
World IPv6 Day

## Slide 18: IPv6 Routed Address Span
Jan
2010
Jan
2011
Jul
2010
Jul
2011
2,000,000/32
10,000,000/32
16,000,000/32
Jan
2012

## Slide 19: IPv6 Routed Address Span
Jan
2010
Jan
2011
Jul
2010
Jul
2011
2,000,000/32
10,000,000/32
16,000,000/32
Jan
2012
Advertising a /8!
Advertising 2400::/12

## Slide 20: IPv6 Routed AS Count
Jan
2010
Jan
2011
Jul
2010
Jul
2011
2,000
3,000
4,000
5,000

## Slide 21: IPv6 Routed AS Count
Jan
2010
Jan
2011
Jul
2010
Jul
2011
2,000
3,000
4,000
5,000
World IPv6 Day

## Slide 22: IPv6 2011 BGP Vital Statistics
Jan-11 Jan-12 p.a. rate
Prefix Count 4,100 7,759 + 89%
Roots 3,178 5,751 + 81%
More Specifics 922 2,008 +118%
Address Span (/32s) 53,415 53,387 + 0%
AS Count 2,966 4,968 + 67%
Transit 556 985 + 77%
Stub 2,343 3,983 + 70%

## Slide 23: IPv6 in 2010 - 2011
Overall IPv6 Internet growth in terms of BGP is 80% - 90 % p.a.
  2009 growth rate was ~ 50%.
(Looking at the AS count, if these relative growth rates persist then the IPv6 network would span the same network domain as IPv4 in 4 years time -- mid/late 2016)

## Slide 24: BGP Size Projections
Generate a projection of the IPv4 routing table using a quadratic (O(2) polynomial) over the historic data
  For IPv4 this is a time of extreme uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of any after-market in IPv4 on the routing table
  which makes this projection even more
  speculative than normal!

## Slide 25: IPv4 Table Size
2004
2008
100,000
300,000
400,000
2006
2010
2012
200,000

## Slide 26: Daily Growth Rates
2004
2008
2006
2010
2012
-50
100
200
0
GFC Mk1
IANA Exhaustion

## Slide 27: Table Growth Model
549 year2 – 2,171,288 year + 2,146,869,663
2004
2008
100,000
300,000
400,000
2006
2010
2012
200,000

## Slide 28: IPv4 Table Projection
2004
100,000
500,000
2008
2012
2016
300,000

## Slide 29: IPv4 BGP Table Size predictions
Jan 2011 347,000 entries
2012 390,000 entries
2013* 424,000 entries
2014* 463,000 entries
2015* 503,000 entries
2016* 545,000 entries
* These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.

## Slide 30: IPv6 Table Size
2007
2,000
6,000
2008
2009
2011
4,000
2010
8,000
2012

## Slide 31: Daily Growth Rates
2007
0
6,000
2008
2009
2011
4,000
2010
2007
0
8
2008
2009
2011
4
2010
12
16
2012

## Slide 32: IPv6 Table Projection
2007
10,000
50,000
2009
2011
2015
40,000
2013
30,000
20,000
430 year2 – 1,729,788 year + 1,736,733,880
e ** (0.469 * year - 934)

## Slide 33: IPv6 BGP Table Size predictions
Jan 2011 4,000 entries
2012 8,000 entries
2013 11,500 entries
2014 16,300 entries
2015 21,800 entries
2016 28,300 entries

## Slide 34: Up and to the Right
Most Internet curves are “up and to the right”
But what makes this curve painful?
  The pain threshold is approximated by Moore’s Law

## Slide 35: Moore’s Law
As a rough rule of thumb, if the rate of growth of the table grows at a rate equal to, or less than Moore’s Law, then the unit cost of storing the forwarding table should remain constant
  Like all rough rules of thumb, there are many potential exceptions, and costs have many inputs as well as the raw cost of the the number of gates in a chip
  Despite this, Moore’s Law still a useful benchmark of a threshold of concern about routing growth

## Slide 37
Moore’s Law
BGP Table Size Prediction
IPv4 BGP Table size and Moore’s Law

## Slide 38: IPv6 Projections and Moore’s Law
Moore’s Law
BGP Table Size Predictions

## Slide 39: eBGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing rapidly, is still relatively small in size in absolute terms
As long as we are prepared to live within the technical constraints of the current routing paradigm it will continue to be viable for some time yet

## Slide 40: BGP Table Growth
However ... continued scalability of the routing system relies on continued conservatism in routing practices.
How good are we at “being conservative” in routing?

## Slide 41: CIDR and BGP
To what extent do we still practice “conservative” routing and refrain from announcing more specifics into the routing table?
Are we getting better or worse at aggregation in routing?
What is the distribution of advertising more specifics? Are we seeing a significant increase in the number of more specific /24s in the routing table?

## Slide 42: An Example:
Prefix AS Path
193.124.0.0/15 4608 1221 4637 3356 20485 2118 ?
193.124.0.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.1.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.2.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.3.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.4.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.5.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.6.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.7.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.8.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.9.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.10.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.11.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.12.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.13.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.14.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.15.0/24 4608 1221 4637 3356 20485 2118 ?
Origin AS: AS 2118 RELCOM-AS OOO "NPO Relcom"

## Slide 43: Who is doing this the most?
www.cidr-report.org
--- 23Dec11 ---
ASnum NetsNow NetsAggr NetGain % Gain Description
Table 388637 227303 161334 41.5% All ASes
AS6389 3473 223 3250 93.6% BELLSOUTH-NET-BLK - BellSouth.net Inc.
AS18566 2093 412 1681 80.3% COVAD - Covad Communications Co.
AS4766 2492 990 1502 60.3% KIXS-AS-KR Korea Telecom
AS7029 2951 1521 1430 48.5% WINDSTREAM - Windstream Communications Inc
AS22773 1515 116 1399 92.3% Cox Communications Inc.
AS4755 1512 201 1311 86.7% TATACOMM-AS TATA Communications
AS4323 1622 387 1235 76.1% TWTC - tw telecom holdings, inc.
AS28573 1557 397 1160 74.5% NET Servicos de Comunicao S.A.
AS10620 1719 641 1078 62.7% Telmex Colombia S.A.
AS1785 1863 787 1076 57.8% AS-PAETEC-NET - PaeTec Communications, Inc.

## Slide 44: BGP Routing Table

## Slide 45: More specifics in the Routing Table
Since 2001 more specifics account for ~50% of the
Routing Table. This has been a relatively constant
Proportion.

## Slide 46: Does everyone see this?
% of entries that are more specific -- as seen by peers of Route Views

## Slide 47: How much address space is announced by more specifics?
% of address space announced by more specifics –
as seen by peers of Route Views

## Slide 48: Does everyone announce more specifics?

## Slide 49: Is it Everyone?
3% of the ASes (1,186 ASes) announce 70% of the more specifics (136,023 announcements)
55% of the ASes announce no more specifics
The top 10 ASes announce 19,163 more specifics

## Slide 50: The Top 10 of More Specifics
AS Aggregates More Specifics
6389 315 3155 BELLSOUTH-NET-BLK - BellSouth.net Inc.
7029 188 2770 WINDSTREAM - Windstream Communications
18566 25 2068 COVAD - Covad Communications Co.
4766 440 2043 KIX-AS-KR - Korea Telecom
1785 132 1731 AS-PAETEC-NET - PaeTec Communications
17974 44 1672 TELKOMNET-AS2-AP PT Telekomunikasi Indonesia
7545 78 1551 TPG-INTERNET-AP TPG Internet Pty Ltd
22773 118 1397 ASN-CXA-ALL-CCI-22773-RDC - Cox Communications
7552 31 1389 VIETEL-AS-AP Vietel Corporation
4755 127 1387 TATACOMM-AS TATA Communications

## Slide 51: Are We Getting Any Better?
Take the daily top 10 Ases over the past 3 years and track the number of more specifics advertised by these Ases over the entire period

## Slide 52: Yes ... and No

## Slide 53: Are We Getting Any Better?
Some ASes are effectively reducing the number of more specifics that are advertised into the global routing system
Some ASes are increasing the number of more specifics
And some are consistently advertising a significant number of more specifics
There is no net change in the overall distribution and characteristics of more specifics in the routing system.

## Slide 54: Why?
The reasons why we see more specifics in the routing system include:
  Different origination (“hole punching” in an aggregate)
  Traffic engineering of incoming traffic flows across multiple inter-AS paths
  “protection” against route hijacking by advertising more specifics
  Poor routing practices

## Slide 55: Types of More Specifics

## Slide 56: Types of More Specifics

## Slide 57: Daily Update Rates
Do more specifics experience a higher update rate than aggregate advertisements?
Lets examine the past 3 years of updates and examine the average daily update per advertised prefix count for aggregates and more specifics

## Slide 58: Daily Update Rates

## Slide 59: Prefix Instability Rates

## Slide 60: Daily Update Rates
Do more specifics experience a higher update rate than aggregate advertisements?
No!
This result is surprising – it was anticipated that more specifics would show a higher level of dynamic instability, particularly
relating to TE more specifics. However nothing is visible in the
data that supports this – advertised “root” prefixes are equally likely to be unstable as advertised more specific prefixes.

## Slide 61: Problem? Not a Problem?
Its evident that the global BGP routing environment suffers from a certain amount of neglect and inattention
Could we do better?
  Yes!
Should we do better?
  It can be difficult to justify the effort and the cost: the current growth rates of the routing table lie within relatively modest parameters of growth and still sit within the broad parameters of constant unit cost of routing technology
  On the other hand, we need to recognize that we could do a lot better in terms of eliminating routing noise, and achieve this with with a relatively modest amount of effort

## Slide 62
Thank You
Questions?