## Slide 1: IPv6
Geoff Huston
APNIC

## Slide 2: Why?

## Slide 3: Because we’ve run out of addresses

## Slide 4: Again.

## Slide 5: We’ve been here before ...
The original ARPAnet design from 1969 used the NCP protocol, which used 8 bit addresses in the NCP packet header
  Maximum network span of 256 nodes
  Enough?
  Well yes, because at the time computers were the size of entire rooms, cost many millions of dollars and there were only a few hundred in the entire world.
  At the time shrinking the computer to something you could hold in one hand and trying to connect billions of them together was just too far into the future to worry about

## Slide 6: ARPAnet IMP

## Slide 7: ARPAnet - September 1978

## Slide 8: Transition V1.0
Turns out that 8 bits of addresses was not enough for the next generation of mini computers
ARPAnet undertook a transition from NCP to a new protocol: TCP/IP
  Expansion from 8 to 32 bit addresses
  Flag Day: 1 January 1983
  Shutdown and reboot every node into the new protocol

## Slide 9: “This time, for sure!” *
* Actually Vint didn’t say this!

## Slide 10: IP Version 4
32 bit address field
  That’s 4,294,967,296 addresses
We’ve used this to build today’s Internet:
  Some 400,000 networks
  Around 1.5 billion connected devices
Some 29 years later, we’ve run out of addresses - again!

## Slide 11: IPv4 Address Allocations

## Slide 12: IPv4 Address Allocations
NSFNET
A&R networks
CIDR
Boom & Bust
GFC
Exhaustion!
Broadband
Mobiles

## Slide 13: IPocalypse?

## Slide 14: So we’ll hit the wall – right?

## Slide 15: Maybe not...
Many ISPs have been stockpiling IPv4 addresses in anticipation of this run out event
In many networks address “recovery” programs are underway
So it’s not a sudden halt to the Internet
But the addressed part of the network grew by more than 250 million services in 2010
  Which was the largest year so far for the Internet

## Slide 16: It’s more like this!

## Slide 17: What are we transitioning to?

## Slide 18: IPv6!

## Slide 19: Layer-3 Protocol Surgery
1
2
3
4
5
Physical
Data Link
IPv4
TCP
UDP
ICMP
Application
Physical
Data Link
IPv6
TCP
UDP
ICMP
Application
Only the IP layer changes – nothing else!
!
Notes: Physical layer and data link layer stay the same: We keep using Ethernet, PPP, etc to carry our packets. Layer-4 protocols like TCP and UDP stay the same too, and applications interact with them in more or less the same way. But they’re carried by a new layer-3 protocol.
That’s all. That’s it. Not hard, is it?

## Slide 20: What changes with IPv6?

## Slide 21: What changes with IPv6?
  128 bit address fields
  Fixed host/network boundary
  Replace Broadcast and ARP with Multicast and SLAAC
  Removed on-the-fly fragmentation with ICMP6 notification to source
  No NATS!
  Multi-Addressing
  Scoped Addresses

## Slide 22: What’s giving us grief?
  128 bit address fields
  Fixed host/network boundary
  Replaced Broadcast and ARP with Multicast and SLAAC
    But we need to retain DHCP for DNS auto-config
  Removed on-the-fly fragmentation with ICMP6 notification to source
  No NATS!
  Multi-Addressing
  Scoped Addresses
  No Backwards Compatibility

## Slide 23: Technology Considerations
For simple LANs it is possible to “just turn it on”
  Although the lack of a NAT can be an issue in terms of shifting from default to explicit security rules in firewalls
For more complex networks IPv6 requires careful engineering
  Particularly around prefix delegation
  And firewall configuration
And the dual stack environment introduces a whole new set of application problems

## Slide 24: Transition, the second time around
A “Flag Day” switchover is impossible
Piecemeal replacement won’t work either as IPv6 is not backward compatible with IPv4
So we need to run both protocols in tandem “for a while”
But bear in mind that one protocol has already run out of addresses
And network growth continues at record levels

## Slide 25: Transition, the second time around
We need to :
deploy IPv6 in parallel with IPv4
deploy ever more stringent IPv4 address conservation measures within the network
allow the network to expand at an ever increasing rate
All at the same time!

## Slide 26: Maybe it’s like this!

## Slide 27: Why is this so hard?

## Slide 28: The IPv6 Transition Plan
IPv6 Deployment
Time
IPv6 Transition – Dual Stack
IPv4 Pool Size
Size of the Internet

## Slide 29: IPv4 Depletion

## Slide 30: A Census of the Network Edge
Counting IPv6 in client devices:
  Some 45% of devices run Windows Vista or Windows 7 - with IPv6 turned on
  Some 8% of devices run Mac OS X - with IPv6 turned on
  Some 35% of devices run Windows XP
About half of the devices out there have IPv6 installed and active
  And a large proportion of the other half are probably running Windows XP
http://en.wikipedia.org/wiki/Usage_share_of_operating_systems

## Slide 31: A Census of the Network Core
4,882 ASNs originate IPv6 prefixes (out of a total of 39,535 ASNs in the IPv4 routing table)
But 33,909 ASNs are stubs and 5,626 ASNs are transit
So 49% of the IPv4 transit ASNs in routing space originate IPv6 prefixes
http://bgp.potaroo.net/v6/as2.0/

## Slide 32: IPv6 capability, as seen by Google
http://www.google.com/intl/en/ipv6/statistics/

## Slide 33
0.0%
0.6%
1.2%
1.8%
Nov
Jan
Mar
Jul
May
Sep
Nov
Jan
IPv6 capability, as seen by APNIC
http://www.potaroo.net/stats/1x1/sitec/
Mar

## Slide 34: Ooops!
Access – 0.5% of end clients are served with an IPv6 access service that provides the client with a native IPv6 unicast address
Services – 0.7% of the Alexa top 1M web sites have AAAA records

## Slide 35: The IPv6 Transition Plan - V2.0
IPv6 Deployment?
2006
IPv6 Transition – Dual Stack
IPv4 Pool Size
Size of the Internet
2008
2010
2012
2014
Date

## Slide 36: What’s gone wrong?
It seems that we’ve managed to achieve only 2 out of 3 objectives for IPv6 deployment
And now the access industry has to deploy (and fund) IPv4 address extension mechanisms in addition to funding an IPv6 deployment
What’s going wrong in this gap between core and edge?
  Why has the access service sector been disinterested in any meaningful levels of IPv6 deployment so far?
  Why is the content industry lagging on IPv6 deployment?

## Slide 37: Lessons from the Past
If this transition to IPv6 is proving challenging, then how did we ever get the IPv4 Internet up and running in the first place?

## Slide 38: IPv4 Deployment Lessons
Technology: packet switching vs circuit switching
  lower network costs though pushing of functionality and cost to end systems exposed a new demand schedule for communications services
i.e. packet switching was far cheaper than circuit switching. This drop in cost exposed new market opportunities for emergent ISPs

## Slide 39: The Demand Schedule
Quantity
Price
q
p
Lower prices increase
Demand, but reduce the
incentive to increase
supply
supply
demand
Higher prices reduce demand, while the higher margins incent higher volumes of supply
Market equilibrium point

## Slide 40: Circuits to Packets: The Demand Schedule Shift
Quantity
Price
q(Circuits)
q(IP)
p(IP)
p(Circuits)
reduced cost of
supply, and increased
perception of value,
resulting in a new
equilibrium point with
higher quantity and
lower unit price
s(IP)
s(C)
d(IP)
d(C)

## Slide 41: IPv4 Deployment
Business: exposed new market opportunity in a market that was actively shedding many regulatory constraints
  exposed new market opportunities via arbitrage of circuits
    buy a circuit, resell it as packets
  presence of agile high-risk entrepreneur capital willing to exploit short term market opportunities exposed through this form of arbitrage
  volume-based suppliers initially unable to redeploy capital and process to meet new demand
    unable to cannibalize existing markets
    unwilling to make high risk investments

## Slide 42: IPv4 Deployment
Time
Size of the Internet
~1990
~2000
High Volume Provider Industry
(Telco Sector)
Small ISP
(Entrepreneur Sector)
~1995

## Slide 43: IPv4 Deployment
Business: exposed new market opportunity in a market that was actively shedding many regulatory constraints
  exposed new market opportunities via arbitrage of circuits
    buy a circuit, resell it as packets
  presence of agile high-risk entrepreneur capital willing to exploit short term market opportunities exposed through this form of arbitrage
  volume-based suppliers initially unable to redeploy capital and process to meet new demand
    unable to cannibalize existing markets
    unwilling to make high risk investments
  the maturing market represented an opportunity for large scale investment that could operate on even lower cost bases through economies of scale

## Slide 44: IPv4 Deployment
Time
Size of the Internet
High Volume Provider Industry
(Telco Sector)
Small ISP
(Entrepreneur Sector)
~1990
~2005

## Slide 45: What about IPv6 Transition?
Will the same technology, cost and regulatory factors that drove the deployment of the IPv4 Internet also drive this industry through the transition from IPv4 to IPv6?

## Slide 46: IPv6 vs IPv4
Are there competitive differentiators?
no cost differential
no functionality differential
no inherent consumer-visible difference
no killer app
no visible consumer demand
no visible competitive differentiators other
than future risk

## Slide 47: IPv4 to Dual Stack: The Demand Schedule Shift
Quantity
Price
QV4
PV4
SV4
SDualStack
DV4 / DualStack
PDualStack
QDualStack
Supply side cost increase due to Dual Stack operation
No change in perception of value, so demand schedule is unaltered
Equilibrium point is at a lower quantity if Dual Stack supply costs are passed on to customers

## Slide 48: The Transition to IPv6
Given that we’ve left it so late in terms of the scale of the transition and the degree of difficultly with IPv4 exhaustion, and given that there appears to be little motivation from some critical industry segments to embark on this transition ...
will it happen at all?

## Slide 49: The Transition to IPv6
Alternatively, is this transition an instance of a market failure?

## Slide 50: “Market Failure”
Wikinomics:
“In economics, a market failure exists when the production or use of goods and services by the market is not efficient. That is, there exists another outcome where market participants' overall gains from the new outcome outweigh their losses (even if some participants lose under the new arrangement). Market failures can be viewed as scenarios where individuals' pursuit of pure self-interest leads to results that are not efficient – that can be improved upon from the societal point-of-view. The first known use of the term by economists was in 1958, but the concept has been traced back to the Victorian philosopher Henry Sidgwick.”
http://en.wikipedia.org/wiki/Market_failure

## Slide 51: The Transition to IPv6
Alternatively, is this transition an instance of a market failure?
Individual self-interest leads to inefficient supply outcomes, as self-interest does not lead the installed based of consumers and suppliers to underwrite the cost of dual stack operation within the transition

## Slide 52: IPv6 Transition as a “Public Good?”
Is the transition to IPv6 is non-excludable and non-rivalrous?
In which case this transition issue parallels that of a public good
With an implication that conventional market dynamics in a deregulated environment will not lead to this transition being undertaken
And a corollary that if this transition is considered to be necessary or essential then some form of public good solution needs to be considered

## Slide 53: Public Good “solutions”
There are a number of conventional approaches to the distribution of a public good:
  Assurance contracts
  Coasian solutions
  Government enterprise provisioning
  Tariffs
  Subsidies
  Taxation remedies
  Regulatory impost

## Slide 54: Regulatory Impost
A regulatory constraint is placed on the ISP carrier licence holders that IPv6 services are to be provided by a given deadline
  as has happened with digital television in many regulatory regimes.
This regulatory constraint acts a form of a assurance contract, where all providers are in effect bound to produce a particular solution

## Slide 55: Government Purchase Contracts
Where the public sector collectively require the provision in IPv6 in all their service contracts.
This is a form of a coasian solution where a group of potential beneficiaries pool together their willingness to pay for the public good.
  We have seen this approach in the past with the Government OSI Profiles (GOSIP) of the late 1980's when the approach proved ineffectual.
  There is no assurance that such collective actions on the part of the public sector have sufficient mass and momentum to create a broader sustainable market that will impel the private sector to undertake the transition.

## Slide 56: Subsidies and Incentives
Where the production of the good is subsidised in some fashion by public funds
  This can be in the form of direct payments to service providers, or in the form of vouchers to consumers which can be redeemed only in exchange for the supply of a specified service.
Related incentive measures include the use of taxation incentives related to infrastructure investment, where the investment in a certain class of infrastructure or in a certain sector can be provided with advantaged taxation treatment.

## Slide 57: Public Provision
Where the service is provided by a publically-owned enterprise.
The funding for such an enterprise can be provided by government-backed investment bonds, or directly from public revenues, and operating losses are underwritten by the public purse.
  This measure was used for most national telephone service providers for a significant part of the twentieth century, so it is not exactly a completely foreign concept for this industry.

## Slide 58: What About IPv4 Exhaustion?
Does IPv4 address exhaustion change this picture?
What are the economic implications of service providers adding CGNs to the current service offering based on IPv4?
Are CGNs and IPv6 mutually exclusive investment options for access providers?

## Slide 59: Adding CGNs to IPv4: The Demand Schedule Shift
Quantity
Price
QV4
PV4
SV4
SCGNs
Supply side cost increase due to Dual Stack operation
CGNs reduce functionality and
impair the performance of some applications
DV4
DCGNs
PCGNs
QCGNs
CGNs represent higher cost and lower value for customers

## Slide 60: But is this all there is to CGNs?
Will CGN’s alter the user’s experience of services?
Does this alter the role (and location) of CDNs?
  Or has the CDN model already evolved to accommodate this evolution?
Do CGNs alter the leverage of the access provider with respect to service deployment?
  Is this an instance of a forced carriage toll gate that allows the carriage sector to renegotiate their relationship with the content access model

## Slide 61: Further musing...
Do we really understand the dynamics and inter-relationships of the components of this industry?
Users
Content
Providers
Data Service
Aggregators
Advertisers
Access Providers
Mobility Providers
Devices
Transit Providers
Carriage
Providers

## Slide 62: Further musing...
What drives the carriage sector?
What drives the content sector?
Who’s winning today?
Is the open network architecture being offered by IPv6 fundamental to the objectives of either of these sectors?
Will the access part of the carriage industry invest in IPv6 infrastructure and service provision?
  If so, then why?
  If not, then why not?

## Slide 63: Your Thoughts?
Carriage vs Content
  Currently advances in IT and the Internet has allowed content to shed carriage mediation and negotiate directly with the end consumer
  Will scarcity in the carriage activity enable carriage players to re-enter the content distribution function in a mediation role and extort toll revenues from content providers?

## Slide 64: Thank You!