## Slide 1: Today’s Mobile Internet
Geoff Huston,
APNIC Labs

## Slide 2
The most profound technologies are those that disappear. They weave themselves into the fabric of everyday life until they are indistinguishable from it...
- Mark Weiser 1991

## Slide 3
So how should we look at mobile devices and the Internet?
Are these merely a temporary consumer fad, destined to be replaced by the next cool technology item?
Or is this an instance of a profound technology change that will bed down to be a part of our everyday life for many years to come?

## Slide 4
To try and answer this, lets try and put this question into some broader context of the evolution the computer and communications enterprise

## Slide 5: The Computing Evolutionary Path
1946 – Eniac – a numeric calculator

## Slide 6: The Computing Evolutionary Path
1964: IBM 360
1964 IBM 360 – commercial computing

## Slide 7
The Computing Evolutionary Path
1984 – Mac - visual personal computing

## Slide 8
The Computing Evolutionary Path
2007 – Apple’s iPhone

## Slide 9
Today’s mobile device is a digital device that has more computing capability than a old mainframe device, with a size of a human hand
It is an Internet-connected device with a general purpose browser and a full set of media capabilities
And they are transforming the Internet!

## Slide 11
With desktop devices the Internet was a destination
lighting
wired bandwidth
large view screens
privacy
dedicated worktop
reliable power

## Slide 12
The Internet is now anywhere and everywhere
Its trivial, commonplace and incidental
radio connectivity
battery power
hand sized
Thumb
operated

## Slide 13: Counting Users...
http://www.itu.int/ITU-D/ict/statistics/
There are 3 billion Internet users today

## Slide 14: Counting Users...
http://www.itu.int/ITU-D/ict/statistics/
There are 2 billion Internet users today
And 7 billion mobile phone users!

## Slide 15: Counting Users...
Source: Generator Research
There are 2 billion Internet users today
And 7 billion mobile phones!
And 2.3 billion mobile Internet users!

## Slide 16: Counting Platforms
http://statcounter.com/
8.5%
4.3%
Mobiles are now
40% of all visible devices

## Slide 17: Mobile Production Numbers
  2014: 1.5 billion units shipped
  Factors:
    Production volumes are bringing down component unit cost
    Android is bringing down software unit cost
    No need for new content - leverage off the the existing web universe of content
    Shift away from the desktop and the laptop by the production industry seeking new markets for their production capability

## Slide 18: Who’s playing
Android
  84% of all smartphone shipments in 2014
  Multi-vendor adoption
  Android also extending into tablets and large screens
Apple iPhone / iPad
  12% of all smartphone shipments in 2014
  Revenues for Apple: $182B in 2014
Windows
  3% market share
  Mostly Lumia models with Nokia

## Slide 19: It’s all about the Money
Source: Generator Research

## Slide 20: Technology for Mobility

## Slide 21: 3G: HSPA
High Speed Packet Access – an evolution of W-CDMA
  Peak data rates 20Mbps downlink, 5.8Mbps Uplink
  Shared channels, shorter Transmission Time Intervals, adaptive use of 16QAM and 64QAM access to increase spectrum efficiency
Mbps – acceptable performance – but nothing special

## Slide 22: 4G: LTE
Theoretical maximum peak speed* 326Mbps
Practical achievable speeds of 4 – 12 Mbps
All IP internal architecture
* Probably assuming the absence of many of the laws of physics as we understand them 
Now it gets interesting!

## Slide 23: 5G:5Gps
5Gbps downloads! *
Yes, that’s 2020!
* In the lab at 15Ghz
  And at that frequency it means that the signal is going to be absorbed by almost anything solid!

## Slide 24: By The Numbers
Lets look at the allocation statistics to examine how mobiles have impacted overall network growth

## Slide 25: IPv4 Allocations

## Slide 26: IPv4 Allocations
Unmet Demand

## Slide 27: IPv6 Allocated Addresses
Chart: 
| 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0
RIPE NCC | 6515 | 1440 | 856 | 883 | 2236 | 2293 | 3857 | 6301 | 8565
ARIN | 53 | 48 | 14489 | 237 | 547 | 6336 | 1663 | 12569 | 5232
APNIC | 3225 | 5236 | 139 | 171 | 1341 | 9493 | 3788 | 4449 | 2663
LACNIC | 12 | 55 | 40 | 89 | 205 | 970 | 4633 | 609 | 1363
AFRINIC | 15 | 13 | 10 | 9 | 101 | 149 | 4196 | 67 | 51
Volume of Allocated IPv6 Addresses (using units of /32s) per year

## Slide 28: IPv6 Allocated Addresses
Chart: 
| 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0
RIPE NCC | 6515 | 1440 | 856 | 883 | 2236 | 2293 | 3857 | 6301 | 8565
ARIN | 53 | 48 | 14489 | 237 | 547 | 6336 | 1663 | 12569 | 5232
APNIC | 3225 | 5236 | 139 | 171 | 1341 | 9493 | 3788 | 4449 | 2663
LACNIC | 12 | 55 | 40 | 89 | 205 | 970 | 4633 | 609 | 1363
AFRINIC | 15 | 13 | 10 | 9 | 101 | 149 | 4196 | 67 | 51
Volume of Allocated IPv6 Addresses (using units of /32s) per year
These allocation volumes are small compared to the unmet demand pressures in IPv4 – currently network operators are unable to use Ipv6 as a substitute for IPv4 and instead have to resort to Ipv4 address sharing to meet network address demands

## Slide 29: Where are we headed?

## Slide 30: Where are we headed?
Up until 2013 mobile Internet had been constructed exclusively using IPv4 infrastructure
Today’s mobile internet continues to grow by extensive use of NATs in the operator’s network
This cannot continue indefinitely

## Slide 31: The Mobile Transition
The mobile industry is very heterogeneous
  Various spectrum allocations and regulatory constraints
  Various service objectives
  Various operator business objectives (incumbent vs challenger)
  Different objectives from handset suppliers vs network operators
The approach to IPv6 transition is highly fragmented across the operators
The result is the deployment of various permutations of transitional IPv4 and IPv6 support in the mobile environment:
  Native mode dual stack over LTE: e.g. Verizon
  IPv4 layered over native IPv6, 464 XLAT: e.g. T-Mobile
  IPv6 tunelled over IPv4

## Slide 32: The Mobile Transition
The mobile industry is very heterogeneous
  Various spectrum allocations and regulatory constraints
  Various service objectives
  Various operator business objectives (incumbent vs challenger)
  Different objectives from handset suppliers vs network operators
The approach to IPv4 exhaustion and transition is highly fragmented
The result is the deployment of various permutations of transitional IPv4 and IPv6 support in the mobile environment:
  Native mode dual stack over LTE: e.g. Verizon
  IPv4 layered over native IPv6, 464 XLAT: e.g. T-Mobile
  IPv6 tunelled over IPv4
This diversity implies that many operators have unique requirements for network and device capabilities
Which implies the imposition of cost and complexity for the service operators through customization of technologies
Which all adds to the cost of service to consumers
Nobody wins from this fragmented transition scenario!

## Slide 33: It’s not just Transitional Complexities
It’s also Spectrum issues:
  The traditional mobile providers operate with exclusive access to spectrum within defined locales (with associated license costs)
  Alternate access competitors can operate in unlicensed spectrum with WiFi network services
  Handsets are also entering the space with platform services that support connection agility across diverse access networks
  Mobile incumbents are being forced to chase this alternate access market or risk losing market share

## Slide 34: Where now for Mobiles?
Mobile Operators are being pushed into undistinguished utility roles
  No more voice premiums
  Erosive pressure on data service margins
Consumers want more for less
  Higher download speeds
  Larger data caps
  Lower premiums
Exclusive Use spectrum is too expensive
  Are they pricing themselves out of the consumer market?
  WiFi access and application handover approaches are placing pressure on the traditional mobile operator’s margins
The underlying problem here is that the mobile network operator has lost control of the access device
  And there is no way back!
  The device vendor and its applications are charting a course that is in direct conflict with the mobile network operator’s desires, and managing to monetize this far more efficiently than the mobile network operator

## Slide 35: Thank You!
Questions?