## Slide 1: IPv6 Performance
Geoff Huston
APNIC Labs
February 2015

## Slide 2: What are we looking at:
How “reliable” are IPv6 connections?
How “fast” are IPv6 connections?

## Slide 3: What are we looking at:
How “reliable” are IPv6 connections?
How “fast” are IPv6 connections?
Do all TCP connection attempts succeed?
Is V6 slower than V4?

## Slide 4: The Measurement Technique
Embed a script in an online ad
Have the script generate a set of URLs to fetch
Examine the packets seen at the server to determine reliability and RTT

## Slide 5: Measurement Count

## Slide 6: Measurement Count
Yes, that’s 12 M measurements per day!

## Slide 7: Measurement Count
Log Count

## Slide 8: What are we looking at:
How “reliable” are IPv6 connections?
How “fast” are IPv6 connections?
Do all TCP connection attempts succeed?
Is V6 slower than V4?

## Slide 9: Let’s dive into Naked SINs!
Y

## Slide 10: Connection Failure
Outbound SYN
Busted SYN ACK
Return path
What the server sees is an incoming SYN, but no matching incoming ACK
server
client

## Slide 11: Compare two data sets
The first data set has been collected across 2011
  Teredo and 6to4 were still active as IPv6 mechanisms
  Little in the way of other IPv6 services
The second data set has been collected across 2015/2016
  Missing comparative IPv4 data for the period September – October 

## Slide 12: 2011 - Measuring Failure

## Slide 13: 2011 - Relative Connection Failure Rates
Why is this failure rate for V6
so incredibly high?

## Slide 14: 2011 - Relative Connection Failure Rates
And why is the V4 relative failure rate dropping over time?
What is this spike?

## Slide 15: What is going on with IPv4?

## Slide 16: What is going on with IPv4?
The failure rate for V4 decreases as the volume of experiments increases – which implies that the number of “naked SYNs” being sent to the servers is not related to the number of tests being performed.
Aside from residual IPv4 failures in the image fetch due to device resets, connection dropouts, etc, the bulk of the recorded failures here is probably attributable to bots doing all-of-address scanning on port 80 – or maybe not!

## Slide 17: What is going on with IPv4?
Syn attacks?

## Slide 18: What about IPv6?
Local Miredo Relay Failures
Why is the base failure rate
of all IPv6 connections sitting
at 40%? This is amazingly bad!

## Slide 19: V6 Failure Rate by Address Type
All V6 Average
Teredo
6 to 4
Unicast

## Slide 20: 6to4 Failure is Local Failure
6to4 failure appears to be related to two factors:
  The client’s site has a protocol 41 firewall filter rule for incoming traffic (this is possibly more prevalent in AsiaPac than in Europe)
  Load / delay / reliability issues in the server’s chosen outbound 6to4 relay (noted in the data gathered at the US server)
Even so, the 10% to 20% connection failure rate for 6to4 is unacceptably high!

## Slide 21: V6 Unicast Failures
January – March 2012:
  110,761 successful V6 connecting endpoints
  6,227 failures
  That’s a failure rate of 5.3%!
  7 clients used fe80:: link local addresses
  7 clients used fc00:/7 ULA source addresses
  2 clients used fec0::/16 deprecated site local addresses
  16 clients used 1f02:d9fc::/16
  Nobody used 3ffe::/16 prefixes!

## Slide 22: Data Set 2: Connection Failure in 2015/2016
January 2015– January 2016
40,359,805 IPv6 endpoints
1,361,256 Failure rate (3.37%)

## Slide 23: Daily IPv6 Failures

## Slide 24: Daily IPv6 Failures
RIP
Flash!
HTML5 + TLS +
Mobile Devices

## Slide 25: 6to4
7,693,849 6to4 endpoints
  19% of all IPv6 used 6to4
  9% failure rate within the set of 6to4 connections
This is still very high!

## Slide 26: Daily IPv6 Failures

## Slide 27: Daily IPv6 Failures
6to4 failure rate has improved from 15%-20% in 2011 to 9% in 2015
Teredo has all but disappeared
Unicast failure rate is between 1.5% and 4% in 2015
  Current unicast failure rate is 2%

## Slide 28: Killing off 6to4
Proportion of IPv6 connections using a 6to4 address

## Slide 29: IPv6 Failures – Sep 2015 – Jan 2016
20,872,173 unique IPv6 Addresses
464,344 failing IPv6 addresses
142,362 6to4 addresses
138 teredo addresses
68 fe80:: local scope addresses
834 unallocated addresses
1,244 unannounced addresses
319,698 addresses from unicast allocated routed space
216,620 unique /64s

## Slide 30: Origin AS’s with High IPv6 Failure Rates

## Slide 31: Origin AS’s with Zero Failure Rates
Ranked by IPv6 measurement count

## Slide 32: What about IPv4 Connection Failures?
2011: failure rate 0.2%

## Slide 33: What about IPv4 Connection Failures?
2011: failure rate 0.2%
2015:
446,414,857 IPv4 endpoints
1,166,332Connection Failures (0.26%)

## Slide 34: IPv4 Connection Failure
Missing PCAP data

## Slide 35: Comparison

## Slide 36: Comparison: Unicast

## Slide 37: Comparison: Unicast

## Slide 38: Comparison Ratio: Unicast

## Slide 39: It’s still not good!
IPv6 Unicast Failure rate: 1.6% (falling)
IPv4 Failure rate: 0.2% (steady)

## Slide 40: What are we looking at:
How “reliable” are IPv6 connections?
How “fast” are IPv6 connections?
Do all TCP connection attempts succeed?
Is V6 slower than V4?

## Slide 41: Why SYNs?
Every TCP session starts with a SYN handshake
It’s typically a kernel level operation, which means that there is little in the way of application level interaction with the SYN exchange
On the downside there is only a single sample point per measurement

## Slide 42: Generating a comparative RTT profile
For each successful connection couplet (IPv4 and IPv4) from the same endpoint, gather the pair of RTT measurements from the SYN-ACK exchanges
  Use the server’s web logs to associate a couplet of IPv4 and IPv6 addresses
  Use the packet dumps to collect RTT information from the SYN-ACK Exchange
  Plot the difference in RTT in buckets

## Slide 43
2012 Data

## Slide 44
IPv6 is slower
IPv6 is faster
RTT Difference (in fractions of a second)
Number of samples (log scale)
Teredo
6 to 4
Unicast
2012 Data

## Slide 45
IPv6 is slower
IPv6 is faster
RTT Difference
Number of samples (log scale)
Unicast
December 2015/January 2016

## Slide 46
IPv6 is slower
IPv6 is faster
RTT Difference
Number of samples (log scale)
6to4
December 2015/January 2016

## Slide 47
IPv6 is slower
IPv6 is faster
RTT Difference
Number of samples (log scale)
December 2015/January 2016

## Slide 48
IPv6 is slower
IPv6 is faster
RTT Difference (millisecs)
Proportion of samples
2015/6 RTT Data CDF
6 to 4
Unicast

## Slide 49
IPv6 is slower
IPv6 is faster
RTT Difference (milliseconds)
Proportion of samples
6 to 4
Unicast
2015/6 RTT Data CDF

## Slide 50
IPv6 is slower
IPv6 is faster
RTT Difference (milliseconds)
Proportion of samples
6 to 4
Unicast
2015/6 RTT Data CDF
Zero point is 0.44
13% of samples unicast IPv6 is more than 10 msec faster than IPv4
32% of samples unicast IPv6 is more than 10 msec slower than IPv4

## Slide 51: Is IPv6 as “good” as IPv4?

## Slide 52: Is IPv6 as “good” as IPv4?
Is IPv6 as fast as IPv4?
  Basically, yes
  IPv6 is faster about half of the time
  For 65% of unicast cases, IPv6 is within 10ms RTT of IPv4
  So they perform at much the same rate
  But that’s just for unicast IPv6
  The use of 6to4 makes this a whole lot worse!

## Slide 53: Is IPv6 as “good” as IPv4?
Is IPv6 as robust as IPv4?
  IPv4 connection reliability currently sits at 0.2%
  The base failure rate of Unicast V6 connection attempts at 1.8% of the total V6 unicast connections is not brilliant.
  6to4 is still terrible!
  It could be better.
  It could be a whole lot better!

## Slide 54: Is IPv6 as “good” as IPv4?
If you can establish a connection, then IPv4 and IPv6 appear to have comparable RTT measurements across most of the Internet
But the odds of establishing that connection are still weighted in favour of IPv4!

## Slide 55: That’s it!
Questions?