## Slide 1: Large (UDP) Packets in IPv6
Geoff Huston
APNIC

## Slide 2: What’s the problem?

## Slide 3: What’s the problem?
IEPG presentation – November 2013

## Slide 4: So what?

## Slide 5: Packet Networks like variable packet sizes
The range of packet sizes supported in a network represents a set of engineering trade-offs:
  Bit error rate of the underlying media
  Desired carriage efficiency
  Transmission speed vs packet switching speed

## Slide 6: IPv4 Packet Design
FORWARD fragmentation
  If a router cannot forward a packet on its next hop due to a packet size mismatch then it is permitted to fragment the packet, preserving the original IP header in each of the fragments

## Slide 7: IPv4 and the “Don’t Fragment” bit
If Fragmentation is not permitted by the source, then the router discards the packet. The router may send an ICMP to the packet source with an Unreacahble code (Type 3, Code 4)
Later IPv4 implementations added a MTU size to this ICMP message
BUT: ICMP messages are extensively filtered in the Internet so applications should not count on receiving these messages!

## Slide 8: Trouble at the Packet Mill
Lost frags require a resend of the entire packet – this is far less efficient than repairing a lost packet
Fragments represent a security vulnerability as they are easily spoofed
Fragments represent a problem to firewalls – without the transport headers it is unclear whether frags should be admitted or denied
Packet reassembly consumes resources at the destination

## Slide 9: The thinking at the time…
Fragmentation was a Bad Idea!
Kent, C. and J. Mogul, "Fragmentation Considered Harmful", Proc. SIGCOMM '87 Workshop on Frontiers in Computer Communications Technology, August 1987

## Slide 10: IPv6 Packet Design
Attempt to repair the problem by effectively jamming the DON’T FRAGMENT bit to always ON
IPv6 uses BACKWARD signalling
  When a packet is too big for the next hop a router should send an ICMP6 TYPE 2 (Packet Too Big) message to the source address and include the MTU of the next hop.

## Slide 11: IPv6 Source Fragmentation

## Slide 12: What changed? What’s the same?
Both protocols may fragment a packet at the source
Both protocols support a Packet Too Big signal from the interior of the network to the source
Only IPv4 routers may generate fragments on-the-fly
IPv6 relies on support for Extension Headers to support its implementation of IP packet fragmentation
  But that has its own set of implications (See slide 3)!

## Slide 13: What does “Packet Too Big” mean anyway?
errrrr

## Slide 14: It’s a Layering Problem
Fragmentation was seen as an IP level problem
  It was meant to be agnostic with respect to the upper level (transport) protocol
But we don’t treat it like that
  And we expect different transport protocols to react to fragmentation notification in different ways

## Slide 15: What does “Packet Too Big” mean anyway?
For TCP it means that the active session referred to in the ICMP payload* should drop its session MSS to match the MTU **
  In an ideal network you should never see IPv6 fragments in TCP!
    * assuming that the payload contains the original end-to-end IP header
    ** assuming that the ICMP is genuine

## Slide 16: What does “Packet Too Big” mean anyway?
For UDP its not clear:
  The offending packet has gone away!
  Some IP implementations appear to ignore it
  Others add a host entry to the local IP Forwarding table that records the MTU
  Others perform a rudimentary form of MTU reduction in a local MTU cache

## Slide 17: Problems
ICMP is readily spoofed
  ICMP messages can consume host resources
  An attacker may spoof a high volume stream of ICMP PTB messages with random IPv6 source addresses
  An attacker may spoof ICMP PTB messages with very low MTU values

## Slide 18: Problems
ICMP is widely filtered
  leading to black holes in TCP sessions
    GET is a small HTTP packet
    The response can be arbitrarily large, and if there is a path MTU mismatch the response can wedge
Get
Response

## Slide 19: Problems
Leading to ambiguity in UDP
  Is this lack of a response due to network congestion, routing & addressing issues, or MTU mismatch?
  Should the receiver just give up, resend the trigger query, or revert to TCP? (assuming that it can)

## Slide 20: What did IPv6 do differently?
IPv6 defined a minimum unfragmented packet size of 1,280 bytes:
IPv6 Specification: RFC2460

## Slide 21: What did IPv6 do differently?
IPv6 defined a minimum unfragmented packet size of 1,280 bytes:
IPv6 Specification: RFC2460
I’ve been told that 1280 is 1024 + 256!
Which seems like a pretty specious line of reasoning to me!
It represented a compromise about non-reassembling tunneling and has resulted in a fractured IPv6 network.
1500 would’ve been a more robust outcome in my view.

## Slide 22: Bewteen 1280 and 1500
What should an IPv6 host use as a local MTU value?
  If you set it at 1280 then you invite fragmentation if you need to send larger packets, which will risk EH loss on fragmented packets
  If you set it at 1500 then you may encounter risks with MTU mismatch and PTB notification loss when talking with a host with a smaller MTU and encounter MTU Black Holes
1280
1500

## Slide 23: Lets look
So if the issue is the combination of IPv6, UDP and larger packets then perhaps we can experiment with this
  It’s called “the DNS” !
So we set up an experiment…
  Response 1 : 131 octets
  Response 2: 1400 octets
  Response 3: 1700 octets
  And set up a name server reachable only on IPv6 and only on UDP

## Slide 24: What we expect to see
Size Fetched Failed Reason
Small (150 octets) 99% 1% Noise
1160 octets 99% 1% Noise
1400 octets ? ? PTB
1700 octets <52% >48% EH Loss,
Frag loss,
PTB

## Slide 25: What we saw
Tested Always Fetched Both Always Missed
150 11,719 8,792 (75.02%) 377 (3.22%) 2,550 (21.76%)
1,160 2,004 1,353 (67.51%) 5 (0.25%) 646 (32.24%)
1,400 9,789 7,374 (75.33%) 385 (3.93%) 2,030 (20.74%)
1,425 1,977 1,313 (66.41%) 7 (0.35%) 657 (33.23%)
1,453 1,987 1,298 (65.32%) 9 (0.45%) 680 (34.22%)
1,700 11,170 5,859 (52.45%) 172 (1.54%) 5,139 (46.01%)
1280
1500

## Slide 26: What we saw
Tested Always Fetched Both Always Missed
150 11,719 8,792 (75.02%) 377 (3.22%) 2,550 (21.76%)
1,160 2,004 1,353 (67.51%) 5 (0.25%) 646 (32.24%)
1,400 9,789 7,374 (75.33%) 385 (3.93%) 2,030 (20.74%)
1,425 1,977 1,313 (66.41%) 7 (0.35%) 657 (33.23%)
1,453 1,987 1,298 (65.32%) 9 (0.45%) 680 (34.22%)
1,700 11,170 5,859 (52.45%) 172 (1.54%) 5,139 (46.01%)
??
1280
1500
There is quite some noise in this data – the small-size response shows a 21%
loss rate, which is likely to be due to a combination of:
DNS multi-slave query engine farms
IPv6 Link Layer address manipulation
ICMPv6 Address unreachable
DNS timeouts

## Slide 27: Unreachables
Dual Stack configurations hide a multitude of sins
And one of these is the use of unreachable IPv6 addresses for DNS resolvers
  11,077 distinct unreachable IPv6 addresses !
  Out of 22,000 distinct IPv6 /128 addresses
    Which is not quite as bad as it looks – a number of resolvers are “aggressive” in their use of /64 interface identifiers

## Slide 28: Filtering the results
Join individual resolver /128 addresses into common /64’s
Only look at resolver /64’s that fetch either of the two low-size controls
  Which means that the IPv6 address is reachable
  And the resolver will successfully resolve a glueless delegation

## Slide 29: What we saw:
Size Tested Always Fetched Both Always Missed
150 5,433 5,290 (97%) 143 (3%) 0
1,160 654 651 (99%) 3 (1%) 0
1400 4,658 4,495 (96%) 133 (3%) 30 (1%)
1425 636 619 (97%) 5 (1%) 12 (2%)
1453 638 609 (95%) 6 (1%) 23 (4%)
1700 4,686 3,464 (74%) 79 (1%) 1,143 (25%)
1280
1500

## Slide 30: What we saw:
Size Tested Always Fetched Both Always Missed
150 5,433 5,290 (97%) 143 (3%) 0
1,160 654 651 (99%) 3 (1%) 0
1400 4,658 4,495 (96%) 133 (3%) 30 (1%)
1425 636 619 (97%) 5 (1%) 12 (2%)
1453 638 609 (95%) 6 (1%) 23 (4%)
1700 4,686 3,464 (74%) 79 (1%) 1,143 (25%)
1280
1500
Between 1280 and 1500 the failure rate rises as the packet size rises.

## Slide 31: PTB MTU size distribution
1280
1500
1480
1460
1492

## Slide 32: What we saw:
Size Tested Always Fetched Both Always Missed
150 5,433 5,290 (97%) 143 (3%) 0
1,160 654 651 (99%) 3 (1%) 0
1400 4,658 4,495 (96%) 133 (3%) 30 (1%)
1425 636 619 (97%) 5 (1%) 12 (2%)
1453 638 609 (95%) 6 (1%) 23 (4%)
1700 4,686 3,464 (74%) 79 (1%) 1,143 (25%)
1280
1500
There is a visible signal here for packets > 1500 octets.
It is not a 48% drop rate, but it is certainly more than 20% over and above the other packet sizes. There is a definite problem here with large IPv6 packets.

## Slide 33: EH drop? Or something more mundane?
1,143 IPv6 /64s consistently cannot fetch a 1,700 octet UDP response
  331 /64’s generated ICMP Fragmentation reassembly ICMP messages
    Firewall front end discarding trailing fragments
  61 /64’s generated Packet Too Big messages
  751 failing /64’s generated no ICMP messages
    i.e. EH packet drop was a maximum of 16% in this experiment

## Slide 34: What we saw with a 1280 MTU:
Size Tested Always Fetched Both Always Missed
150 4,777 4,600 (96%) 177 (4%) 0
1400 4,662 3,695 (79%) 80 (2%) 887 (19%)
1700 4,635 3,429 (74%) 95 (2%) 1,111 (24%)
1280
1500
Dropping the local MTU pushes a further 18% fragmentation drop into the 1,400 Byte packet

## Slide 35: What are we seeing?
Whether its EH drop of frag filtering, there is something deeply concerning in these numbers:
  A protocol that suffers a ~20% packet drop rate on fragmented packets presents a problem!
  Hosts should use the largest locally supported MTU for UDP (and use a 1,220 MSS for TCP)
  Applications should assume that large IPv6 fragmented packets may silently die in transit. They should be prepared to perform a rapid cutover to TCP in the event of suspected packet loss in UDP
  Should we revive draft-bonica-6man-frag-deprecate?

## Slide 36: Thanks!