## Slide 1: Desperately Seeking Default
Geoff Huston
APNIC

## Slide 2: In the Telephone Network
All telephones were equally reachable
Anyone could dial anyone else

## Slide 3: In the Telephone Network
Are all connected endpoints equally reachable?
Can anyone can reach anyone else?
Internet

## Slide 4: In the Telephone Network
Are all connected endpoints are equally reachable?
Can anyone can reach anyone else?
Internet
NATs and Firewall Filters changed all that – so our current expectations are that if you stand up a public service on port 80 (or 443 for that matter) then maybe everyone can reach you, but otherwise, no.
No!

## Slide 5: In the Telephone Network
All connected endpoints are equally reachable
Can anyone can reach anyone else?
Internet

## Slide 6: In the Telephone Network
All connected endpoints are equally reachable
Anyone can reach anyone else
Internet
We might THINK this, but is it true ALL the time?

## Slide 7: What do we see?
On the Internet is everyone really connected to everyone else?

## Slide 8: How We See
We use an online ad to present a sequence of small fetches to the user’s browser

## Slide 9: How We See
The sequence of tests is used to test a number of types of actions including fetches of IPv4,
IPv6 and Dual stack

## Slide 10: How We See
We use tcpdump to record all packet activity at the experiment’s servers

## Slide 11: How Much do We See?

## Slide 12: What we see: Connection Failure
Outbound SYN
Busted SYN ACK
Return path
What the server sees is an incoming SYN, but no matching incoming ACK
server
client

## Slide 13: Daily IPv6 Failures
RIP
Flash!
HTML5 + TLS +
Mobile Devices

## Slide 14: Daily IPv6 Failures

## Slide 15: Daily IPv6 Failures

## Slide 16: IPv6 Failures
1.5% failure for unicast V6 is unacceptable!
Why is this happening
  Auto-tunnelling?
  Lousy CPE firmware?
  Strange firewall filters?
But is all of this due to local configuration / equipment? What is the comparable view in IPv4?

## Slide 17: IPv4 Connection Failure
Missing PCAP data

## Slide 18: IPv4 Failures
IPv4 failures are around 1 in 500
And we are pretty sure its NOT:
  Auto-tunnelling
  Lousy CPE firmware
  Strange firewall filters
So what is the reason for this residual asymmetric failure rate?
Is it asymmetric routing connectivity?

## Slide 19: Route Views Routing Table

## Slide 20
25 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route Views

## Slide 21: 2015/16, Route Views + RIS
This is a view pulled together from each of the routing peers of Route Views and RIS
That’s a
range of 75,000
routes!

## Slide 22: Different peers see a slightly different Internet
But is this just traffic engineering more specifics?
Or do different peers see a different set of reachable addresses in the routing table?

## Slide 23: Address Span (Route Views + RIS data sets)

## Slide 24: Address Span (Route Views + RIS data sets)
15 M Addresses

## Slide 25: What does this mean?
Each peer of RouteViews and RIS announces a span of addresses that appears to be a unique span.
In total, these spans agree with other to within ~20M addresses, but this means that there are potentially some 20M uniquely addressed endpoints that cannot be reached from all other endpoints.
This variation is stable over time for each peer, so its not transient routing that is generating this – the reasons for this difference in reachability are structural

## Slide 26: What about IPv6?

## Slide 27: The Route Views view of IPv6
World IPv6 Day
IANA IPv4 Exhaustion

## Slide 28: Number of IPv6 Routes in 2015/16
That’s a
range of 2,300
routes!

## Slide 29: IPv6 Announced Address Span Variation (RV + RIS)

## Slide 30: IPv6 Announced Address Span Variation (RV + RIS)

## Slide 31: What is “default”?
There is no “default” route set that we can all agree on

## Slide 32: What is “default”?
At best “default” is an informal quorum
  So lets define this quorum by arbitrarily setting the quorum threshold at 2/3
  i.e. if 2/3 of the peers of a route collector advertise a route then it is part of the default quorum.
Individual peer networks will contain route sets that differ from this quorum by having both additional prefixes and holes.
  Lets look at the variance from the quorum

## Slide 33: A “Quorum” deviation view of IPv4

## Slide 34: A magnified view

## Slide 35: IPv6 “Quorum” Deviation

## Slide 36: Zooming In

## Slide 37: And Again

## Slide 38: And Again!

## Slide 39: Quorum Deviation for RVA IPv4 Peers (18th August 2016)

## Slide 40: Quorum Deviation for RIS IPv4 Peers 18th August 2016)

## Slide 41: Quorum Deviation: IPv6, RVA

## Slide 42: Quorum Deviation: IPv6, RIS

## Slide 43: It’s structural, not temporal
There is a visible stability to this deviation from the quorum route set
  The variation from the quorum is long–term stable, and does not rapidly self-correct – its not a transient routing state
We appear to assume that all Tier 1 providers, and their Tier 2, 3, … resellers offer the same reachability set as each other – i.e. ”default” is consistent everywhere
But this is not necessarily the case all the time for every address in the routing system
“Default” appears to vary by provider and by location
  E.g.: 25 April, 1600 UTC:
    AS2914: RouteViews 2,808,560,896 addresses
    RIS: 2,807,358,208

## Slide 44: So What?
Surely all this is patched up by the widespread use of default in addition to specific routes? (*)
* Internet Optometry: Assessing the Broken Glasses in Internet Reachability”,
R. Bush, O. Maennel, M. Roughan, S Uhlig, ACM SIGCOMM IMC, 2009

## Slide 45: So What?
Surely all this is patched up by the widespread use of default in addition to specific routes?
  Well, not really
  Default points along upstream transits
  It does not patch downstreams
A
B
Route to B not propagated on this connection
Packet from B to A follows explicit route
Packet from B to A follows default and then
dropped

## Slide 46: To Recap: What is causing this?

## Slide 47: To Recap: What is causing this?
Could part of this be due to connectivity failure?

## Slide 48: Connection Failure
Outbound SYN
server
client

## Slide 49: Connection Failure
Outbound SYN
SYN ACK
Return path
server
client

## Slide 50: Connection Failure
Outbound SYN
Busted SYN ACK
Return path
server
client
router

## Slide 51: Connection Failure
Outbound SYN
Busted SYN ACK
Return path
server
client
router
ICMP Dest Unreachable

## Slide 52: Connection Failure
Outbound SYN
Busted SYN ACK
Return path
What the server sees is an incoming SYN, and then an ICMP destination unreachable
server
client
router
ICMP Dest Unreachable

## Slide 53: And we see this … here’s an example
14:16:05.999497 IP (tos 0x0, ttl 55, id 31005, offset 0, flags [none], proto ICMP (1), length 80)
84.41.108.74 > 139.162.146.97: ICMP host 46.163.63.47 unreachable, length 60
Outer packet is an ICMP Packet with a “destination unreachable” code sent to the server from the router at address 84.41.108.74
IP (tos 0x0, ttl 57, id 0, offset 0, flags [DF], proto TCP (6), length 52)
139.162.146.97.443 > 46.163.63.xx.52087: Flags [S.], cksum 0x5130 (correct), seq 3917125220, ack 685287936, win 29200, options [mss 1460,nop,nop,sackOK,nop,wscale 7], length 0
Payload packet is a SYN+ACK packet

## Slide 54: Connection Failure
Outbound SYN
Busted SYN ACK
Return path
What the server sees is an incoming SYN, and then an ICMP destination unreachable
server
client
router
ICMP Dest Unreachable
But this is not a reliable signal – routers do not always generate an ICMP Dest Unreachable, and firewalls often filter them. But they are still visible some of the time.

## Slide 55: Of course it’s not the only reason why connections fail in IPv4
NATs are also erratic:
14:16:37.959604 IP (tos 0x38, ttl 55, id 40091, offset 0, flags [none], proto ICMP (1), length 80)
197.114.50.xx > 139.162.146.97: ICMP host 197.114.50.20 unreachable, length 60
IP (tos 0x20, ttl 49, id 0, offset 0, flags [DF], proto TCP (6), length 52)
139.162.146.97.443 > 197.114.50.xx.55648: Flags [S.], cksum 0xeb1e (correct), seq 3454637726, ack 3599361621, win 29200, options [mss 1400,nop,nop,sackOK,nop,wscale 7], length 0
Why is the destination telling us that it is unreachable?

## Slide 56: Of course it’s not the only reason why connections fail in IPv4
NATs are also erratic:
14:16:37.959604 IP (tos 0x38, ttl 55, id 40091, offset 0, flags [none], proto ICMP (1), length 80)
197.114.50.xx > 139.162.146.97: ICMP host 197.114.50.20 unreachable, length 60
IP (tos 0x20, ttl 49, id 0, offset 0, flags [DF], proto TCP (6), length 52)
139.162.146.97.443 > 197.114.50.xx.55648: Flags [S.], cksum 0xeb1e (correct), seq 3454637726, ack 3599361621, win 29200, options [mss 1400,nop,nop,sackOK,nop,wscale 7], length 0
Why is the destination telling us that it is unreachable?
It’s probably a CGN that has lost its binding state while the TCP session was being established!

## Slide 57: Connectivity appears to have a 1 in 500 failure rate in IPv4
Some of it is based on asymmetric views of connectivity from the routing system
Some of it is based on anomalous NAT behaviours
And some of it … we just can’t tell!

## Slide 58: In the Telephone Network
All connected endpoints are equally reachable
Anyone can reach anyone else
Internet
Almost
almost
most of the time!

## Slide 59: In the Telephone Network
All connected endpoints are equally reachable
Anyone can reach anyone else
Internet
Almost
almost
most of the time!
As long as all the feeder access networks can connect to Facebook, Google, Netflix, Ebay, Amazon,… then nobody seems to care enough any more to be motivated to fix it
What we now have in 2016 is a tier 1 feeder system, as it’s no longer a true uniquitous fully connected peer network
And that makes me sad!

## Slide 60: Thanks!