## Slide 1: Routing and Addressing in 2017
Geoff Huston
Chief Scientist, APNIC

## Slide 2: Through the Routing Lens …
There are very few ways to assemble a single view of the entire Internet
The lens of routing is one of the ways in which information relating to the entire reachable Internet is bought together
Even so, its not a perfect lens…

## Slide 3
1994: Introduction of CIDR
2001: The Great Internet Boom and Bust
2005: Consumer Market
2011: Address Exhaustion
24 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route-Views

## Slide 4: 2016-2017 in detail

## Slide 5: 2016-2017 in detail
average growth trend
Route Views Peers
RIS Peers

## Slide 6: Routing Indicators for IPv4
Routing prefixes – growing by some 53,000 prefixes per year
AS Numbers– growing by some 3,400 prefixes per year

## Slide 7: Routing Indicators for IPv4
More Specifics are still taking up slightly more than one half of the routing table
But the average size of a routing advertisement continues to shrink

## Slide 8: Routing Indicators for IPv4
Address Exhaustion is now visible in the extent of advertised address space
The “shape” of inter-AS interconnection appears to be relatively steady

## Slide 9: AS Adjacencies (Route-Views)
6,934 AS6939 HURRICANE - Hurricane Electric, Inc., US
5,301 AS174 COGENT-174 - Cogent Communications, US
5,037 AS3356 LEVEL3 - Level 3 Communications, Inc., US
2,467 AS3549 LVLT-3549 - Level 3 Communications, Inc., US
2,388 AS7018 ATT-INTERNET4 - AT&T Services, Inc., US
2,068 AS209 OBIT-AS "OBIT" Ltd., RU
2,056 AS57463 NETIX , BG
1,997 AS209 CENTURYLINK, US
1,776 AS37100 SEACOM-AS, MU
1,755 AS6461 ZAYO Bandwidth, US
43,368 out of 60,493 ASNs have 1 or 2 AS Adjacencies (72%)
3,543 ASNs have 10 or more adjacencies
20 ASNs have >1,000 adjacencies
Most networks are stub AS’s
A small number of major connectors

## Slide 10: What happened in 2017 in V4?
Routing Business as usual – despite IPv4 address exhaustion!
  From the look of the growth plots, its business as usual, despite the increasing pressures on IPv4 address availability
  The number of entries in the IPv4 default-free zone reached 700,000 by the end of 2018
  The pace of growth of the routing table is still relatively constant at ~53,000 new entries and 3,400 new AS’s per year
    IPv4 address exhaustion is not changing this!
    Instead, we are advertising shorter prefixes into the routing system

## Slide 11: What about IPv4 Address Exhaustion?
ARIN – no free pool left
AFRINIC – June 2019
LACNIC – September 2019
RIPE NCC – September 2020
APNIC – February 2021
RIR Address Pool runout projections as of the start of 2018:

## Slide 12: Post-Exhaustion Routing Growth
What’s driving this post-exhaustion growth?
  Transfers?
  Last /8 policies in RIPE and APNIC?
  Leasing and address recovery?

## Slide 13: Advertised Address “Age”
80% of all new addresses announced in 2010 were allocated or assigned within the past 12 months
2% of all new addresses announced in 2010 were >= 20 years ‘old’ (legacy)
2010

## Slide 14: Advertised Address “Age”
25 % of all new addresses announced in 2017 were allocated or assigned within the past 12 months
32 % of all new addresses announced in 2017 were >= 20 years ‘old’ (legacy)
2017

## Slide 15: 2000 – 2017: Advertised vs Unadvertised

## Slide 16: 2000 – 2017: Unadvertised Addresses
Total volume of
“reclaimed” addresses

## Slide 17: 2017: Assigned vs Recovered
Growth in Advertised Addresses
Change in the Unadvertised Address Pool
RIR Allocations
“address
recovery”
“draw down”

## Slide 18: V4 in 2017
The equivalent of 1.4 /8s was added to the routing table across 2017
Approximately 0.8 /8s were assigned by RIRs in 2015
  0.5 /8’s assigned by Afrinic
  0.3 /8s were assigned by RIPE NCC and APNIC (Last /8 allocations)
And a net of 0.6 /8’s were recovered from the pool of previously Unadvertised addresses

## Slide 19: The Route-Views View of IPv6
IANA IPv4 Exhaustion

## Slide 20: 2016-2017 in Detail

## Slide 21: Routing Indicators for IPv6
Routing prefixes – growing by some 10,000 prefixes per year
AS Numbers– growing by some 1,700 prefixes per year (which is half the V4 growth)

## Slide 22: Routing Indicators for IPv6
More Specifics now take up more than one third of the routing table
The average size of a routing advertisement is getting smaller

## Slide 23: Routing Indicators for IPv6
Advertised Address span is growing at a linear rate
The “shape” of inter-AS interconnection in IPv6 appears to be steady, as the Average AS Path length has been held steady through the year

## Slide 24: AS Adjacencies (Route Views)
10,415 out of 14,975 ASNs have 1 or 2 AS Adjacencies (69%)
1,020 ASNs have 10 or more adjacencies
5 ASNs have >1,000 adjacencies
4,190 AS6939 HURRICANE - Hurricane Electric, Inc., US
1,711 AS174 COGENT-174 - Cogent Communications, US
1,436 AS3356 LEVEL3 - Level 3 Communications, Inc., US
1,179 AS37100 SEACOM-AS, MU
1,041 AS1299 Telia Carrier, SE

## Slide 25: V6 in 2017
Overall IPv6 Internet growth in terms of BGP is steady at some 10,000 route entries p.a.

## Slide 26: What to expect

## Slide 27: BGP Size Projections
For the Internet this is a time of some uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of market-mediated movements of IPv4 on the routing table
    Uncertainty over the timing of IPv6 takeup leads to a mixed response to IPv6 so far, and no clear indicator of trigger points for change for those remaining IPv4-only networks

## Slide 28: V4 - Daily Growth Rates
Growth in the V4 network appears to be constant at a long term average of 140 additional routes per day, or some 51,000 additional routes per year

## Slide 29: V4 BGP Table Size Predictions
Jan 2016 587,000
2017 646,000
2018 699,000
2019 744,000
2020 795,000
2021 846,000
2022 897,000
2023 948,000

## Slide 30: V6 - Daily Growth Rates

## Slide 31: V6 BGP Table Size Predictions
Jan 2016 27,000 27,000
2017 37,000 37,000
2018 45,000 45,000
2019 47,000 63,000
2020 53,000 83,000
2021 59,000 110,000
2022 65,000 146,000
2023 71,000 194,000
Linear Exponential

## Slide 32: BGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
  The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing at a faster relative rate, is still small in size in absolute terms
  As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet

## Slide 33: BGP Updates
What about the level of updates in BGP?

## Slide 34: IPv4 BGP Updates

## Slide 35: IPv4 BGP Convergence Performance

## Slide 36: Updates in IPv4 BGP
Still no great level of concern …
The number of updates per instability event has been relatively constant, which unanticipated.
Likely contributors to this outcome are the damping effect of widespread use of the MRAI interval by eBGP speakers, and the compressed topology factor, as seen in the relatively constant V4 AS Path Length

## Slide 37: V6 BGP Updates

## Slide 38: V6 Convergence Performance

## Slide 39: Updates in IPv6
BGP Route Updates are very unequally distributed across the prefix set – they appear to affect a very small number of prefixes which stand out well above the average

## Slide 40: Updates in IPv6
The busiest 6 origin AS’s prefixes accounted for 70% of all BGP IPv6 prefix updates

## Slide 41: Routing Futures
There is little in the way of scaling pressure from BGP as a routing protocol – the relatively compressed topology and stability of the infrastructure links tend to ensure that BGP remains effective in routing the internet
The issues of FIB size, line speeds and equipment cost of line cards represent a more significant issue for hardware suppliers – we can expect cheaper line cards to to use far smaller LRU cache local FIBs in the high speed switches and push less used routes to a slower / cheaper lookup path. This approach may also become common in very high speed line cards

## Slide 42: Some Practical Suggestions
Understand your hardware’s highspeed FIB capacity in the default-free parts of your network
Review your IPv4 / IPv6 portioning - a dual-stack eBGP router will need 850,000 IPv4 slots and 85,000 IPv6 slots for a full eBGP routing table in line cards over the coming 24 months
Judicious use of default routes in your internal network may allow you drop this requirement significantly

## Slide 43: That’s it!
Questions?