## Slide 1: TCP and BBR
Geoff Huston
APNIC

## Slide 2: Computer Networking is all about moving data
The way in which data movement is controlled is a key characteristic of the network architecture
The Internet protocol passed all controls to the end systems, and treated the network as a passive switching environment
But that was many years ago, and since then we have seen the deployment of active middleware in networks and control traffic flows
All this is changing again as we see a what could well be a new generation of flow control algorithms being adopted in the Internet
Lets look at one of the more interesting initiatives: Bottleneck Bandwidth and Round-Trip Time (BBR)

## Slide 3: Let’s talk about speed
How fast can we push a single session to move data through the network?
Session speed is the result of a combination of:
    available transmission speeds,
    end-to-end latency and
    protocol efficiency
  All of these factors are critical

## Slide 4: The Evolution of Speed
1980’s
  TCP rates of Kilobits per second
1990’s
  TCP rates of Megabits per second
2000’s
  TCP rates of Gigabits per second
2010’s
  TCP rates of Gigabits per second

## Slide 5: Today
Optical transmission speeds are approaching Terrabit capacity
But peak TCP session speeds are not keeping up
What’s going on?

## Slide 6: TCP
The Transmission Control Protocol is an end-to-end protocol that creates a reliable stream protocol from the underlying IP datagram device
TCP operates as an adaptive rate control protocol that attempts to operate fairly and efficiently

## Slide 7: TCP Design Objectives
To maintain an average flow which is Efficient and Fair
Efficient:
  Minimise packet loss
  Minimise packet re-ordering
  Do not leave unused path bandwidth on the table!
Fair:
  Do not crowd out other TCP sessions
  Over time, take an average 1/N of the path capacity when there are N other TCP sessions sharing the same path

## Slide 8: It’s a Flow Control process
Think of this as a multi-flow fluid dynamics problem
Each flow has to gently exert pressure on the other flows to signal them to provide a fair share of the network, and be responsive to the pressure from all other flows

## Slide 9: TCP Control
TCP is an ACK Pacing protocol
Data sending rate is matched to the ACK arrival rate

## Slide 10: TCP Control
ACK pacing protocols relate to a past network state, not necessarily the current network state
  The ACK signal shows the rate of data that left the network at the receiver that occurred at ½ RTT back in time
  So if there is data loss, the ACK signal of that loss is already ½ RTT old!
    So TCP should react quickly to ‘bad’ news
  If there is no data loss, that is also old news
    So TCP should react conservatively to ‘good’ news

## Slide 11: “Classic TCP” – TCP Reno
Additive Increase Multiplicative Decrease (AIMD)
  While there is no packet loss, increase the sending rate by One Segment (MSS) each RTT interval
  If there is packet loss decrease the sending rate by 50% over the next RTT Interval
Start Up
  Each RTT interval, double the sending rate
  We call this “slow start” – probably because its anything but slow!!!

## Slide 12: Idealised TCP Reno
Time
Slow Start
Rate Doubles
each RTT
Interval
Congestion Avoidance
Rate increases by 1 MSS per RTT
Rate halves on Packet Loss
Notification of Packet Loss via Duplicate ACKs causes RENO to halve its sending rate

## Slide 13: TCP RENO and Idealized Queue Behaviour
Total Queue Capacity
(Onset of Packet Loss)
Link Capacity Capacity
(Onset of Queuing)
Network Buffers Fill
Network Buffers Drain

## Slide 14: Reno is too slow
TCP Reno tries to oscillate between sending rates R and 2 x R that span the actual link capacity
It increases its sending rate slowly so it’s really lousy when trying to run at very high speed over long delay networks
It over-corrects on loss and leaves available path capacity idle
  10Gbps rates over 100ms RTT demands a packet loss rate of less than 0.000003%
  An average 1% loss rate over a 100ms RTT can’t operate faster than 3Mbps

## Slide 15: Faster than Reno?
Can we make TCP faster and more efficient by changing the way in which the sending rate is inflated?
Of course!

## Slide 16: Refinements to RENO
There have been many efforts to alter RENO’s flow control algorithm
In a loss-based AIMD control system the essential parameters are the manner of rate increase and the manner of loss-based decrease
  For example:
    MulTCP behaves as it it were N simultaneous TCP sessions: i.e. increase by N segments each RTT and rate drop by 1/N upon packet loss
What about varying the manner of rate increase away from AI?

## Slide 17: Enter CUBIC
CUBIC is designed to be useful for high speed sessions while still being ‘fair’ to other sessions and also efficient even at lower speeds
Rather than probe in a linear manner for the sending rate that triggers packet loss, CUBIC uses a non-linear (cubic) search algorithm

## Slide 18: CUBIC and Queue formation
Total Queue Capacity
(Onset of Packet Loss)
Link Capacity Capacity
(Onset of Queuing)
Network Buffers Fill
Network Buffers Drain

## Slide 19: CUBIC assessment
Can react quickly to available capacity in the network
Tends to sit for extended periods in the phase of queue formation
Can react efficiently to long fat pipes and rapidly scale up the sending rate
Operates in a manner that tends to exacerbate ‘buffer bloat’ conditions

## Slide 20: Can we do better?
Lets look at the model of the network once more, and observe that there are three ‘states’ of flow management in this network:
  Under-Utilised – where the flow rate is below the link capacity and no queues form
  Over-Utilised – where the flow rate is greater that the link capacity and queues form
  Saturated – where the queue is filled and packet loss occurs
Loss-based control systems probe upward to the Saturated point, and back off quickly to what they guess is the Under-Utilised state in order to the let the queues drain
But the optimal operational point for any flow is at the point of state change from Under to Over-utilised, not at the Saturated point

## Slide 21: RTT and Delivery Rate with Queuing
Under-Utilised
Over-Utilised
Saturated

## Slide 22: How to detect the onset of queuing?
By carefully measuring the Round Trip Time!

## Slide 23: BBR Design Principles
Probe the path capacity only intermittently
Probe the path capacity by increasing the sending rate for a short interval and then drop the rate to drain the queue:
  If the RTT of the probe equals the RTT of the previous state then there is available path bandwidth that could be utilised
  If the RTT of the probe rises then the path is likely to be at the onset of queuing and no further path bandwidth is available
Do not alter the path bandwidth estimate in response to packet loss
Pace the sending packets to avoid the need for network buffer rate adaptation

## Slide 24: Idealised BBR profile
sending rate
network queues

## Slide 25: BBR Politeness?
BBR will probably not constantly pull back when simultaneous loss-based protocols exert pressure on the path’s queues
BBR tries to make minimal demands on the queue size, and does not rely on a large dynamic range of queue occupancy during a flow

## Slide 26: From Theory to Practice
Lets use BBR in the wild
I’m using iperf3 on Linux platforms (Linode)
  The platforms are dedicated to these tests
It’s the Internet
  The networks paths vary between tests
  The cross traffic is highly variable
  No measurement is repeatable to a fine level of detail

## Slide 27: Cubic vs BBR over a 12ms RTT 10G circuit

## Slide 28: Wow!
That was BRUTAL!
As soon as BBR started up it collided with CUBIC, and BBR startup placed pressure on CUBIC such that CUBIC’s congestion window was reduced close to zero
At this stage CUBIC’s efforts to restart its congestion window appear to collide with BBR’s congestion control model, so CUBIC remains suppressed
  The inference is that BBR appears to be operating in steady state with an ability to crowd out CUBIC

## Slide 29: BBR vs Cubic – second attempt
Same two endpoints, same network path across the public Internet
Using a long delay path AU to Germany via the US

## Slide 30: BBR vs Cubic
BBR (1) starts
Cubic starts
BBR (2) starts
Cubic ends
BBR(2) ends
The Internet is capable of offering a 400Mbps capacity path on demand!
In this case BBR is apparently operating with filled queues, and this crowds out CUBIC
BBR does not compete well with itself, and the two sessions oscillate in getting the majority share of available path capacity

## Slide 31: BBR and Loss Recovery
Packet loss causes retransmission that appears to occur in addition to the stable link capacity model used by BBR.
Once loss is reduced, BBR maintains a more consistent sending model

## Slide 32: Parallel BBR Streams
We used 50 parallel BBR streams between the same two endpoints (200ms RTT)
In this larger setup the majority of sessions managed to equilibrate between each other and evenly share the path bandwidth

## Slide 33: So what can we say about BBR?
It’s “interesting” in so many ways:
  It’s a move away from the more common loss-based flow control protocols
  It looks like it will operate very efficiently in a high-speed small-buffer world
    High speed small buffer chips are way cheaper, but loss-based TCP reacts really badly to small buffers by capping its flow rate
  It will operate efficiently over ECMP paths, as it is relatively impervious to packet re-ordering
  It also looks as if it will operate efficiently in rate policed environments
  Unlike AIMD systems, it will scale from Kbps to Gbps over long delay paths very efficiently
  It resists the conventional network-based traffic control mechanisms

## Slide 34: Why use BBR?
Because it achieves
Its incredibly efficient
It makes minimal demands on network buffer capacity
It’s fast!

## Slide 35: Why not use BBR?
Because it over achieves!
The classic question for many Internet technologies is scaling – “what if everyone does it?”
  BBR is not a scalable approach
  It works so well while it is used by just a few users, some of the time
  But when it is active, BBR has the ability to slaughter concurrent loss-based flows
  Which sends all the wrong signals to the TCP ecosystem
    The loss-based flows convert to BBR to compete on equal terms
    The network is then a BBR vs BBR environment, which is unstable

## Slide 36: Is this BBR experiment a failure?
Is it just too ‘greedy’ and too ‘insensitive’ to other flows to be allowed out on the Internet to play?
  Many networks have been provisioned as a response to the aggregate behaviours of loss-based TCP congestion control
  BBR changes all those assumptions, and could potentially push many networks into sustained instability
  We cannot use the conventional network control mechanisms to regulate BBR flows
    Selective packet drop just won’t create back pressure on the flow

## Slide 37: Where now?
BBR 2.0
  Alter BBR’s ‘sensitivity’ to loss rates, so that it does not persist with an internal bandwidth delay product (BDP) that exceeds the uncongested BDP
    This measure would moderate BBR 1.0’s ability to operate for extended periods with very high loss levels
  Improve the dynamic sharing fairness by moderating the Bandwidth Delay Product by using an estimated ‘fair’ proportion of the path BDP
  Accommodate the signal distortion caused by ACK stretching middleware
  Place an upper bound on the volume of in-flight data
  Alter the +/- 25% probe factors dynamically (i.e. allow this to be less than 25% overload)

## Slide 38: The new Network Architecture
We are seeing a shift away from network-level active middleware back towards edge-centric control in the Internet
QUIC and BBR are instances of a recent push back from the network-level QoS bandwidth control mechanisms, and result in greater levels of autonomous control being passed back to the end hosts

## Slide 39: What is all this telling us?
The Internet still contains a large set of important unsolved problems
Moving large data sets over high speed networks requires a different approach to what we are doing today
BBR seems to be a step in an interesting direction, particularly for very high speed networking
But it still calls for more research and more testing at scale

## Slide 40: That’s it!
Questions?