## Slide 1: What’s the Time?
Geoff Huston
APNIC

## Slide 2: Background
All computers run with some kind of internal oscillator (called a ‘clock’)
  This clock manages the internal state changes at each cycle of the central processing unit
  Clock ‘ticks’ are fed to a digital counter
  From this counter the computer can maintain a conventional clock and maintain the current time

## Slide 3: Why is Time useful for a computer?
To understand when things happen
  Crontab and event scheduling to ensure that a computer performs certain tasks at precise times
To understand the relative age of things
  For example, with NFS file systems its vital to understand which file is more recent
To understand when things are valid

## Slide 4: Security Certificates and Time
These security credentials are only usable in a defined window of time
The computer’s local clock is compared to these dates to determine whether to trust this certificate or not

## Slide 5: So we need to keep “time”
But this can be challenging
Computer clocks are based on quartz crystal oscillation
  Quartz crystal oscillation is only stable if the temperature and excitation voltage are kept stable. Changes in temperature or voltage will cause oscillation changes
Computer time of day clocks rely on counting ticks in a register
  Which is performed by software running in the processor at an elevated interrupt level
  If the processor runs for extended times at an even higher interrupt level then clock ticks can be ‘lost’

## Slide 6: Example of Computer Clock Stability
Dave Mill’s 2001 experiment on looking at clock stability over a one week period using a Linux PC
https://www.eecis.udel.edu/~ntp/ntpfaq/NTP-s-sw-clocks.htm

## Slide 7: So we need to keep “time”
We actually want to keep accurate and stable time
  Accurate in that every reference timekeeper keeps the same time
    (modulo the spacetime stretch factors of relativity)
  Stable in that the duration of each measured interval is exactly the same

## Slide 8: So we need to keep “time”
What is “time”?
We all know that time is divided into days, where a ‘day’ is defined as the duration between successive events when the sun is at precisely the same elevation in the sky
  But we don’t do this any more because the earth and the sun are poor timekeepers
We turned to distant quasars as the reference point
  But we don’t do this any more because we needed even greater precision

## Slide 9: So we need to keep “time”
We turned to nuclear physics:
  Time is defined using Système International (SI) seconds, defined as the duration of 9,192,631,770 periods of the radiation emitted by a caesium-133 atom in the transition between the two hyperfine levels of its ground state at a temperature of 0K

## Slide 10: Keeping Accurate Time
Not everyone can afford to run their own caesium clock

## Slide 11: Keeping Accurate Time
Not everyone can launch their own GPS network
The GPS satellite constellation is a set of 31 active earth-orbiting spacecraft operated by the US Air Force
These spacecraft are equipped with Caesium-133 reference clocks that broadcast time signals
GPS receivers can use triangulation from multiple satellites and delay measurement to determine the receiver’s position and provide an accurate reference time

## Slide 12: Distributing Accurate Time
Not every computer runs their own Cesium Clock or runs a GPS receiver to maintain accurate time
  But some folk do, and that’s a good thing!
So what we would like is a way to take this set of highly accurate reference time sources and provide a mechanism for others to synchronize their local clock against a reference source
On the Internet we use the Network Time Protocol (NTP) to perform this time synchronization function

## Slide 13: NTP Operation
Time sources are classified by their accuracy
  A Stratum 0 server is a reference clock (GPS or cesium)
  A Stratum 1 server is directly connected to a reference clock source
  A Stratum 2 server receives its time from a Stratum 1 server, and so on
NTP is a simple clock exchange UDP protocol
1 – client time
1 – client time
2 – server time
T1
T3
T4
1 – client time
1 – client time
2 – server time
Client Offset = ½ ((T2-T1) + (T3-T4))
T2
Client
Server

## Slide 14: NTP UDP Packets
A 48 byte UDP packet is passed between the client and server
The fields in the packet are:
The header section contains leap seconds, NTP version, NTP mode, Stratum level, polling interval and clock precision
Server’s round trip delay to its reference source and dispersion
Identification of reference source
64 bit reference date (seconds and fractions from 1 January 1900 00:00:00 UTC)
Time the request left the client
Time the request arrived at the server
Time the response left the server
NTP runs UTC – remember this!

## Slide 15: NTP Operation
In steady state the UDP clock packet exchange happens every 16 seconds
  Faster clock exchanges happen when the client clock has lost synchronisation with the server, and it will burst 8 packets evenly spaced across a 16 second interval
If the local clock needs to be adjusted the client time application will use adjtime() to slew the local clock. Clock correction is slow – 0.5ms per second
  Jumping the clock can fatally confuse applications, so this gentle slew is far kinder
NTP can normally maintain a client clock within a few hundredths of second of the server reference clock

## Slide 16: So we all agree on the time?
If everything supports NTP, and there is a well structured mesh of NTP reference clock servers then every connected Internet device that runs a clock should have the same value of time
  “same” is within a tenth of a second or less
But does the Internet agree on the time?

## Slide 17: The Experiment
Use a scripted online ad to direct a client to report back the value of the client’s clock
  Use the Javascript getTime() method to get the local UTC clock value
  Pass this value to the server as an argument to a URL fetch operation
Use NTP-managed clock on the server to maintain a stable reference clock
Record the distribution of differences
  Ignore the fine-grained differences due to local processing and network propagation time
  Which means that we are looking at measurements of time within +/- 1 second as being equivalent

## Slide 18: Results

## Slide 19: Log Scales can be misleading

## Slide 20: Results
We tested the clock of 202,460,921 clients over a 80 day period:
  11% of clocks are more than 1 second fast
  57% of clients are more than 1 second slow
  We observed clock slew values of up to 1 year both fast and slow
  92% of clients are within 120 seconds of the reference clock

## Slide 21: Fast Clocks
0.05% of all clocks are ahead by more than 2 days
There is a clear step function in this distribution that is aligned quite precisely to whole days
How can a client clock maintain a stable per-second clock, yet report a time value that is off by a number of whole days?

## Slide 22: Fast Clocks
0.7% of all clocks are ahead by more than 1 hour
As with the day distribution, there is a marked clustering of the clock offsets into units of hours, and a slightly smaller clustering into half-hours
Similar question: How can a client clock maintain a stable per-second clock, yet report a time value that is off by a number of whole hours?

## Slide 23: Slow Clocks
0.15% of all clocks lag by more than 2 days (3 x the number of fast clocks)
The per-day clustering is not so clear for slow clocks with a lag of greater than 2 days.

## Slide 24: Slow Clocks
1.05% of all clocks lag by 1 hour or more
Here there is a marked clustering of the clock offsets into units of hours

## Slide 25: Clustering of Clock Slew Values
This is a distribution of the clock slew values when the whole hours are removed
There is a very strong signal that when a clock has slewed from UTC time it does so in units of hours (and less so in units of half-hours)
NTP does not stabilize a local clock into a slew value of a whole number of hours, so this distribution is not an artefact of NTP.
What is going on here?

## Slide 26: Clustering of Clock Slew Values
This is a distribution of the clock slew values when the whole hours are removed
There is a very strong signal that when a clock has slewed from UTC time it does so in units of hours (and less so in units of half-hours)
NTP does not stabilize a local clock into a slew value of a whole number of hours, so this distribution is not an artefact of NTP.
What is going on here?
Does anyone here have some idea of what causes this?

## Slide 27: A Possible Theory
Localtime and UTC time are getting confused
We can test this theory with some additional data
Lets look at 3 countries with a large user population

## Slide 28: Brazil
LocalTime is UTC – 2, UTC-3, UTC -4, UTC-5
DST is variously applied in Brazil
So we should expect localtime at UTC -1 through UTC-5

## Slide 29: India
LocalTime is UTC +5:30
DST is not applied in India
So we should expect localtime at UTC +5:30
This is not clearly evident in the data
There is a strong bias to 30 minute offsets, but no pronounced peak at +5:30

## Slide 30: China
LocalTime is UTC +8
DST is not applied in China
So we should expect a peak of localtime at UTC +8

## Slide 31: A Possible Theory
Localtime and UTC time are getting confused
For the remainder of cases this is not simple clock drift. Some time source is syncing the local hosts UTC clock to the right second, but the hour value of the sync source is incorrect
This occurs between 10% to 20% of the time

## Slide 32: A view of Whole of Internet Time
Only 58% of visible clients run their clock with 2 seconds of UTC time
92% of visible clients run a clock that is within 60 seconds of UTC time
98% of clients are within 1 hour of UTC time

## Slide 33: If your application’s behavior relies on a consistent view of UTC time …
Its probably a poor idea to assume that all local clocks are tracking UTC time to within 1 hour
Its probably more robust to work in periods of days rather than seconds, minutes or even hours

## Slide 34
Thanks!