## Slide 1: The Resolvers We Use
Joao Damas, Geoff Huston
APNIC

## Slide 2: One of those wtf moments…

## Slide 3: One of those wtf moments…
10% of users are taking more than 300ms to resolve a DNS name
3% of users are taking more than 1s to resolve a DNS name

## Slide 4: One of those wtf moments…
10% of users are taking more than 300ms to resolve a DNS name
3% of users are taking more than 1s to resolve a DNS name
Why is DNS resolution performance so poor for this many users?

## Slide 5: And that leads to…
It appears that what we think about how the DNS works and how folk actually are using the DNS is not well aligned
We all think we understand how DNS resolution works in terms of the interchange of DNS protocol elements
  But the performance of DNS name resolution depends on a number of additional factors, both in terms of the users’ choice of resolvers and the name admin’s choice of authoritative servers

## Slide 6: But…
The issue is more than just a question of unexpected poor performance of name resolution.
There’s more to this...

## Slide 7: Why is DNS resolution data valuable?
Almost everything we do on the Internet starts with a DNS name resolution operation
DNS resolver query logs contain a rich vein of real time information about what users are doing:
  query logs and can be analyzed to infer information about the users themselves through the names that their applications resolve
  query logs contains indirect pointers that can be used to derive aggregate aspects of users’ demographics, preferences, purchases, etc

## Slide 8: Information Leaks
The question of where your DNS query traffic is being sent is also a question of whether you are leaking a real time trail of your online activities
Which leads to an interesting question about today’s Internet:
  To what extent is this DNS resolution data stream “leaked” outward?
    Across network boundaries?
    Across national boundaries?
  This second form of information leakage is “interesting”
    While many national regimes include regulations concerning personally identifying data, its not clear if these regulations extend these same protections to aliens who are not citizens of the country where the information is held

## Slide 9: Measuring the Internet via its Users
At APNIC Labs we’ve been using online ads to measure the user’s view of the Internet for some years
  We ask users to fetch a unique URL
  This involves a DNS resolution and a HTTP GET to our servers
  So we collect sets of DNS queries and WEB queries
  To see
    how we are doing with the IPv6 transition
    where DNSSEC validation is being used
    And similar questions

## Slide 10: Users and Resolvers
These data sets also allow us to match
  the IP address of the resolver that queries the authoritative name server (the “visible resolver”)
to
  the IP address of the client agent that retrieves the URL

## Slide 11: Some Numbers
Ad Placements: 11M – 14M ad placements per day
Ad Distribution: Most countries have some 100K – 250K ad placements per day

## Slide 12: Top 25 Resolvers – By IP Address
Rank Resolver Use % AS AS Name
1 125.5.210.212 0.57% AS7629 EPLDT, PH
2 196.188.52.8 0.49% AS24757 EthioNet-AS, ET
3 202.56.215.67 0.34% AS24560 Bharti Airtel, IN
4 2401:4900:50:9::5 0.34% AS9498 Bharti Airtel, IN
5 129.205.112.254 0.28% AS37148 Globa Com, NG
6 101.95.144.211 0.27% AS4812 China Telecom, CN
7 2405:200:160c:1957:78::6 0.27% AS55836 Reliance Jio, IN
8 49.45.29.22 0.27% AS55836 Reliance Jio, IN
9 2405:200:160c:1957:78::4 0.27% AS55836 Reliance Jio, IN
10 49.45.29.20 0.27% AS55836 Reliance Jio, IN
49.45.29.21 0.27% AS55836 Reliance Jio, IN
12 2405:200:160c:1957:78::5 0.26% AS55836 Reliance Jio, IN
13 221.228.15.194 0.25% AS4134 Chinanet Backbone, CN
14 101.95.144.210 0.25% AS4812 China Telecom, CN
15 219.128.128.102 0.21% AS58543 China Telecom, CN
16 2405:200:1613:1957:78::4 0.20% AS55836 Reliance Jio, IN
17 49.44.189.220 0.20% AS55836 Reliance Jio, IN
18 2405:200:1613:1957:78::5 0.20% AS55836 Reliance Jio, IN
19 49.44.189.221 0.20% AS55836 Reliance Jio, IN
20 49.44.189.222 0.20% AS55836 Reliance Jio, IN
21 2405:200:1613:1957:78::6 0.20% AS55836 Reliance Jio, IN
22 49.45.28.53 0.19% AS55836 Reliance Jio, IN
23 2405:200:1609:1957:78::5 0.19% AS55836 Reliance Jio, IN
2405:200:1609:1957:78::7 0.19% AS55836 Reliance Jio, IN
49.45.28.55 0.19% AS55836 Reliance Jio, IN

## Slide 13: Top 25 Resolvers – By IP Address
Rank Resolver Use % AS AS Name
1 125.5.210.212 0.57% AS7629 EPLDT, PH
2 196.188.52.8 0.49% AS24757 EthioNet-AS, ET
3 202.56.215.67 0.34% AS24560 Bharti Airtel, IN
4 2401:4900:50:9::5 0.34% AS9498 Bharti Airtel, IN
5 129.205.112.254 0.28% AS37148 Globa Com, NG
6 101.95.144.211 0.27% AS4812 China Telecom, CN
7 2405:200:160c:1957:78::6 0.27% AS55836 Reliance Jio, IN
8 49.45.29.22 0.27% AS55836 Reliance Jio, IN
9 2405:200:160c:1957:78::4 0.27% AS55836 Reliance Jio, IN
10 49.45.29.20 0.27% AS55836 Reliance Jio, IN
49.45.29.21 0.27% AS55836 Reliance Jio, IN
12 2405:200:160c:1957:78::5 0.26% AS55836 Reliance Jio, IN
13 221.228.15.194 0.25% AS4134 Chinanet Backbone, CN
14 101.95.144.210 0.25% AS4812 China Telecom, CN
15 219.128.128.102 0.21% AS58543 China Telecom, CN
16 2405:200:1613:1957:78::4 0.20% AS55836 Reliance Jio, IN
17 49.44.189.220 0.20% AS55836 Reliance Jio, IN
18 2405:200:1613:1957:78::5 0.20% AS55836 Reliance Jio, IN
19 49.44.189.221 0.20% AS55836 Reliance Jio, IN
20 49.44.189.222 0.20% AS55836 Reliance Jio, IN
21 2405:200:1613:1957:78::6 0.20% AS55836 Reliance Jio, IN
22 49.45.28.53 0.19% AS55836 Reliance Jio, IN
23 2405:200:1609:1957:78::5 0.19% AS55836 Reliance Jio, IN
2405:200:1609:1957:78::7 0.19% AS55836 Reliance Jio, IN
49.45.28.55 0.19% AS55836 Reliance Jio, IN
This list looks pretty strange!
A number of these resolvers share the same subnet – Are they different resolvers or part of a larger resolver “farm”?

## Slide 14: Top Resolvers – by Origin AS
Rank Resolver Use % Open Resolver / AS
1 Google DNS 9.39% GOOGLE, US
2 AS55836 7.89% Reliance Jio, IN
3 AS4134 5.22% ChinaNET Backbone, CN
4 AS4837 2.86% China Unicom, CN
5 AS9498 2.17% Bharti Airtel, IN
6 AS9808 1.66% China Mobile, CN
7 114dns 1.55% ChinaNET Backbone, CN
8 OpenDNS 1.49% OpenDNS, US
9 AS58543 1.47% China Telecom, CN
10 AS24560 1.25% Bharti Airtel, IN
11 dnspai 1.19% China Telecom, CN
12 AS38266 1.10% Vodafone India, IN
13 Onedns 1.01% China Unicom Beijing Province Network, CN
14 AS8151 0.92% Uninet, MX
15 AS45271 0.88% Idea Cellular, IN
16 AS56040 0.83% China Mobile, CN
17 AS7922 0.79% Comcast, US
18 Cloudflare 0.76% Cloudflare, US
19 Level3 0.76% Level 3, US
20 AS23693 0.73% Telekomunikasi Selular, ID
21 AS56046 0.71% China MobilE, CN
22 AS9121 0.66% TTNET, TR
23 AS17974 0.65% Telekomunikasi Indonesia, ID
24 AS7629 0.63% EPLDT, PH
25 AS132199 0.58% Globe Telecom, PH

## Slide 15: First Resolver or Full Resolver Set?
End hosts are often configured with 2 or more recursive resolvers
Is there much of a change in the use of recursive resolvers when we look at this full resolver set?

## Slide 16: Top Resolvers – by Origin AS
Rank Resolver Use % Open Resolver / AS
1 googlepdns 22.84% Google, US
2 AS55836 7.92% Reliance Jio Infocomm Limited, IN
3 AS4134 5.59% ChinaNET Backbone, CN
4 AS4837 3.14% China Unicom, CN
5 114dns 3.13% ChinaNET, CN
6 AS9498 2.90% Bharti Airtel IN
7 opendns 2.56% OpenDNS, US
8 AS24560 2.54% Bharti Airtel, IN
9 AS9808 1.87% China Mobile, CN
10 level3 1.54% Level 3, US
11 AS58543 1.53% China Telecom, CN
12 dnspai 1.37% China Telecom, CN
13 cloudflare 1.23% Cloudflare, US
14 onedns 1.20% China Unicom, CN
15 AS38266 1.10% Vodafone India, IN
16 AS56046 1.05 % China Mobile, CN
17 AS8151 1.00% Uninet, MX
18 AS56040 0.96% China Mobile, CN
19 AS45271 0.91% Idea Cellular, N
20 AS7922 0.80% Comcast, US
21 AS23693 0.73% Telekomunikasi Selular, ID
22 AS7629 0.70% EPLDT, PH
23 AS9121 0.68% TTNET, TR
24 AS17974 0.66% Telekomunikasi Indonesia, ID
25 AS132199 0.58% Globe Telecom, PH
Full Resolver Set

## Slide 17: Resolver Distribution

## Slide 18: Resolver Distribution
Just 3 resolver farms process 30% of users!
450 visible resolver sets handle the query load for 90% of all users
90% of users

## Slide 19: Counting Resolver Use

## Slide 20: Counting Resolver Use
55% of users use resolvers located in the same network
40% of users use resolvers located in the same country
23% of users use Google’s public DNS service

## Slide 21: Mapping Open Resolvers
For each country can we show the distribution of the resolvers used by users located within that country?

## Slide 22: Where is Google’s Public DNS used?

## Slide 23: Where are Google’s DNS Users?

## Slide 24: Why is this happening?
At lot of this story is Google’s Public DNS, which now has a “market share” of more than 9% of the Internet’s user population for first query
User’s efforts to circumvent content control via national DNS filtering measures
Network service providers redirecting queries towards Google (Its cheaper than running a local recursive resolver service!)
<insert your favourite theory here>

## Slide 25: Spain?
78% of users use resolvers located in the same network
First Resolver
10% of users use resolvers located in Spain
9% of users use Google

## Slide 26: Spain?
85% of users use resolvers located in the same network
All Resolvers
20% of users use resolvers located in Spain
18% of users use Google

## Slide 27: DNS over HTTPS
Today most DNS is the result of ISP configuration
Most users are willing to accept the service provider defaults
But what happens with DNS over HTTPS?
  What happens when Firefox directs their DNS queries to a different resolver?
  Will applications exercise greater control of the choice of DNS resolution?

## Slide 28: Where is the DNS heading?
Is the DNS under pressure to aggregate to ever larger resolvers and server farms?
What is the economic model of name resolution in a highly aggregated environment? Will resolver operators turn to data mining of queries to generate revenue streams?
Is it possible to reduce the information exposure while still using common resolver caches?
What is the nature of the trade-off between resolution performance and information leakage in DNS resolution?

## Slide 29
Thanks!