## Slide 1: BGP in 2023
Geoff Huston

## Slide 2: A super-brief summary of BGP!
BGP is the distributed routing protocol that manages the reachability of address prefixes across the Internet
  Its objective is to distribute to all BGP speakers a current list of reachable address prefixes and the local next-hop interface to use to forward packets to each address prefix
This is an instance of a Bellman-Ford Distance Vector routing protocol
  BGP uses a “Path Vector” to prevent loop formation and aid in the comparison of routes

## Slide 3: For example:…
bgpd# show ip bgp
BGP table version is 0, local router ID is 203.133.248.2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, r RIB-failure, S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
* 1.0.0.0/24 202.12.28.1 0 4777 13335 i
* 203.119.104.2 0 4608 13335 i
*> 203.119.104.1 0 4608 13335 i
* 1.0.4.0/22 202.12.28.1 0 4777 2500 7660 4635 7545 2764 38803 i
* 203.119.104.2 0 4608 1221 2764 38803 i
*> 203.119.104.1 0 4608 1221 2764 38803 i
* 1.0.5.0/24 202.12.28.1 0 4777 2500 7660 4635 7545 2764 38803 i
*> 203.119.104.2 0 4608 1221 2764 38803 i
* 203.119.104.1 0 4608 1221 2764 38803 i
* 1.0.16.0/24 202.12.28.1 0 4777 2516 3356 2519 i
* 203.119.104.2 0 4608 1221 3356 2519 i
*> 203.119.104.1 0 4608 1221 3356 2519 i

## Slide 4: Why look at BGP Tables?
BGP is one of the few tools that lets us see all of the Internet at once.
The functional objective of BGP is to flood reachability information for all reachable address prefixes to all BGP speakers
Which means that looking at BGP tables can be related to looking at the entire Internet!

## Slide 5: The Highlights
IPv4 Summary
IPv6 Summary
FIB Projections
Churn
Directions

## Slide 6
1994: Introduction of CIDR
2001: The Great Internet
Boom and Bust
2005: Consumer Market
2011: Onset of Address Exhaustion
30 Years of Routing the IPv4 Internet
This is a view pulled together from each of the routing peers of Route-Views and RIPE RIS

## Slide 7: IPv4 in 2023

## Slide 8: IPv4 in 2023
Large Withdrawal
60K entry variation
22 Feb
TTNET – Turkey
AS9121 -5,279 prefixes
AS47331 -2,427 prefixes

## Slide 9: Aside: What happened to TTNET?
These are all withdrawals of more specific prefixes

## Slide 10: AS Prefix Count over 2023
Dropped Prefixes
Added Prefixes

## Slide 11
2001: The Great Internet
Boom and Bust
30 Years of IPv4 Advertised Address Span
This is a view pulled together from each of the routing peers of Route-Views and RIPE RIS
2011: Onset of Address Exhaustion
2021: Advertised DoD blocks
2005: Consumer Market

## Slide 12
2023 in Detail
Amazon O2 – 22 Aug

## Slide 13: 2023: Assigned vs Recovered Addresses
Change in UnAdvertised Addresses
Change in the Advertised Address Pool
RIR Allocations
3.0B advertised
-18M delta
3.6B allocated
-0.02M delta
640M unadvertised
+18M delta

## Slide 14: 2023: Assigned vs Recovered Addresses
Change in UnAdvertised Addresses
Change in the Advertised Address Pool
RIR Allocations
3.0 advertised
-18M delta
3.7B allocated
+0,5M delta
640M unadvertised
+18M delta
No net “address recovery” occurred across 2023 in IPv4
A total of 18M addresses were withdrawn from the advertised network, and shifted to the unadvertised pool
The net change in the unadvertised pool was an increase of 18M addresses

## Slide 15: 2018-2023: 6 Year Assigned vs Recovered Addresses
DoD block Advertisments
Advertised IPv4 span
starts to decline
Residual RIR Address pools are exhausted

## Slide 16: Advertised Span per Origin AS over 2023
Reduced Advertised Address Span
Increased Advertised Address Span

## Slide 17: What happened in 2023 in V4?
  From the look of the routing growth plots, the growth of the size of the IPv4 network is slowing down
  The number of entries in the IPv4 default-free zone reached 920K – 960K by the end of 2023
  The pace of growth of the routing table was slightly lower than the rolling 5-year average, with 20,000 new entries in 2023 (was 36,000 in 2022)
  The AS position was slightly lower with 1,100 new AS’s advertised in 2023 (was 1,400 in 2021)
  Transit relationships have not changed materially over 2022 for most networks
  The address range spanned by the advertised route set declined in 2023 by the equivalent of 1 /8
  The overall IPv4 routing growth trends slowed down or even reversed through 2023

## Slide 18: What happened in 2023 in V4?
  From the look of the routing growth plots, the growth of the size of the IPv4 network is slowing down
  The number of entries in the IPv4 default-free zone reached 920K – 960K by the end of 2023
  The pace of growth of the routing table was slightly lower than the rolling 5-year average, with 20,000 new entries in 2023 (was 36,000 in 2021)
  The AS position was slightly lower with 1,100 new AS’s advertised in 2023 (was 1,400 in 2021)
  Transit relationships have not changed materially over 2022 for most networks
  The address range spanned by the advertised route set declined in 2023 by the equivalent of 1 /8
  The overall IPv4 routing growth trends slowed down or even reversed through 2023
Have we reached Peak IPv4?

## Slide 19: The Highlights
IPv4 Summary
IPv6 Summary
FIB Projections
Churn
Directions

## Slide 20: The 20-Year View of IPv6
IANA IPv4 Exhaustion

## Slide 21: 2023 IPv6 FIB in Detail

## Slide 22: 2023 IPv6 FIB in Detail
AS18403 + 3,292 prefixes – FPT, VN
AS60539 + 2,049 prefixes – HUICAST_TELECOM, HK

## Slide 23: More Specifics in IPv6
45% of all IPv6 prefixes are /48’s
IPv6
IPv4

## Slide 24: 20-Year IPv6 Advertised Address Span

## Slide 25: IPv6 Advertised Address Span in 2023

## Slide 26: V6 in 2023
Overall IPv6 Internet growth in terms of BGP is still increasing, and is currently at some 30,000 route entries p.a. (17%)
  Predominate use of /48 more specifics
  2,000 more AS’s advertising IPv6 prefixes
  Growth of 2,500 /32 equivalents in the advertised address span ( 1.6%)
  Growth rates across 2023 are lower than 2018 – 2020 annual rates

## Slide 27: The Highlights
IPv4 Summary
IPv6 Summary
FIB Projections
Churn
Directions

## Slide 28: V4 BGP Table Size Predictions
Date RIB Size Prediction
Jan 2019 760,000
2020 814,000
2021 856,000
2022 906,000
2023 942,000
2024 944,0000 949,000
2025 958,000
2026 958,000
2027 947,000
2028 928,000
2029 898,000

## Slide 29: V4 BGP Table Size Predictions
Date RIB Size Prediction
Jan 2019 760,000
2020 814,000
2021 856,000
2022 906,000
2023 942,000
2024 944,0000 949,000
2025 958,000
2026 958,000
2027 947,000
2028 928,000
2029 898,000
The best fit projection model to the past 4 years of FIB data is a polynomial function that peaks in 2024 at just under 1M entries

## Slide 30: V6 BGP Table Size Predictions
Jan 2019 62,000
2020 79,000
2021 106,000
2022 147,000
2023 172,000
2024 201,000 198,000 227,000
2025 226,000 293,000
2026 254,000 380,000
2027 282,000 491,000
2028 310,000 635,000
2029 337,000 822,000
Linear Exponential
Note that the IPv6 tables are 128bits wide – i.e. 4x the size of the IPv4 tables!

## Slide 31: V6 BGP Table Size Predictions
Jan 2019 62,000
2020 79,000
2021 106,000
2022 147,000
2023 172,000
2024 201,000 198,000 227,000
2025 226,000 293,000
2026 254,000 380,000
2027 282,000 491,000
2028 310,000 635,000
2029 337,000 822,000
Linear Exponential
Note that the IPv6 tables are 128bits wide – i.e. 4x the size of the IPv4 tables!
The growth model for IPv6 is highly uncertain today – It looks like a linear growth model matches the most recent 24 months of data
The underlying network growth is lower, and over half of the growth in this model is due to the continued intensive use of /48 more specifics

## Slide 32: BGP Table Growth
The absolute size of the IPv6 routing table is growing much faster than the IPv4 table
  These two tables will require the same storage/lookup size in around 1 year from now, given that each IPv6 entry is 4 times the bit size of an IPv4 entry
The good news …
  As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet

## Slide 33: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Directrions

## Slide 34: IPv4 BGP Updates – Daily Updates

## Slide 35: IPv4 BGP Updates – Daily Updates
The IPv4 network is surprisingly stable
The number of withdrawals per day has been relatively steady for some 15 years (aside from some increases in 2022/3)
The number of updates per day has been declining through 2023

## Slide 36: IPv4 Unstable Prefixes per Day

## Slide 37: IPv4 Unstable Prefixes per Day
The number of prefixes that are the subject of updates has been slowly increasing over this 15-year period
The rate of increase of unstable prefixes is far lower than the number of advertised prefixes

## Slide 38: IPv4 BGP Convergence Performance

## Slide 39: IPv4 BGP Convergence Performance
Convergence performance has been steady for 15 years, despite the massive growth in the network
The network topology continues to increase in density, keeping critical AS Paths short as the network itself increases in size

## Slide 40: Updates in IPv4 BGP
The IPv4 inter-domain routing system is still highly stable
The number of updates per instability event and the time to converge to a stable forwarding state has been relatively constant for many years - it rose in 2019 - 2020 and has declined again in 2021, and stabilized in 2022
20% of prefixes generate 80% of all updates. Less than 5% of all origin networks are linked to 80% of all updates. Routing instability is concentrated in a small number of highly unstable cases.

## Slide 41: V6 BGP Updates

## Slide 42: V6 BGP Updates
The growth trajectory of IPv6 has slackened off, and the daily total of updates and withdrawals has been steady across 2023

## Slide 43: V6 Unstable Prefixes
LOG Scale!

## Slide 44: V6 Unstable Prefixes
The number of unstable address prefixes stabilised across 2023
Proportionally, IPv6 prefixes are ~2x more likely to be updated as compared to the IPv4 BGP network
LOG Scale!

## Slide 45: V6 Convergence Performance

## Slide 46: V6 Convergence Performance
Time to converge has been very unstable for years in IPv6
This is now stabilising to a level that is on a par with the IPv4 network

## Slide 47: Updates in IPv6 BGP
It’s improving …
Compared to IPv4, the IPv6 network has exhibited a high level of skew of routing instability, where a small number of networks contribute disproportionately to the overall level of BGP updates in IPv6.
Just 2 AS’s generated 50% of the BGP IPv6 update load in the last 2 weeks of 2023. IPv6 routing instability is still concentrated in a small number of pathologically unstable cases.

## Slide 48: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Directions

## Slide 49: Directions: Securing Routing
The plan of study in securing the routing system is to:
  Characterize the current behaviour of the Internet’s inter-domain routing system
  Understand the bounds of “normal” behavior
  Characterize the ways in which routing information can be manipulated
  Ways to identify anomalous routing information
  Augment the routing environment with means to perform this detection

## Slide 50: Some Open Questions
Should a useful secured routing system be reactive or preventative?
In a market-drive economy who pays for security?
Is the most effective response technical or regulatory?
Where / how should we respond?
  Is this a network issue with a network solution?
  Or should applications protect themselves?
What is the nature of “trust” in a networked environment?
How can crypto help?

## Slide 51: That’s it!
Questions?