## Slide 1: Quality of Service in the Internet: Fact, Fiction, or Compromise?
Paul Ferguson, Cisco Systems, Inc.
Geoff Huston, Telstra

## Slide 2: Quality of Service Definitions Approaches Mechanisms Considerations Summary

## Slide 3: What is the problem?
Today’s Internet is plagued by sporadic poor performance
This is getting worse, not better
Customers want access to an Internet service which provides consistent & predictable high quality service levels
Network mechanisms intended to meet this demand are categorized within the broad domain of Quality of Service

## Slide 4: Rationale
The Internet is commercial & competitive.
    No major revelation here.
Internet Service Providers are looking for ways to generate new sources of revenue.
    Again, nothing new.
Creation of new services creates new sources of revenue.
Preferential treatment is an attractive service which customers are indicating they desire to purchase.

## Slide 5: Non-Rationale
QoS is not a tool to compensate for inadequacies elsewhere in the network.
    Massive over-subscription.
    Horrible congestion situations.
    Sloppy network design.
No magic here™.

## Slide 6: What is the expectation?
A requirement for a premium differentiated service within the network that will provide predictable and consistent service response for selected customers and traffic flows.
Guarantees on bandwidth & delay.
But can the Internet deliver?

## Slide 7: Expectation setting
QoS is not magic.
  QoS cannot offer cures for a poorly performing network.
  QoS does not create nonexistent bandwidth.
    Elevating the amount of resources available to one class of traffic decreases the amount available for other classes of traffic.
  QoS will not alter the speed of light.
    On an unloaded network, QoS mechanisms will not make the network any faster.
      Indeed, it could make it slightly worse!

## Slide 8: Expectation setting
QoS is unfair damage control.
  QoS mechanisms attempt to preferentially allocate resources to predetermined classes of traffic, when the resource itself is under contention.
  Resource management only comes into play when the resource is under contention by multiple customers or traffic flows.
    Resource management is irrelevant when the resource is idle or not an object of contention.

## Slide 9: Expectation setting
QoS is relative, not absolute.
  QoS actively discriminates between preferred and non-preferred classes of traffic at those times when the network is under load (congested).
  Qos is the relative difference in service quality between the two generic traffic classes.
    If every client used QoS, then the net result is a zero sum gain.

## Slide 10: Expectation setting
QoS is intentionally elitist and unfair.
  The QoS relative difference will be greatest when the preferred traffic class is a small volume compared to the non-preferred class.
  QoS preferential services will probably be offered at a considerable price premium to ensure that quality differentiation is highly visible.

## Slide 11: What is Quality?
Quality cannot be measured on an entire network.
  Flow bandwidth is dependant on the chosen transit path.
  Congestion conditions are a localized event.
  Quality metrics degrade for those flows which transit the congested location.
Quality can be measured on an end-to-end traffic flow, at a particular time.

## Slide 12: Quality metrics
The network quality metrics for a flow are:
  Delay - the elapsed time for a packet to transit the network.
  Jitter - the variation in delay for each packet.
  Bandwidth - the maximal data rate that is available for the flow.
  Reliability - the rate of packet loss, corruption, and re-ordering within the flow.

## Slide 13: Quality metrics
Quality metrics are amplified by network load.
  Delay increases due to increased queue holding times.
  Jitter increases due to chaotic load patterns.
  Bandwidth decreases due to increased competition for access.
  Reliability decreases due to queue overflow, causing packet loss.
Quality differentiation is only highly visible under heavy network load.

## Slide 14: Service Quality
Not every network is designed with quality in mind…
Adherence to fundamental networking engineering principals.
Operate the network to deliver Consistency, Stability, Availability, and Predictability.
Cutting corners is not necessarily a good idea.
Without Service Quality, QoS is unachievable.

## Slide 15: Quality of Service Definitions Approaches Mechanisms Considerations Summary

## Slide 16: Integrated Services
Per flow traffic management to undertake one of more of the following service commitments:
  Place a preset bound on jitter.
  Limits delay to a maximal queuing threshold.
  Limit packet loss to a preset threshold.
  Delivers a service guarantee to a preset bandwidth rate.
  Deliver a service commitment to a controlled load profile.
Challenging to implement in a large network.
Relatively easy to measure success in meeting the objective.

## Slide 17: IntServ and the Internet
Integrated Services requires the imposition of flow-based dynamic state onto network routers in order to meet the stringent requirements of a service guarantee for a flow.
Such mechanisms do not readily scale to the size of the Internet.

## Slide 18: Differentiated Services
Active differentiation of network traffic to provide a better than best effort performance for a defined traffic flow, as measured by one of more of:
  Packet jitter
  Packet loss
  Packet delay
  Available peak flow rate
Implementable within a large network.
Relatively difficult to measure success is providing service differentiation.

## Slide 19: DiffServ and the Internet
Differentiated Services can be implemented through the deployment of differentiation router mechanisms triggered by per-packet flags, preserving a stateless network architecture within the network core.
Such mechanisms offer some confidence to scale to hundreds of millions of flows per second within the core of a large Internet

## Slide 20: Quality of Service Definitions Approaches Mechanisms Considerations Summary

## Slide 21: QoS Service Element
Q: What is the service element for QoS services?
A1: Network ingress selection
  Application-based differentiation:
    TCP or UDP port number
  Sender’s traffic has elevated QoS:
    Source IP address
  Traffic to client has elevated QoS
    Destination IP address
  Combinations of the above
    Flow based QoS, or flow-class based QoS

## Slide 22: QoS Service Element (cont)
  Admission traffic profile filter
    In-Profile traffic has elevated QoS, out-of-profile uses non-QoS
A2: User selected - network filtered
  User authentication
    Allow the user to set QoS flags
    Admission filter authenticates user settings
A3: - Combinations of the above

## Slide 23: Virtual Circuits
Segmented bandwidth resource for QoS states:
  Ingress traffic shaping (token or leaky bucket)
  Virtual circuits & statistical muxing (e.g. ATM, Frame Relay)
  RSVP admission control & reservation state
Segmentation mechanisms by themselves are unrealistic in a large scale heterogeneous Internet which uses end-to-end flow control.

## Slide 24: QoS Paths
Alternate path selection
  Alternative physical paths
    E.g., cable and satellite paths
  QoS Routing v. administrative path selection
Must be managed with care.
Can lead to performance instability.
Prone to inefficient use of transmission.
May not support end-to-end path selection.

## Slide 25: QoS per packet indicators
Explicit per packet signaling of:
  Precedence indication (delay)
  Discard indication (reliability)
As an indication of preference for varying levels of best effort.
This is deployable - today.

## Slide 26: Quality of Service Definitions Approaches Mechanisms Considerations Summary

## Slide 27: End-to-End QoS
Reliance on a particular link-layer technology to deliver QoS is fundamentally flawed.
TCP/IP is the “common bearer service,” the most common denominator in today’s Internet.
Partial-path QoS mechanisms introduce distortion of the data flow and are ineffectual.
Notes: It is also unrealistic to attempt to provide end-to-end QoS in the Internet with any particular link-layer technology, such as ATM, since a packet in flight between a source and destination may traverse any number of link-layer transport media types (e.g. Ethernet, point-to-point serial links).
This is where the “most common denominator” philosophy comes into play. Since the “common bearer service” in the Internet is the TCP/IP protocol suite, this is the natural place to do traffic differentiation.

## Slide 28: Pervasive homogeneity - Not!
Reliance on link-layer mechanisms to provide QoS assumes pervasive end-to-end, desktop-to-desktop, homogenous link-layer connectivity.
This is simply not realistic.

## Slide 29: State and Scale
To undertake firm commitments in the form of per-flow carriage guarantees requires network-level state to be maintained in the routers.
State becomes a scaling issue.
Wide-scale RSVP deployment will not scale in the Internet (See: RFC2208, RSVP Applicability Statement).

## Slide 30: Network Layer Tools
Traffic shaping and admission control.
IP packet marking for both delay indication & discard preference.
Weighted Preferential Scheduling algorithms.
Preferential packet discard algorithms (e.g. Weighted RED, RIO).
End result: Varying levels of best effort under load.
Of Course: No congestion, no problem.
Notes: Various IP packet marking schemes have been proposed in the IETF. See:
  http://diffserv.lcs.mit.edu/
  http://www.employees.org:80/~ferguson/QoS.html
  http://cio.cisco.com/warp/public/732/net_enabled/qos_wp.htm
For more information on RED (Random Early Detection), see:
  http://www-nrg.ee.lbl.gov/floyd/red.html
If there is no congestion in the network, everyone’s packets get delivered and everyone is happy.

## Slide 31: QoS Implementation Considerations
Complexity: If your support staff can’t figure it out, it is arguably self-defeating.
Delicate balance between network design & architecture and QoS.
Notes: Building a network is only a small percentage of solving the overall problem -- once the network is built, someone has to provide ongoing management, maintenance, and troubleshooting support. If the network is excessively complex to the point where your support staff cannot figure it out, or has trouble pinpointing problems due to the complex nature of the network, then this is an important liability.
Remember Occam’s Razor, “All things being equal, choose the solution which is simpler.”
There is a delicate balance between the design & architecture of the network, and the ability to provide ongoing Quality of Service. If the network is designed poorly, then one might suggest that the ability to provide QoS is diminished significantly.

## Slide 32: Yet to be Resolved
Long held adaptive flows are susceptible to network layer shaping.
Short held flows (WWW transactions)
  Are not very susceptible to network layer shaping
  Modify stack behavior by augmenting initial cwnd?
UDP flow management
  Unicast flow model (ingress filter or sender moderation?)
  Multicast flow model (multi-layering of the signal?)
Inter-Provider semantics for differentiated services.
Notes: Some other unanswered questions still are being examined, such as non-adaptive flows and bit semantics interpretation between different administrative domains.
The IETF Integrated Services working group has begun examining these issues in an effort dubbed “Differential Services” (diffserv). More information can be found on diffserv efforts at:
http://diffserv.lcs.mit.edu/

## Slide 33: Unanswered Questions
How does the provider measure QoS?
How does the customer measure QoS?
How do you tariff, account, and bill for QoS?
How will QoS work in a heterogeneous Internet?
  QoS across transit administrative domains which may not participate or use different QoS mechanisms?
Notes: Unanswered questions still exist in several areas with regard to QoS, such as how to measure and bill for QoS services, as well as how to provide end-to-end QoS when an administrative domain within the traffic path does not participate (or honor) the QoS mechanisms and semantics.
A couple of groups are looking a traffic measurement in the Internet, and perhaps in the future, may also begin to look at how to measure QoS:
The IETF IP Performance Metrics (ippm) working group:
  http://www.ietf.org/html.charters/ippm-charter.html
  Cooperative Association for Internet Data Analysis (CAIDA):
  http://www.caida.org/

## Slide 34: Quality of Service Definitions Approaches Mechanisms Considerations Summary

## Slide 35: Summary
There is no magic QoS bullet.
There are no absolute guarantees in the Internet. Sorry.
There is possibly a “middle ground” somewhere between traditional single level best effort and guaranteed customized services.

## Slide 36: References
Differential Services in the Internet http://diffserv.lcs.mit.edu/
Quality of Service: Delivering QoS in the Internet and the Corporate Network http://www.wiley.com/compbooks/ferguson/

## Slide 37: Questions? Thank you.
Paul Ferguson
Consulting Engineer,
Internet Architecture
ferguson@cisco.com
Geoff Huston
Technology Manager
Telstra Internet
gih@telstra.net