## Slide 1: Internet Addressing A Technical Overview
David R. Conrad
drc@isc.org
Internet Software Consortium

## Slide 2: Overview
Background
Internet Address History
Internet Address Allocators
Conclusions

## Slide 3: Addresses -- How to get here from there
Addresses provide information on how to locate something, e.g., what route to take from here to there.
Internet addresses combine
  a routing portion, known as the network part
  a name portion known as the host part
How to split an Internet address into the network part and the host part has changed over time…

## Slide 4: The Beginning
Back when the TCP/IP protocols were first being designed, there was a big argument between fixed length and variable length addresses
  Fixed length will always be limited
    But if you make it big enough, no one will notice
  Variable length will always take more cycles to process
    But there are tricks you can play to minimize the difference
The decision was made for fixed, 32 bit addresses
  Rumor has it, by a flip of a coin...

## Slide 5: IP version 4 Addresses
32 bit unsigned integers
  possible values 0 - 4,294,967,295
Typically written as a “dotted quad of octets”
  four 8 bit values with a range of 0-255 separated by “.”
  For example, 202.12.28.129 can be written as below

## Slide 6: Internet Addresses
A subset of IPv4 addresses
  One of an infinite number
Guaranteed globally unique by the IANA
  Generally allocated by delegated authorities such as Internet service providers or regional registries
  Assumed to be routable
    Bad assumption
Partitioned into two parts
  A host part that identifies a particular machine on a local or wide area network
  A network part that gives routers information how to get to the local or wide area network via the Internet

## Slide 7: Internet Address Structure
Originally, the architects of the Internet thought 256 networks would be more than enough
  Assumed a few very large (16,777,216 hosts) networks
  They were wrong (in case you were wondering)
Addresses were partitioned as below
  8 bit network part, 24 bit host part

## Slide 8: Classfull Addressing
Original addressing plan too limiting
  More than 256 networks with many fewer hosts than 224
Solution was to create address classes

## Slide 9: The Problem
Class A way too big
  16 million hosts in a flat network is unthinkable
Class B too big
  Even 65536 host addresses is too many in most cases
    Imagine 65534 hosts all responding to a broadcast
Class C too small
  Most sites initially connecting to the Internet were large Universities, 256 was too small for them
Need more flexibility!

## Slide 10: Subnetting
Classfull addressing was a better fit than original
  but class A and B networks impossible to manage
Solution was to partition large networks internally into sub-networks (subnets)
  Typically “class C” (8 bit host part) sized subnets although variable length subnets used too

## Slide 11: Classless Addressing
Forget what I just told you
  Classfull addressing is officially “Bad”™
    3 sizes just don’t fit all -- very wasteful
Better solution is to use variable length partitioning between the host and network parts
  Actual partitioning for a site provided by routing protocol
  notation is dotted quad followed by a “/” and the network part length, e.g., 202.12.28.129/26  First host on 64 host network starting at 202.12.28.128
No need for subnets

## Slide 12: Example of Classless Addressing
Prefix 202.12.28.0/22
  1024 host addresses
  announced as a single network (important!)
Consists of 7 subnets
  202.12.28.0/25
  202.12.28.128/26
  202.12.28.192/26
  202.12.29.0/24
  202.12.30.0/24
  202.12.31.0/25
  202.12.31.128/25

## Slide 13: Summary
Internet addresses are 32 bit fixed length globally unique numbers
  One subset of all IPv4 address spaces
Internet addresses have evolved over time to be more flexible and to include hierarchy
Currently, classless addressing is in use providing arbitrary host and network part lengths.