## Slide 1: Addressing Issues
David Conrad
drc@isc.org
Internet Software Consortium

## Slide 2: Addressing Issues
Routability, hierarchical addressing, and address ownership
Address Scarcity
Allocation Policies
Static vs. Dynamic/Private vs. Global Addressing
Multi-homing and Virtual Hosting
Confederations/National NICs

## Slide 3: Routability
The Internet is growing fast
  Faster than router vendors can keep upgrading router technology (and keep router prices reasonable)
Every address allocated outside a service provider block must show up in the global routing tables
  The number of entries in those tables are very limited
  Every update to those entries must be propagated globally
Some service providers are filtering out smaller globally routed allocations
  Smaller allocations affect fewer people and tend to “flap” more
  If ISPs don’t filter, their routers melt

## Slide 4: Internet Routing Table Growth

## Slide 5: Hierarchical Addressing
The only way high performance large networks can get larger is if you hide information
  Details always take time/resources to process
One way to hide information is to aggregate it
  +65 aggregates all telephone numbers in Singapore
  “Ulaan Bataar”, Mongolia aggregates all postal addresses in Ulaan Bataar
  202.12.28.0/22 aggregates all 1024 hosts from 202.12.28.0 - 202.12.31.255
Internet addresses are hierarchically assigned
  Service providers get a block from a regional registry
    The ISP’s customers get address from that ISP block
      The ISP customer’s customers get addresses from the customer block

## Slide 6: Address Ownership
The problem with hierarchical addressing?
  If a site changes providers, it should renumber out of the old provider’s address space into the new
    If not, the non-aggregatable addresses be treated the same as top level aggregated addresses
      i.e., must show up in the global routing tables
  This implies the service providers own the addresses not the customers
Renumbering can be expensive
  Dynamic addressing can help

## Slide 7: Address Scarcity
The Internet is growing fast
  There are concerns that 4,294,967,295 addresses are not sufficient
    Especially given an average utilization < 1%
  Some people think we have already run out of IPv4 addresses
However:
  Only about half of the address space has been used
  New technologies (NAT, ALG) reduce the need for addresses
  As address gets scarcer, organizations will have incentive to use it more efficiently

## Slide 8: Address Registry Policies
RFC 2050 documented address allocation procedures
  Documents current practice
    Took two years to write
    Makes no claims whether current practice is a good idea or not
Policies documented by RFC 2050 were defined by the “Internet Community”
  An uneasy balance between end users and service providers
Official authority is the IANA
  But where does the IANA get its authority?

## Slide 9: Static vs. Dynamic Addressing
Dynamic addressing
  When dialing up to the Internet, addresses assigned when the modem connects
  LANs can be configured so that machines get Internet addresses when they boot
Efficient use of address space
  Only those machines on the net have addresses
Can be inconvenient
Static Addressing
  Addresses are assigned to the user or the machine, regardless of whether it is connected
Can be convenient as Internet connectivity OK over physical disconnect/reconnect
Can be less efficient in use of address space
  Particularly if users have multiple dialup accounts

## Slide 10: Private vs. Global Addressing
Private addressing
  Use of networks that cannot be routed on the Internet with address translation techniques to provide Internet connectivity
Very efficient
  Only one Internet address necessary for an entire site
Controversial
  Thought to break fundamental TCP/IP assumptions
  Adds another point of failure
Global Addressing
  Using normal Internet addresses
Can be particularly wasteful for sites which do not connect to the Internet or do so through firewalls
  Don’t really need global addresses for this
Provide most flexibility in case site decides to connect to the Internet

## Slide 11: Multi-homing
Multi-homing is defined as a single site having multiple connections to the Internet
  Usually done for reliability reasons
    But may not offer the level of reliability thought
For multi-homing to be effective, addresses must be in the global routing tables
  The less aggregated the address, the more likely it will still be visible if part of the network goes away
  But, filters still apply...

## Slide 12: Virtual Hosting
The WWW protocol (HTTP 1.0) is broken
  Each web site requires an additional IP addresses, even though a single machine can host multiple web sites
  Results in a single machine having hundreds or thousands of addresses
Fixed in HTTP 1.1
  But a lot of browsers won’t understand 1.1 for a while

## Slide 13: Confederations/National NICs
APNIC and ARIN have an intermediate layer between the regional registry and the ISP
  Confederations of service providers, perhaps organized by national boundaries (national NICs)
Can provide better local support
  For the same reason the regional registries were created
Can contribute to the global routing load
  Unless the confederations only assign to ISPs

## Slide 14: Internet Protocol Version 6
People were (are) very worried about running out of address space
  232 just doesn’t go as far as it used to…
IPv6 fixes this problem and some others
  128 bits of address space
    340,282,366,920,900,000,000,000,000,000,000,000,000+ possible addresses
  Simplifies IP header, adds more easily processed options, includes “flow tags”
Prototype implementations available from most vendors
  ISPs less than enthusiastic
    IPv6 does not solve routing problems

## Slide 15: Summary
Internet Addresses are a critical resource managed via a hierarchy of allocation entities
  ISPs are the normal allocators for most
  Regional registries generally allocate to ISPs
Efficiency of use predominates concerns
  Primarily due to routability requirements
  Also concerns about availability of addresses
IPv6 resolves the availability issue
  But doesn’t address the routability issue