## Slide 1: Architecting the Network Part 2
Geoff Huston
  Chief Scientist, Internet
  Telstra
  ISOC Workshop

## Slide 2: Abstract Design
Router Interface design model

## Slide 3: The Client Interface

## Slide 4: The Client Interface
Single Homed Clients
  Permanently connected clients using any one of:
    leased line
    radio link
    permanent modem connection
  Client uses single service provider who offers the client a "default" network service
  Client's networks are advertised to the Internet exclusively via the provider

## Slide 5: The Client Interface
Clear demarcation of boundary between client and network is required for consistency of service
Single demarcation model is required for the network to ensure manageability and operability.
The network service should never transit a client network

## Slide 6: The Client Interface
The POP Access Model
  Client is responsible for CPE router and tail loop
  Network Provider provides router attachment points at a number of locations
  Network Boundary located at POP interface

## Slide 7: The Client Interface
The Comprehensive Service Model
  Network provider installs and operates CPE router and tail loop
  Network provider attaches to client LAN
  Network Boundary located at LAN attachment point

## Slide 8: The Client Interface
The Confused Model
  Network Provider installs tail loop
  Network Provider installs router interface card in client router
  Client and network provider operate client router simultaneously

## Slide 9: The Client Interface
POP or end-to-end service model depends on:
  telco bulk purchase tariff discounting
  router vendor bulk purchase discounting
  staff availability
  client expertise levels
  defined service level
Client Site service model is preferable from a commercial perspective

## Slide 10: The Client Interface
You can do both POP and end-to-end
  as long as all routing integrity is maintained within the POP locations for all clients
The integrity of the system is maintained within a set of "core" routers

## Slide 11: The Client Interface
The client has a network with some IP addresses
You operate a network with some IP addresses
How do you join these two networks together at the IP level?
This is a ROUTING problem

## Slide 12: The Client Interface

## Slide 13: The Client Interface
Choice of client boundary routing protocol
Use of RIP as Network / client boundary routing protocol?
   simple
   widely implemented
  NOT applicable in all cases
   no support for classless address exchange

## Slide 14: The Client Interface
Choice of client boundary routing protocol Use of RIPv2 as Network / client boundary routing protocol?  simple  not yet widely implemented NOT applicable in all cases  no support for classless address exchange

## Slide 15: The Client Interface
Choice of client boundary routing protocol
Use of STATIC ROUTES as Network / client boundary routing protocol?
   simple
   widely implemented
   can support classless address advertisements
   requires careful design to scale
   cannot support dynamic multi-homed connections

## Slide 16: The Client Interface
Choice of client boundary routing protocol
Use of Classless Client boundary routing protocol?
  EIGRP - proprietary B-F Distance Vector
  OSPF - IETF Std Link State
  RIPV2 - IETF Std B-F Distance Vector
  BGP4 - IETF Std Inter Domain Routing Protocol
Issue of clean separation between interior routing environment and client boundary routing environment may dictate use of BGP4

## Slide 17: The Client Interface
A proposed client interface routing architecture
  use static routes for all singly homed clients
  use statics of specifics plus aggregates for multiple connections to the same provider
  use BGP4 for multiply homed clients using multiple providers

## Slide 18: The Client Interface
Static routing
(plus sink)
single connection

## Slide 19: The Client Interface
Dynamic Routing Guidelines
  Use of inbound routing filters to preserve network integrity
    prevent client advertising bogus routes
    preserve integrity of client network

## Slide 20: The Client Interface
Dynamic Routing Guidelines
  Use of outbound static default route to simplify client routing
    stability of presented service
    simplicity of presented service
    client sees only an external default path

## Slide 21: The Client Interface
Dynamic routing
single connection

## Slide 22: The Client Connection
Routers provide:
  security capability
  management capability
    routing management
    traffic management
    service management
  efficiency
  integration

## Slide 23: The Client Connection
SLIP / PPP implementations in hosts
  cheap!
  Capital price differential between hosts and router is small
  Operating cost is higher using hosts as routers
use as single end host access system

## Slide 24: Routing to the Client
Multiple client interfaces
  split of client and provider network - multiple default paths
  asymmetric routes can be generated
  client network internal breakage causes black hole routing
requires careful management and clear understanding of the routing issues
need to use CIDR routing
to best advantage!

## Slide 25: Routing to the Client
Multiple providers
  Only one provider can provide "default"
  other connected providers must resort to explicit provision of routes to enumerated networks
  All providers must ensure that the client is not used as a transit facility through explicit route management on the part of all providers

## Slide 26: Distributed Client support
Virtual Private Network architecture issues
  VPNs via filtering - unwise!
  VPNs via tunnelling
  VPNs via MPLS

## Slide 27: Variations
Address translation technologies at the interface
Combined firewall / routing interfaces
Encryption at the interface

## Slide 28: Dial Access

## Slide 29: Dial Access Management
PSTN dial access
ISDN dial access
Support issues are similar:
user authentication and user access profile
accounting and billing records
infrastructure support for intermittent access

## Slide 30: Dial Access Components
Client Device
Dial Access
Server
Radius
Servers
Mail,
News
servers
Service Provider
Network

## Slide 31: Access Mechanisms
Modem banks
  entry level for small ISPs
  high management cost
ISDN Primary Rate access
  higher cost
  more reliable
  high manageability
  smaller size and power budget
  combine PSTN and ISDN service requirements

## Slide 32: Authenticating the User
PPP component of link setup
  pass authentication details to access server
  access server consults Radius servers
  Radius server providers answer:
    no / yes with profile loaded into access server
  Session accounting enabled
Radius Accounting provides per session accounting at session termination

## Slide 33: User Accounting
Collect session accounting record:
  user identification
  location of session service (server and port)
  start time
  duration
  session termination reason
  volume counters
  IP address assigned for session

## Slide 34: Address Management
Address Pools configured per ISDN PRI port
Dynamic address assignment per session
  this has service implications, as the client cannot assume a permanent name / address association
Client LAN connection is not readily supported
  dynamic route filter loading is required

## Slide 35: Client Services
Required Services
  Mail server
  POP access and account management
  Proxy Domain name services
  NEWS browser access
  WEB server access

## Slide 36: Other Services
Other services
  WEB proxy systems
  News servers
  ftp servers
  game servers
  ...

## Slide 37: Dial Access Services
Service Intensive Environment
  The Helpdesk is the major cost component of a dial access service
Highly Competitive Environment
  Small startup capital costs for new players
  Linking of equipment retail with access service
  High service margins are now a myth

## Slide 38: Dial Access Directions
commodity low margin market
virtual dial pops via L2 tunneling from CO telco port banks
QoS on dial access

## Slide 39: Other Access Models
Cable
  shared infrastructure
  speed matching
  third party ISP access
  voice / data integration
  integration with CATV rollout

## Slide 40: Other Access Models
xDSL
  non-uniform service model
  speed matching
  third party ISP access
  PSTN impact
  CATV impact
  IP infrastructure impact
  use existing copper infrastructure

## Slide 41: Other Access Models
wireless
  spread spectrum, packet radio, GSM data
  high utility model
  limited spectrum availability
  limited coverage with LOS earth facilities
  limited available bandwidth
  But no wires!