## Slide 1: Architecting the Network Part 3
Geoff Huston
  Chief Scientist, Internet
  Telstra
  ISOC Workshop

## Slide 2: Network Peer Interface

## Slide 3: Network Peer Interface
Who is my peer?
  Differentiating between:
    client network (they pay me!)
    service provider network (I pay them!)
    peer network (we pay each other!)
There are no Internet mechanisms to objectively determine who is a peer network!

## Slide 4: Network Peer Interface
Where do I peer?
  Onshore 1:1
  Onshore at a layer 2 exchange
  Offshore via Service Provider
  Offshore at a layer 2 exchange

## Slide 5: Network Peer Interface
Routing Considerations
  Export routes via BGP4 using CIDR
  Import routes using whatever works easily!
Operational Considerations
  Minimise bandwidth used by routing
  maximise operational stability

## Slide 6: Network Route Management
Obtain registered Autonomous System number (AS)
  from your Regional Registry
Generate aggregate mask which covers all announced networks
Announce CIDR aggregate to peer via BGP4 session

## Slide 7: Single Exterior Peer
Announce local nets via CIDR aggregate using BGP4
Synthesise static default route directed to exterior peer gateway

## Slide 8: Multiple Exterior Peers
Externally Imposed Policy differentiation
  For example:
    Academic & Research peer external network
    Commercial peer external network
Routing is Destination address-based - not source address
  Default route based on best policy match
  Explicit routes are imported from other network peers
  Traffic path based on destination net - not local source policy

## Slide 9: Multiple Exterior Peers
multi-default
routes
Explicit
routes
imported
via BGP4
Policy Matched CIDR
Aggregate announcement
statically configured in
exterior gateways

## Slide 10: Multiple Exterior Peers
Transit Arrangement
  Importation of transiting AS network numbers
  Announcement of transiting networks via AS path mechanism

## Slide 11: Exterior Peering
Importing a default route is cost effective and highly efficient as long as there is a suitable policy and capability match with the peer
Default-less routing is expensive, time-consuming, and can be unstable
Default-less routing allows greater levels of self-determination of policy - with an operational cost

## Slide 12: Exterior Peering
Use a simple model initially:
  Single exterior peer
  Derived default route
  Announce CIDR aggregate to peer

## Slide 13: Network Infrastructure

## Slide 14: Network Infrastructure
Bandwidth is a coarse control tool
link load

## Slide 15: Network Infrastructure
Engineer capacity for peak demand periods
Understand end-to-end flow patterns
Attempt to avoid sustained (> 15 minutes) acute congestion on any link
Constantly monitor bandwidth utilisation and flow patterns
Generate trend patterns and plan accordingly

## Slide 16: Network Infrastructure

## Slide 17: Network Infrastructure
Communications technology choices:
  Dedicated Facilities
    point to point leased circuit
    point to point radio
  Common Switched Facilities
    X.25
    Frame Relay
    SMDS access
    ATM

## Slide 18: Network Infrastructure
Leased circuit design
  Performance
  Reliability
  (In)Flexibility
  Cost

## Slide 19: Network Design

## Slide 20: Network Infrastructure
Hierarchy (Star) Topology
  + Minimal Cost
  + Simple Topology
  + Maximal efficiency
  - Critical points of failure

## Slide 21: Star Topology
Perth
Hobart
Brisbane
Sydney
Canberra
Melbourne
Adelaide
US
Darwin

## Slide 22: Network Design

## Slide 23: Network Infrastructure
Mesh Topology
  + Resiliency against link or site failure
  - Higher communications lease cost

## Slide 24: Mesh Topology
Perth
Hobart
Brisbane
Sydney
Canberra
Melbourne
Adelaide
US
Darwin

## Slide 25: Network Design

## Slide 26: Network Design
34Mb
45Mb
155Mb
155Mb
250Mb
155Mb
Telstra Internet Jun 2000
300Mb
300Mb
45Mb
400Mb
Telstra Internet Point of Presence
to USA
Hobart
Canberra
Sydney
Brisbane
Adelaide
Darwin
Perth
to NZ
to USA
20Mb
to Asian
Loc’ns
to USA
155 Mb
Melbourne
600Mb
45Mb
Auckland
34Mb

## Slide 27: Network Infrastructure
Hybrid - Resiliency via Dial-on-Demand
  Establish backup circuits using ISDN, X.25 or modems
  Issue of matching backup capacity against primary capacity

## Slide 28: Network Infrastructure
Access to common switched services
  X.25
  Frame Relay
  SMDS
  ATM

## Slide 29: Network Infrastructure
Frame and ATM issues
  Delivered Service contract (and enforceability)
  Tariff issues
  Dynamic vs static virtual channels
  Efficiency
  Congestion behaviour

## Slide 30: Network Infrastructure Design
Core routers driving major internal trunk lines
Edge Routers providing client connection point
Access Routers used on client site

## Slide 31: Routing within the Network
Choosing an Interior Routing Protocol
  RIP (V2)
  OSPF
  (E)IGRP
  IS-IS
Classless routing protocols are now essential for this domain

## Slide 32: Routing within the Network
Integrity and stability of the routing domain is essential
The routing protocol is not used to learn new routes
  authenticity of the route
  security and integrity of the routing domain
The routing protocol is only used to promulgate the route within the network

## Slide 33: Routing within the Network
Use of static routes to dampen down route flaps
  A transition of a route (up / down) causes all routers to undertake a cache dump and rebuild the route table from received routing information
  Route Flapping can destroy network performance

## Slide 34: Routing within the Network
One approach – used for scaleability
  Use OSPF as a link state maintenance protocol for the internal network infrastructure
  Use static routes at the edge for retail customer access
  Use eBGP for wholesale, peer and upstream accesss
  Use BGP route attributes to associate policy with the route
  Use I-BGP + default to carry customer routes in the Access net
  Use I-BGP to carry full routes in the Core net