## Slide 1: Architecting the Network Part 4
Geoff Huston
  Chief Scientist, Internet
  Telstra
  gih@telstra.net
Notes: This presentation was authored for the Internet Society's 1995 Workshop for Developing Countries.
The topic covered is the architecture issues concerned with the development of national network infrastructures, focusing specifically on the issues involved with developing countries, the the issues involved with the establishment of such infrastructure activity. The presentation looks at this from a perspective of the architecture of such systems.
There are a number of non-technical issues which touch on policy formulation at a national level which enable such activity. These are briefly summarised at the end of the presentation.
It is noted that this presentation is not intended to be a specific "cookbook" for the design and implementation of a national Internet network service - this presentation will cover various aspects of this task in very general terms. In this task there is no universal "right" or "wrong" way to undertake such activity. The following are very much views derived from the personal experience of constructing a national network infrastructure within Australia over the period from 1989 until 1995, and the associated experience of working with the Internet environment globally over this same period. It is readily acknowledged that whatever attempts at "guidelines" that are proposed within this presentation will, necessarily, be extensively modified within the practical environment of a particular nation or region, and accordingly the author cautions any reader to view the following more as a set of personal observations rather than a more substantive set of objective and rigid principles.
Bio Notes:
This presentation was written by Geoff Huston, who is the Network Technical Manager of the Australian Academic and Research Network (AARNet). He is one of the co-chairs of the IEPG, the Internet Service Operators' forum, and is a participant within the IETF community. He is also a member of the Board of Trustees of the Internet Society, and is currently the Secretary of the Society.

## Slide 2: Service Management
Use of router facilities to define service levels
  form of bandwidth management:
    transmission priority lists
    bandwidth class scheduling
  Can improve performance of defined services under load
Effectively such measures are within the area of "congestion management"
  The intent is to provide resources to some services when the bandwidth resource is under load

## Slide 3: Service Management
Priority Example:
  High priority on packets to and from port 23 (telnet) and 513 (rlogin)
  Low priority on packets to/from port 119 (net news)
Class Scheduling
  Allow telnet and rlogin up to 50% of available bandwidth when under contention
  Allow nntp up to 2% of bandwidth when under contention
Class Scheduling is a more stable approach to congestion management

## Slide 4: Network Operation
Management of IP numbers is critically important:
  Ensure network number registration information is accurate
  Publish correct IP numbers to external network peers
  Ensure that correct IP numbers are routed
  Ensure that end clients are using correctly allocated numbers

## Slide 5: Operation of a Service
Service Quality is achieved by a match of capability to demand:
  technical capability to carry traffic load
  financial capability to provide adequate resource
  Accurate and fast activation and service assurance processes

## Slide 6: Stitching it all Together
Site design and preparation
shipping
installation
end site training / interaction

## Slide 7: Site Design
Local LAN switch
Core Router
(backbone)
Client Access Systems
Analogue modem rack
ISDN modem rack
Leased circuit termination

## Slide 8: Site Design
Core
Network
to
customer
sites
Access Routers
LAN Switch
Network Services

## Slide 9: Site Design
FDDI Switch
Servers
Data Service
Termination
Units
DC/AC Inverters
Modem
Access Routers
Leased Line
Access Router
Servers
Backbone
Router

## Slide 10: Site Design
AC/DC power sources
Stability of power
Air Conditioning requirements
Site security and access arrangements
Access to spares
Expansion space

## Slide 11: Operational Management
All active elements of the network centrally managed
SNMP used as platform for management
routers are the central component of operations

## Slide 12: Operational Management
snmp traps used for exception reporting
never underestimate the power of ping !
traceroute - the route reporter
dig - DNS diagnosis

## Slide 13: Operational Management
Each management environment has particular requirements
Routers are the most reliable network element
carrier services are the greatest point of vulnerability
careful router configuration will isolate LAN faults

## Slide 14: Operational Management
Internet issues - working within a larger multi-provider environment:
  NOC obligations
  trouble ticket management

## Slide 15: Reporting
Goals of data collections and reporting:
  operational management
  trend analysis of traffic volumes
  monitor levels of delivered service
  monitor usage patterns
  marketing material!

## Slide 16: Reporting
Balance of cost of data collection and analysis against benefit of resultant data sets
Data collection points affect ability to gather data

## Slide 17: Reporting
Routers:
  Interface volumes
  Line errors
  routing tables
  router resource use
Routers
  15 minute interface volumes and error count

## Slide 18: Network Reports
weekly report of 15 minute link load levels
Notes: As noted in the section on internal infrastructure, datagram systems with reliable end to end protocols are very sensitive to congestion events, and to track network performance it is necessary to monitor the load of links at relatively short intervals on a continuous basis as the means of determining the frequency and severity of congestion events and monitoring average line loading levels.
Some work by the author, and similar efforts noted by the Operational Statistics Working Group of the IETF found that in general 15 minute sampling periods were sufficiently small to give good indication of such events while not entering areas of data overload. The technique generally used is o poll the interface statistics of each router every 15 minutes, and then post-process this data to produce link utilisation figures using the delta of these values for each measurement interval.

## Slide 19: Network Reports
monthly reports
quarterly trend reports and projections
Notes: Longer term reports are typically useful in terms of providing longer term prowth projections, and can be of assistance in forecasting trend levels for capacity.
Generally bandwidth requires some months of lead time on ordering, particularly when the capacity is in the megabit capacity level, and it is also noted that the process of funding such large expenditure items is a process which often must commence years in advance of the actual time of requirement - indeed this becomes a critical determinant when the capacity required from the network totally overwhelms the somewhat conservative growth projections undertaken by the telephone-based carriage providers.
It is therefore esstential to be able to analyse usage figures to the level of being able to deduce large scale trands in traffic growth, and to be able to extrapolate, with a sutiable level of approximation, at which stage in the future additional bandwidth (and additional elvels of expenditure) are required to ensure that the network operates outside of areas of catastrophic congestion-induced collapse or operates in an administrative or system-induced denial of service mode.
It is therefore essential to be able to generate forweard usage projections and map these projections into both future network capacity requirements and future network funding requirements, with a suitabally large period of forward notice which matches the managerial process associated with the network.
The typical experience is that given a sufficiently large measurement base the usage base exhibits relatively predictable movement trends which are invaluable for the capacity planning process.
They are also invaluable reports in the process of gathering funding for expansion in those cases where external funding is the basis of financial support for the network's infrastructure.
Additional r

## Slide 20: Network Reports

## Slide 21: Policy Considerations
The technology base of the network must match the commercial objectives of the enterprise – this match is often termed ‘policy’, where the network is configured to meet business demands
  Such business demands will vary network by network
Notes: There are two areas of consideration here
- the changing nature of the policy environment of the Internet itself, and
- the policy context of the development of national Internet infrastructures.
The first domain is the subject of a paper (by the author) presented at INET'94, and can be found at http://www.aarnet.edu.au/aarnet/organisation/gih/inet-94.html. Accordingly these notes will not be repeated here in detail. The observation is that the Internet, when viewed from a national perspective, is currently in the middle of three major sources of tension:
- the collaborative community who developed the Internet and pioneered its culture and usage (typically concentrating on the academic and research community within the national environment).
- the open market sector, who percieve this as a new market area which can be exploited. The highlight of the Internet from the perspective of this sector is the opening up of a new global market without the traditional costs of conventional marketing exercises
- the government sector, who have reached the point where they percieve the Internet as a critical component of the national environment's communications infrastructure, and seeking apprpriate regulatory models to ensure the achieval of national strategic objectives (ubiquity of service, affordability of service, rational consumption of public resources and internationally competitive positioning of domestic commerce and industry).
The paper notes that these tensions are largely unresolved in any national environment today, and that the near term future development of the Internet in each country, and globally, will be determined through the interplay of these tensions.
The following are very brief notes on the second policy domain (that of development of national Internet infrastructure).
The general consideration is the policy model for the construction of a national Internet network service. The "traditional" model (if traditions can be considered as traditions even if they are less than five year old experiences!) is that a national Internet service starts out as a university-sponsored academic and research facility with strong governmental involvement from the public academic and research arms of government, and attract little support from the national telephone communications operators.
This development then attracts other research players within the country, which in turn widens the brief of the facility, and places government money in a lose confederation with industry-based research funding.
The third step is the increasing level of interest by other national sectors, and typically the result is the genesis of other network service providers, as the constraints imposed by the publically-funded facility typically preclude commercial activities, and often noted in conjunction with this step is the belated visible interest on the part of the telephone companies to be involved in this area of the communications business.
For many of the developing economies this model is one which tends to be overly slow and inefficient, and results in a number of dramatic upheavals at distinct intervals in time as the context of the Internet changes at each step.
It is parhaps useful to learn from this experience, and structure the initial proprosals for the construction of such a facility as a program of national infrastructure, and attempt to construct an environment where there is a program which from the outset admits areas of funded commercial services in response to demand as well as the initial focus on servicing the inital areas of academic and research requirement for such services. Such a program is one which is more adaptible in the various stages of growth from a small specialized operation to a communications service enterprise, and allows development of the facility to proceed at a much faster pace than one which is constrained by a set of distinct restructing events at sequenced intervals.
Within this context government funding for the establishment of such a national Internet service is a step which must be considered carefully, as the constraints imposed by such funding often preclude smooth and efficient expansion of the service to meet an emerging national need. Creative partnerships with both the communications service providers, the academic and research sector and the supportive involvement of government as a facilitator rather than as a policy and agenda setting body would appear to match the rather pressing requirement for rapid infrastructure development in many countries.
The major objective of such facilities, as a longer term objective, is one of adding a new element to the national communications infrastructure inventory, and can be viewed as the establishment of a national asset which can lead to the enhanced productivity and efficiency of operation and international competiveness of both the academic and research sector as well as the commercial, industrial, governmetn and service sectors.
The result is the the instigators of the initial moves to establish an Internet service very quickly are drawn into a larger domain of policy determination at a national level - and it would appear that we are creating a new class of Internet citizen - the Internet Politician!

## Slide 22: Summary
Network Design defined by router interaction
  Client Service interface
  Network Peer interface
  Internal network design
Operational Considerations
Policy Considerations