## Slide 1: BGP4
1
Notes: 1

## Slide 2: Ravi Chandra
2
Cisco Systems Confidential
0799_04F7_c2
cisco Systems
Notes: 2

## Slide 3: Border Gateway Protocol (BGP)
Introduction to BGP
BGP Peer Relationship
BGP Attributes
Applying Policy with BGP
Putting it all together
Notes: 3

## Slide 4: Autonomous System (AS)
Collection of networks with same policy
Single routing protocol
Usually under single administrative control
AS 100
A
Notes: 4

## Slide 5: Autonomous System...
Identified by ‘AS number’
Examples:
  - service provider
  - multihomed customers
  - anyone needing policy descrimination
Notes: 7

## Slide 6: Terminology: Exterior routes
Routes learnt from other autonomous systems
Notes: 7

## Slide 7: What Is an IGP?
Interior Gateway Protocol
Within an Autonomous System
Carries information about internal prefixes
Examples—OSPF, ISIS, EIGRP…
Notes: 5

## Slide 8: What Is an EGP?
Exterior Gateway Protocol
Used to convey routing information between Autonomous Systems
Decoupled from the IGP
Current EGP is BGP
Notes: 6

## Slide 9: Why Do We Need an EGP?
Scaling to large network
  Hierarchy
  Limit scope of failure
Policy
  Control reachability to prefixes
Notes: 7

## Slide 10: Interior vs. Exterior Routing Protocols
Interior
  Automatic discovery
  Generally trust your IGP routers
  Routes go to all IGP routers
Exterior
  Specifically configured peers
  Connecting with outside networks
  Set administrative boundaries
Notes: 10

## Slide 11: Demilitarized Zone (DMZ)
AS 100
AS 101
AS 102
DMZ Network
A
B
C
D
E
Shared network between ASs
Notes: 11

## Slide 12: Static Routes
no path information
very versatile
low protocol overhead
high maintainance
very bad convergence time
requires manual configuration
Notes: 7

## Slide 13: BGP Basics
Runs over TCP
Path vector protocol
Incremental update
AS 100
AS 101
AS 102
E
B
D
A
C
Peering
Notes: 12

## Slide 14: General Operation
Learns multiple paths via internal and external BGP speakers
Picks the best path and installs in the IP forwarding table
Policies applied by influencing the best path selection
Notes: 13

## Slide 15: Internal BGP Peering
BGP peer within the same AS
Not required to be directly connected
IBGP neighbors should be fully meshed
AS 100
A
E
B
D
Notes: 14

## Slide 16: External BGP Peering
AS 100
AS 101
C
B
A
Between BGP speakers in different AS
Should be directly connected
Notes: 15

## Slide 17: Basic BGP commands:
router bgp <as-number>
neighbor <ip address> remote-as <as-number>
show commands
  - show ip bgp summary
  - show ip bgp neighbors
Notes: 7

## Slide 18: Exercise - 1
Define a static route
Bring the route into BGP table
Verify if route is in the BGP table
Notes: 7

## Slide 19: Exercise - 2
IBGP peering
Verify IBGP peering
Notes: 7

## Slide 20: Exercise - 3
EBGP peering
Verify EBGP peering
Notes: 7

## Slide 21: Stub Network
AS 100
AS 101
B
A
Notes: 40

## Slide 22: Stub Network
No need for BGP
Point default towards the ISP
ISP advertises the stub network
Policy confined within ISP policy
Notes: 41

## Slide 23: Multi-Homed AS
AS 100
AS 200
AS 300
D
C
B
A
Notes: 42

## Slide 24: Multihomed AS
Internal BGP used with IGP
IBGP only between border gateways
Only border gateways speak BGP
Exterior routes must be redistributed into IGP or use defaults
Notes: 7

## Slide 25: Common Service Provider Network
AS 100
AS 200
AS 400
AS 300
F
E
D
G
H
C
B
A
Notes: 49

## Slide 26: Service Provider Network
IBGP used to carry exterior routes
IGP carries local information only
Full IBGP mesh is required
Notes: 7

## Slide 27: Stable IBGP Peering
Peer with loop-back address
IBGP session is not dependent on a single interface
Loop-back interface does not go down
Notes: 38

## Slide 28: Peering to Loop-Back Address
AS 100
Notes: 39

## Slide 29: Exercise - 4
Stable IBGP peering
Verify IBGP peering
Notes: 7

## Slide 30: BGP - Update messages
withdrawn routes
attributes
advertised routes
Notes: 7

## Slide 31: BGP: Update Messages..
Network reachability information
network prefix/length
Example :
  - 131.108/16
    - 131.108.0.0 255.255.0.0
  - 198/8
    - 198.0.0.0 255.0.0.0
Notes: 7

## Slide 32: BGP Attributes
What is an attribute?
AS path
Next hop
Local preference
Multi-Exit Discriminator (MED)
Notes: 16

## Slide 33: BGP Attributes
BGP community
Others
Notes: 17

## Slide 34: What Is an Attribute?
Describes the characteristics of prefix
Transitive or non-transitive
Some are mandatory
Next Hop
AS Path
...
...
MED
...
Notes: 18

## Slide 35: AS-Path
Sequence of AS a route has traversed
Loop detection
Apply policy
AS 100
AS 300
AS 200
AS 500
AS 400
170.10.0.0/16
180.10.0.0/16
150.10.0.0/16
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200
150.10.0.0/16 300 400
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200
Notes: 19

## Slide 36: Exercise - 5
Look at live routing table
Notes: 7

## Slide 37: Next Hop
Next hop to reach a network
Usually a local network is the next hop in EBGP session
160.10.0.0/16
150.10.0.0/16
150.10.1.1
150.10.1.2
AS 100
AS 300
AS 200
150.10.0.0/16 150.10.1.1
160.10.0.0/16 150.10.1.1
A
B
20
Cisco Systems Confidential
0799_04F7_c2
Notes: 20

## Slide 38: Third Party Next Hop
192.68.1.0/24
150.1.1.3
150.1.1.1
150.1.1.2
192.68.1.0/24 150.1.1.3
AS 201
AS 200
C
A
B
More efficient
Notes: 21

## Slide 39: IBGP Next Hop
Next hop not changed
160.10.0.0/16
150.10.0.0/16
150.10.1.1
150.10.1.2
AS 100
AS 300
AS 200
A
B
C
150.10.0.0/16 150.10.1.1
160.10.0.0/16 150.10.1.1
Notes: 22

## Slide 40: Next Hop-More
IGP should carry route to next hops
Recursive route look-up
Unlinks BGP from actual physical topology
Allows IGP to make intelligent fowarding decision
Notes: 23

## Slide 41: Exercise - 6
IBGP nexthop exercise
Notes: 7

## Slide 42: Local Preference
AS 400
AS 200
160.10.0.0/16
AS 100
AS 300
160.10.0.0/16 500
> 160.10.0.0/16 800
500
800
E
B
C
A
D
Notes: 24

## Slide 43: Local Preference
Local to an AS
Used to influence BGP path selection
Path with highest local preference wins
Notes: 25

## Slide 44: Exercise - 7
Local Preference exercise
Notes: 7

## Slide 45: Multi-Exit Discriminator (MED)
AS 201
AS 200
192.68.1.0/24
C
A
B
192.68.1.0/24 1000
192.68.1.0/24 2000
Notes: 26

## Slide 46: Multi-Exit Discriminator
Non-transitive
Used to convey the relative preference of entry points
Influences best path selection
Comparable if paths are from same AS
IGP metric can be conveyed as MED
Notes: 27

## Slide 47: Origin
Conveys the origin of the prefix
Three values—igp, egp, incomplete
Influences best path selection
Notes: 28

## Slide 48: Communities
BGP attribute
Used to group destinations
Represented as an integer
Each destination could be member of multiple communities
Community attribute carried across ASs
Useful in applying policies
Notes: 30

## Slide 49: Community
AS 300
AS 200
160.10.0.0/16 1000
190.10.0.0/16 1000
170.10.0.0/16 1001
180.10.0.0/16 2000
170.10.0.0/16 1001
160.10.0.0/16 1000
180.10.0.0/16 2000
190.10.0.0/16 1000
AS 400
AS 100
AS 500
A
G
C
E
F
D
H
B
Notes: 31

## Slide 50: Applying Policy with BGP
Policy-based on AS path, community or the prefix
Rejecting/accepting selected routes
Set attributes to influence path selection
Notes: 32

## Slide 51: BGP Path Selection Algorithm
Do not consider IBGP path if not synchronized
Do not consider path if no route to next hop
Highest weight (local to router)
Highest local preference (global within AS)
Shortest AS path
Notes: 33

## Slide 52: BGP Path Selection
Lowest origin code
  IGP < EGP < incomplete
Multi-Exit Discriminator
  Considered only if paths are from the same AS
Prefer EBGP path over IBGP path
Notes: 34

## Slide 53: BGP Path Selection
Path with shortest nexthop metric wins
Lowest router-id
Notes: 35

## Slide 54: BGP Path Selection
BGP TABLE IN AS-201:
192.68.1.0/24 150.1.1.1
160.1.1.1
A’s IP TABLE:
192.68.1.0/24 150.1.1.1
B’s IP TABLE:
192.68.1.0/24 160.1.1.1
C’s IP TABLE:
Either one depending on IGP metric to nexthop
150.1.1.1
AS 201
AS 200
192.68.1.0/24
160.1.1.1
A
B
C
D
F
Notes: 36

## Slide 55: BGP Path Selection—More
AS 400
AS 200
AS 100
AS 300
B
A
D
AS 200 prefered path
AS 300 backup
Increase AS path length to 300
Notes: 37

## Slide 56: Multi-Homed AS
Many situations possible
  Multiple sessions to same ISP
  Secondary for only backup
  Load share between primary and secondary
  Selectively use different ISPs
Notes: 43

## Slide 57: Multiple Sessions to an ISP
EBGP to loopback address
EBGP prefixes learnt with loopback address as nexthop
Parallel paths to loopback address allows load sharing
ISP
44
Cisco Systems Confidential
0799_04F7_c2
AS 201
Notes: 44

## Slide 58: Multiple Sessions to an ISP
Simplest scheme is to use defaults
Learn/advertise prefix for better control
AS 201
ISP
D
F
A
B
45
Cisco Systems Confidential
0799_04F7_c2
Notes: 45

## Slide 59: Multiple Session to ISPs
Difficult to achieve load sharing
Point default towards one ISP
Learn selected prefixes from second ISP
Modify the number of prefixes learnt to acheive acceptable loadsharing
Notes: 47

## Slide 60: Putting it all together
Your network is going to grow at an exponential rate
Design to scale... but be prepared to reorganize from scratch
Don’t be afraid of change!
  - Most network redisigns are only configuration changes
Notes: 7

## Slide 61: Putting it all together
Requirements for IGPs for backbones
IGP connects your backbone together, not your client’s routes
Must
  - converge quickly
Should
  - carry netmask information
Notes: 7

## Slide 62: Putting it all together.. Connecting to a customer
Static routes
  - you control directly
  - no route flaps
Shared routing protocol or leaking
  - You must filter your customers info
  - route flaps
BGP for multihomed customers
Notes: 7

## Slide 63: Putting it all together Building your backbone
Keep it simple
redundancy is good, but expensive
use an IGP that carrys mask information
use an IGP that converges quickly
use OSPF, ISIS or EIGRP
Notes: 7

## Slide 64: Putting it all together Connecting to other ISPs
Use BGP4
advertise only what you serve
take back as little as you can
Notes: 7

## Slide 65: Putting it all together The internet exchange
Long distance connectivity is expensive
Connect to several providers at a single point
Notes: 7

## Slide 66: Q&A
Notes: 51