## Slide 1: Capacity Planning for Internet Service Networks
Geoff Huston
NTW Track4

## Slide 2: Issues
TCP/IP Protocol Behavior
Issues
Usage Profile
Capacity Guidelines
Growth Levels

## Slide 3: Planning Issues
Understand the domain of operation
  technical issues
  market issues
  competitive issues
  regulatory issues

## Slide 4: TCP/IP Protocol Issues
TCP/IP is NOT a flow damped protocol
  end to end flow management
  sliding window protocol
  adaptive flow rate designed to probe and use max available end to end bandwidth
  only limited by end system buffering size
    bandwidth x delay
  system buffers are getting larger as OS vendors come to understand the problem

## Slide 5: TCP/IP Protocol Issues
TCP/IP Data Flow Rate Adaptation
Time
Data Flow Rate
Steady State Available Bandwidth
Rate overflow loading
into network queues

## Slide 6: TCP/IP Protocol Issues
No network-based flow control mechanism
Network-based packet loss signals end systems to collapse transmission window size
Varying window size allows adaptive flow metrics to adapt to changing maximum available capacity
Sustained insufficient capacity leads to congestion induced collapse of data throughput

## Slide 7: TCP/IP Protocol Issues
Many simultaneous TCP sessions interact with non-predictive non-uniform load (ftp://thumper.bellcore.com/pub/dvw/sigcom93.ps.Z)
Peaks start to synchronize with each other
Buffering evens out individual flows, but buffers themselves behave with fluctuating load
Buffering adds latency

## Slide 8: TCP/IP Protocol Issues
TCP/IP efficiency under congestion load
Traffic Level
Data Throughput
33% 66%
33% 66%
Congestive Collapse -
The slide to misery
and packet loss

## Slide 9: TCP/IP Protocol Issues
TCP vs UDP
UDP-based applications
  Internet Phone, Video, Workgroup
UDP Issues
  no flow control mechanism
  sustained use forces precedence over TCP flows
  increasing use of flow bandwidth negotiated protocols for these applications (RSVP)

## Slide 10: TCP/IP Protocol Issues
Damping network capacity is not a demand management tool
Network capacity must be available to meet peak demand levels without congestion loss

## Slide 11: Usage Profile
Two major Internet use profiles:
  Business use profile
    peak at 1500 - 1600
    plateau 1000 - 1730
  Residential dial profile
    peak at 2030 - 2330
    plateau 1900 - 2400

## Slide 12: Usage Profile
Distance profiles
  12% Local
  18% Domestic Trunk
  70% International
Traffic mix due to:
  Distance invisible applications without user control
  Distance independent user tariff

## Slide 13: Capacity Guidelines
Link Utilisation
  Average weekly traffic level set to 50% of available bandwidth.
Core network capacity should be dimensioned according to aggregate access bandwidth

## Slide 14: Link Usage Profile - optimal
peak loading less than 10% time
greater than 50% loading for 50% time
traffic bursting visible

## Slide 15: Link Usage Profile - overloaded
90% peak loading for 45% time
60% peak loading for 60% time
no burst profile at peak loads
imbalanced traffic (import based)

## Slide 16: Link Usage Profile - saturated
visible plateau traffic load signature
small load increases cause widening plateau

## Slide 17: Overall Growth Levels
Two growth pressures:
  serviced population
  the changing Internet service model
    more network-capable applications
    using more bandwidth

## Slide 18: Overall Growth Levels
For a constant service model the growth curve will exhibit demand saturation

## Slide 19: Overall Growth Levels
For a changing service model the saturation point will move
More intense network use by increasingly sophisticated applications
Technology shift

## Slide 20: How to plan
Generate a market demand model
  forecast the number of services in operation
    existing services
    growth rate
    market capture level (competitive position)
  forecast the average demand per service
    dial access, leased line
    web, ftp, usenet
    caching trends
    new Internet services

## Slide 21: How to plan
demand models are typically very uncertain indicators
  high level of uncertainty of externalities
  highly dynamic competitive position
  poorly understood (and changing) service demand model

## Slide 22: How to plan
Forward extrapolation
  assume existing traffic follows a general growth model
  forward extrapolat the growth model
Good for short term planning (12 months)
Cannot factor
  latent demand
  market price sensivity

## Slide 23: Trend forecasting
historical usage vs capacity data

## Slide 24: Growth Trends

## Slide 25: Planning
undertake demand and trend forecast models
constantly review the model against generated usage data
recognise that the larger the capacity you need the longer the lead time to purchase it
recognise that the bigger the purchase the greater the requirement for capital