## Slide 1
Network Management
Who's the boss?
You or the network?

## Slide 2: Parts of Network Management
network management is not just keeping bits moving
OSI network management components
  fault management
  performance management
  security management
  configuration and name management
  accounting management
add policy-based management
reporting

## Slide 3: Fault Management
detect network problems
  transient/persistent
  failure/overload
detect server problems
isolating problems
reporting mechanism
  link to help desk
  notify on-call personnel
setup & control alarm procedures
repair/recovery procedures
ticket system

## Slide 4: Fault Management - Ticket System
system provides for:
  short term memory & communication
  scheduling and work assignment
  referrals and dispatching
  oversight
  statistical analysis
  long term accountability

## Slide 5: Fault Management - Ticket Usage
create a ticket on ALL calls
create a ticket on ALL problems
create a ticket for ALL scheduled events
copy of ticket mailed to reporter and mailing list(s)
all milestones in resolution of problem create a new ticket entry with reference to original

## Slide 6: Fault Management - Ticket Example
From nearnet-ops-request@nic.near.net Fri Dec 14 13:12:56 1990
  Received: from nic.near.net by nic.near.net id aa22499; 14 Dec
  Date: Fri, 14 Dec 90 13:01:42 EST
  From: ops@nic.near.net
  Subject: NEARnet Ticket #1582
  To: nearnet-ops@nic.near.net, nearnet-outages@nic.near.net,
  tmurphy@athena.mit.edu
  Status: R
  Ticket Number: 1582 Ticket Status: open
  Ticket Type: unplanned Ticket Source: email
  Ticket Scope: host Site/Line: mit
  Ticket Owner: perfetti Problem Fixer:
  Ticket Opened: 12/14/90 12:56 Problem Started: 12/14/90 11:20
  Problem Description:
  User is experiencing difficulty in reaching a host located at Rutgers. The host in question is quartz.rutgers.edu (128.6.4.8). This problem is being investigated.
  For a complete history of this ticket, do "finger ticket-1582@nic.near.net".

## Slide 7: Performance Management
evaluate the behavior of network elements
information used in planning
    interface stats
    throughput
    error rates
    software stats
    usage
    queues
    system load
    disk space
    availability per cent
    response time

## Slide 8: Security Management
security required to operate network and protect managed objects
security services
  Kerberos
  PGP key server
  secure time
security tools
  cops - host configuration checker (www.cert.org)
distribute security information
  bug reports
  bug fixes
  intruder alerts

## Slide 9: Security Management, cont.
reporting procedure for security events
  e.g. break-ins
control internal and external gateways
  control firewalls (external and internal)
security logs
privacy issues can be a conflict

## Slide 10: Configuration and Name Management
network state information
  network topology
  operation status of network elements
    including resources
  network element configuration
control network elements
  start/stop
  modification of network attributes
  addition of new features
configuration modification
  allocation and addition of network resources
  reconfiguration if dictated by link outages

## Slide 11: Config. Mgmt. - Network State Info.
e.g. SNMP driven display
nnhvd
husc6
harvard
geo
oitgw1
mghgw
sphgw1
wjhgw1
wjh12
generali
talcott
harvisr
huelings
pitirium
nngw
lmagw1
dfch
tch
tch

## Slide 12: SNMP
Simple Network Management Protocol
mostly a query - response system
little network traffic initiated by agent
currently only a primitive security system
  SNMPv2 was to have real security but working group fragmented, SNMPv3 now ready
uses database defined in MIB
can have "enterprise" extensions to MIB
SMI defines structure of MIB
SMI defines data structure using ASN.1

## Slide 13: ASN.1
ISO standard
specification of Abstract Syntax Notation One (ASN.1)
  defines a language used to describe data types
specification of Basic Encoding Rules for Abstract Notation One (ASN.1)
  defines a method for unambiguous transmission of data
machine architecture independent.
operating system independent.
network protocol independent.

## Slide 14: ANS.1 Data Encoding (TLV)
tag
  asn.1 data type
length
  length in octets
value
  value of data element
  format dependent on type
tag
length
value

## Slide 15: ANS.1 Data encoding, length
data element length field
if element length <= 126 octets
  actual tag value is in length octet with high bit = 0
  (value 127 is reserved)
if element length > 127 octets
  length made up of chunks of 7 bits per octet
  high bit in all but the last octet = 1
  high bit in the last octet = 0
tag
length
value
length
0

## Slide 16: ASN.1, Object Identifier
OBJECT IDENTIFIER
  sequence of integers that describe a pathway taken in traversing a tree of options, must be unique
  e.g.
  1.3.6.1.2.1.1.1
  or
  iso org dod internet mgmt mib system sysDescr
  the base of the tree is defined by ISO,
  sections are defined by other authorities

## Slide 17: SNMP, MIBII
iso
joint
citt
sysDescr
sysObjec tID
sysUpTime
sysContact
sysName
sysLocation
sysServices
system
interfaces
at
ip
icmp
tcp
udp
egp
transmission
snmp
mib-2
mgmt
internet
directory
experimental
private
enterprises
dod
memb
reg
std
org
reserved
Proteon
IBM
CMU
UNIX

## Slide 18: SNMP, cont.
defines three query messages to get information from an agent being monitored
defines a set message to be used in managing an agent
defines a response message for an agent to use in responding to a query or set message
defines a set of trap messages by which an agent can send notification of a status change to a management station
defines an inform message for reliable communications

## Slide 19: SNMP: Query Messages
GetRequest
  request to an agent to return the current value of a specific MIB variable can take more than one variable in one request.
GetNextRequest
  request to an agent to return the "next" MIB variable used to walk the tree in an agent
GetBulkRequest
  request to an agent to return large blocks of data

## Slide 20: SNMP: Set Message
SetRequest
  request to an agent to change the values of one or more MIB variables to specific new values.
  if there is an error in the SetRequest and one or more variables cannot be set, none will be set
error conditions
  1/ one or more objects not available for set operation, given access controls
  2/ contents of value field does not correspond to definition
  3/ size of response message would be larger than local limitations
  4/ some other reason a value cannot be altered

## Slide 21: SNMP: Response Message
Response
  message from an agent to a NMS in response to a GetRequest, a GetNextRequest or a SetRequest
  used to return requested values or to indicate success or failure of set request
  includes an error status and an error index

## Slide 22: SNMP: Trap Message
trap message:
  message from an agent to a NMS in response to a status change or event in the agent
trap conditions:
  coldStart
  warmStart
  linkDown
  linkUp
  authenticationFailure
  egpNeighborLoss
  enterpriseSpecific

## Slide 23: SNMP: InformRequest
like a “reliable trap”
designed to be used between network management stations
expanding to other uses
resent until acknowledged

## Slide 24: SNMP: Communities
provides trivial security
like a password
community name sent in clear over net with each message
some agents have more than one community for different access modes
  these are know as "views"
some agents can link access to community name and IP address of NMS

## Slide 25: SNMPv3
add security to SNMPv2
  secure SET support
  protect against
  modification of information
  masquerade
  message stream modification
  disclosure
  does not deal with
  denial of service
  traffic analysis

## Slide 26: SNMPv3, contd.
three levels of security
  no authentication, no privacy
  authentication, no privacy
  authentication & privacy
can support more than one security model
  user-based security model defined
  security based on “name” of a user
new message format
  to add security information
overview in RFC 2261

## Slide 27: Accounting Management
what do you account for?
if you count packets sent
  it can inhibit anonymous ftp & web sites
  QoS differences in the future
want to charge "user" of service
  application dependent determination of "user"

## Slide 28: Accounting, Cont.
could do settlements based in routing information
  try to minimize size of routing tables
telco model
  everyone shares in revenue
  call an 800 number from a pay phone
    800 destinations pays pay phone owner
  receive a long distance call to your own switch
    you get fee for local delivery

## Slide 29: getoctets
simple traffic stats collector
cron-driven shell procedure
  get-octets router1 router2 router3 ...
figures out interface list for each router
then gets
  ifInOctets, ifOutOctets, ifInUcastPkts, ifOutUcastPkts
  ifInNUcastPkts, ifOutNUcastPkts, system.sysUpTime
ftp://conrad.harvard.edu/pub/SNMPoll/octets.tar
  needs cmu snmp package

## Slide 30: getoctets, contd.
makes separate stats file for each interface
  example filename: 128.103.1.2.WJHgw1
example data
1997,06,23,160,09,1,00,02,37,EDT,1764089502,1045789221,99138769,92200835,10,628226,758006814
1997,06,23,160,09,1,00,22,37,EDT,1766362487,1047093977,99151676,92213338,10,628281,758126831
1997,06,23,160,09,1,00,42,36,EDT,1768439726,1048266407,99163118,92224546,10,628342,758246748
processing a bit hard
  must deal with counter wrap & router reboots
  sample period must be < 59 min for an Ethernet
link utilization calculation complex
  must include link encapsulation etc

## Slide 31: getoctets, processing
UpDate routine
  bug in 32 bit versions of perl (gives bad results)
example output
week millions of bits per second millions of octets
ending peak in peak out 95% in 95% out in out total
1997.06.01 5.0976 0.9330 1.3389 0.4104 18782 13752 32534

## Slide 32: Policy Based Management
want to manage the network not just network elements
define policy rules to tell network what to do
  e.g. network operations center gets access to all routers
  e.g. accounting department gets priority last 3 days of month
  e.g. max of 10% video on any link
policy rule gets translated into changes in configurations of devices

## Slide 33: Parts of a Policy-Based System
conceptual parts
  policy management tool
  used to create policy rules
  policy repository
  store policy rules
  policy consumer
  pushes policy rules (or translations) to policy target
  policy target
  functional element effected by policy rule

## Slide 34: Example Policy System
policy management stations
policy repository
policy consumers
policy targets

## Slide 35: Policy Sequence
rule defined
  check for static conflicts
  put in repository ( could use LDAP )
retrieved by policy consumers ( could use LDAP )
  processed to create configuration for policy target
  can use conceptual rather than actual interfaces
  e.g. “backbone interface”, “customer interface”
  can have time component
  pushed to policy targets
  using COPS or SNMP

## Slide 36: Policy Sequence, contd.
policy target
  installs configuration
  may have to translate conceptual to physical interfaces
  e.g. “customer interface” -> interfaces 1, 3 & 8
  e.g. “backbone interface” -> interfaces 2 & 7

## Slide 37: Management for Real
A few basic tools
echo request
  ping on IP
  function in many protocols - IP, OSI, AppleTalk, XNS
  checks path & basic node function
  can return round trip time
  normally not higher node function
      newdev> ping noc.barrnet.net
      PING noc.barrnet.net (131.119.245.5): 56 data bytes
      64 bytes from 131.119.245.5: icmp_seq=0. time=83. ms
      64 bytes from 131.119.245.5: icmp_seq=1. time=83. ms
      64 bytes from 131.119.245.5: icmp_seq=2. time=83. ms
      ^C
      ----noc.barrnet.net PING Statistics----
      3 packets transmitted, 3 packets received, 0% packet loss
      round-trip (ms) min/avg/max = 83/83/83

## Slide 38: Management for Real, Cont.
traceroute - finds path to node with delays
  function only in some protocols
    must have error returned on TTL exceeded
    golem> traceroute gatekeeper.dec.com
    traceroute to gatekeeper.dec.com (204.123.2.2), 30 hops max, 38 byte packets
    1 38.1.1.1 (38.1.1.1) 0 ms 0 ms 17 ms
    2 ipl-node17.camb.ma.cable.psi.net (38.127.88.1) 17 ms 0 ms 17 ms
    3 38.146.139.1 (38.146.139.1) 0 ms 17 ms 17 ms
    4 leaf.net121.psi.net (38.1.10.15) 50 ms 50 ms 33 ms
    5 38.1.2.16 (38.1.2.16) 101 ms 117 ms 133 ms
    6 San-Jose5.CA.ALTER.NET (137.39.29.1) 133 ms 283 ms 251 ms
    7 Palo-Alto1.CA.ALTER.NET (137.39.29.3) 133 ms 133 ms 100 ms
    8 Palo-Alto3.CA.ALTER.NET (137.39.47.7) 117 ms 100 ms 133 ms
    9 border-gwl.pa-x.dec.com (204.123.0.241) 117 ms 117 ms 100 ms
    10 gatekeeper.dec.com (204.123.2.2) 133 ms 117 ms 133 ms
    file: pub/net/jacobson/traceroute.tar.Z

## Slide 39: Management for Real, Cont.
network monitors/analyzers
local systems
  take unit to problem
  don't depend on working network
  wide range of cost & function
remote systems
  leave unit on problem or key network
  remote control & viewing of information
  SNMP standard from IETF RMON working group
privacy & security issues

## Slide 40: Management for Real, Cont.
management agents
  SNMP agents in all "gateway" devices
  SNMP agents in all servers
need something that knows what it is looking at it
  not all SNMP variables are the same

## Slide 41: Monitoring
simple monitoring tools do 95% of task
  e.g. ftp://conrad.harvard.edu/pub/SNMPoll
monitor should be both poll & trap based for best reliability
  but just polling will do better than just traps
  and will work fine other than response latency
simple, terse, messages on problems

## Slide 42: Example SNMPoll Error Messages
interface
Date: Mon, 16 Jun 97 09:11 EDT
From: SNMPoll@Conrad.Harvard.EDU
To: HDN-mail@Conrad.Harvard.EDU
Subject: FMD_175_No_Harva 128.103.245.1 down
FMD_175_No_Harva 128.103.245.1 down : Hamgw1 128.103.15.21 Eth 5 down at 09:11:03
router
Date: Fri, 13 Jun 97 17:17 EDT
From: SNMPoll@Conrad.Harvard.EDU
To: HDN-mail@Conrad.Harvard.EDU
Subject: MEEIgw1 not responding
MEEIgw1 not responding : No Response from 204.166.68.1 at 17:17:37

## Slide 43: SNMPoll
command to cause auto configuration
  needs config.seed
retries if failed poll of router
  reduce false error messages
understands hierarchy
  tries next step “back up” hierarchy if failed poll
query for many interfaces in same get_request
  minimize network traffic and router load

## Slide 44: Things to Look For
dup protocol addresses
  very bad in AppleTalk and IPX
network/link load
router/bridge
  CPU load
  errors
  drops!!
  interface resets
  collisions (if CSMA/CD network)

## Slide 45: Things to Do (Defensive)
filter
filter
filter

## Slide 46: Route Filtering
NAP
MCI
SPRINT
PSI
BBN Planet
MIT
dial-up
provider
in FL
MIT

## Slide 47: Problems
we are early in the Internet management game
  there is still a lot to learn
little AI
  not NETVIEW
prices still high for functionality
still gurus
data networks are not "plug and play" with large scale
nefarious people

## Slide 48: More Problems
not so good at providing simple, easy to understand, warning to non-gurus
mostly managing elements
  policy-based management should help
  but still monitoring elements - no “big picture”
needs to be usable by “normal” people
needs to say when users will complain