## Slide 1: Introduction to IP Routing
Geoff Huston

## Slide 2: Routing
How do packets get from A to B in the Internet?
A
B
Internet

## Slide 3: Connectionless Forwarding
Each router (switch) makes a LOCAL decision to forward the packet towards B
A
B
R1
R4
R2
R3
R6
R7
R5
R8

## Slide 4: Connectionless Forwarding
This is termed destination-based connectionless forwarding
How does each router know the correct local forwarding decision for any possible destination address?
  Through knowledge of the topology state of the network
  This knowledge is maintained by a routing protocol

## Slide 5: Routing Protocols
Distribute the knowledge of the current topology state of the network to all routers
This knowledge is used by each router to generate a forwarding table, which contains the local switching decision for each known destination address

## Slide 6: Routing Protocols
correct operation of the routing state of a network is essential for the management of a quality network service
  accuracy of the routing information
  dynamic adjustment of the routing information
  matching aggregate traffic flow to network capacity

## Slide 7: ISP Routing Tasks
Exterior routing
customers
internal
peer / upstream
Interior routing
Customer routing

## Slide 8: Interior Routing
discovers the topology of a network through the operation of a distributed routing protocol

## Slide 9: Path Selection
A
20
10
4
10
40
5
6
10
15
10
5
B
5
5
45
R1
R4
R2
R3
R6
R7
R5
R8
Minimum cost from A to B is 39 units

## Slide 10: Dynamic Path Adjustment
A
20
10
4
10
40
5
6
15
10
5
B
5
5
45
R1
R4
R2
R3
R6
R7
R5
R8
If R5 – R7 breaks, minimum cost path from A to B is
Now 46 units

## Slide 11: Interior Routing Protocols
describe the current network topology
Routing protocols distribute how to reach address prefix groups
Routing protocols function through either
  distributed computing model (distance vector)
  parallel computing model (link state)

## Slide 12: Routing Protocols
Distance Vector Routing Protocols
  Each node sends its routing table (dest, distance) to all neighbors every 30 seconds
  Lower distances are updated with the neighbor as next hop
  cannot scale
  cannot resolve routing loops quickly
  RIP is the main offender

## Slide 13: Routing Protocols
Link State Routing Protocols
  Each link, the connected nodes and the metric is flooded to all routers
  Each link up/down status change is incrementally flooded
  Each router re-computes the routing table in parallel using the common link state database
  OSPF is the main protocol in use today

## Slide 14: Suggestions
Just engineering a physical link does not ensure that traffic will flow
  some system somewhere must provide routing information about how to reach the newly connected network
Installing backup circuits is easy, making the routing work may not be

## Slide 15: Suggestions
need a clear understanding of how the client networks want their traffic to flow before you can start making routing configuration changes

## Slide 16: Interior and Exterior Routing Protocols
Exterior Routing Space
Interior
Route
Space
Interior
Route
Space
Interior
Route
Space
Interior
Route
Space
Interior
Route
Space
AS1
AS1221
AS2402
AS3561
AS701

## Slide 17: Exterior Routing Protocols
You tell me all the address prefixes you can reach, but don’t tell me the path you use to get there
  I’ll tell you the same
If anything changes, please let me know
If you tell me an address I’ll send you traffic destined to that address.
  If I tell you an address I will accept traffic destined to that address

## Slide 18: Exterior Routing Protocols
Border Gateway Protocol version 4 (BGP4)
Each interior route collection is described by an Autonomous System (AS) number
Internal topology is hidden
Routes are announced with associated AS value
  139.130.0.0/16 + AS 1221

## Slide 19: BGP example
AS 1221
AS 3561
139.130.0.0/16
203.10.60.0/24
148.10.0.0/16 3561
24.192.36.0/24 3561
202.23.45.0/23 3561
148.10.0.0/16
24.192.36.0/24
202.23.45.0/23
139.130.0.0/16 1221
203.10.60.0/24 1221

## Slide 20: BGP Example of TRANSIT
AS 1221
AS 3561
139.130.0.0/16 i
203.10.60.0/24 I
148.10.0.0/16 3561
24.192.36.0/24 3561
202.23.45.0/23 3561
210.10.0.0/16 3561,5727
139.1.0.0/16 3561,5727
148.10.0.0/16 i
24.192.36.0/24 i
202.23.45.0/23 i
210.10.0.0/16 5727
130.1.0.0/16 5727
139.130.0.0/16 1221
203.10.60.0/24 1221
AS 5727
210.10.0.0/16 i
130.1.0.0/16 I
148.10.0.0/16 3561
24.192.36.0/24 3561
202.23.45.0/23 3561
139.130.0.0/16 3561,1221
203.10.60.0/24 3561,1221

## Slide 21: Exterior Routing Protocols
Internal transit paths use I-BGP
AS 3561
AS 1221
AS 5727
A
B
Q: How does router A tell router B about AS1221 addresses?
A: Router A sets un an INTERIOR BGP session with router B

## Slide 22: Exterior Routing Protocols
AS 1
AS 2402
AS 1221
AS3561
AS 701
I-BGP
E-BGP

## Slide 23: Exterior Routing Protocols
Normally chose minimal AS path length
203.10.60.0/24 701,3561,1221
203.10.60.0/24 5727,1221
Selected path is via peer session to AS 5727 as this
Is 1 AS shorter that the other path

## Slide 24: Exterior POLICY
How can I share the traffic load between 2 or moreexterior providers?
How can I create a backup link to support my main exterior link?
You can bias minimal path selection by AS path filter lists or community attributes or local preferences

## Slide 25: Exterior Routing Protocols plus Policy
AS 1
AS 2402
AS 1221
AS 3561
AS 701
Accept AS paths
1221
2402
1221,3561
2402,701

## Slide 26: Exterior Routing Protocols plus Policy
policy settings control
  what you advertise to your immediate peers
  What you accept from your immediate peers
  What transits you will accept (send traffic)
you cannot control
  transit path of received traffic
  symmetry of transit policy