## Slide 1: Architecting the Network
Multiple Internet Service Providers
Notes: This presentation was formulated for the Internet Society's 1995 Workshop for Developing Countries, held in Honolulu, June 1995.
The topic covered is the architecture issues concerned with the development of national network infrastructures, focusing specifically on the issues involved with developing countries, the the issues involved with the establishment of such infrastructure activity. The presentation looks at this from a perspective of the architecture of such systems.
There are a number of non-technical issues which touch on policy formulation at a national level which enable such activity. These are briefly summarized at the end of the presentation.
It is noted that this presentation is not intended to be a specific "cookbook" for the design and implementation of a national Internet network service - this presentation will cover various aspects of this task in very general terms. In this task there is no universal "right" or "wrong" way to undertake such activity. The following are very much views derived from the personal experience of constructing a national network infrastructure within Australia over the period from 1989 until 1995, and the associated experience of working with the Internet environment globally over this same period. It is readily acknowledged that whatever attempts at "guidelines" that are proposed within this presentation will, necessarily, be extensively modified within the practical environment of a particular nation or region, and accordingly the author cautions any reader to view the following more as a set of personal observations rather than a more substantive set of objective and rigid principles.
Bio Notes:
This presentation was written by Geoff Huston, who is the Network Technical Manager of the Australian Academic and Research Network (AARNet). He is one of the co-chairs of the IEPG, the Internet Service Operators' forum, and is a participant within the IETF community. He is also a member of the Board of Trustees of the Internet Society, and is currently the Secretary of the Society.

## Slide 2: Provider Interaction
Policy Issues in a Multi-provider Environment
Notes: This presentation will treat the subject area within six broad areas -
- The definition of architectural principles for national network infrastructure
- The translation of such architectural principles into a design for a national network
- The generation of a specific engineering plan for the implementation and operation of the network service
- Implementation considerations
- Operational Considerations
- Some comments regarding the political environment of construction of national Internet services

## Slide 3: Multiple Providers
Either a starting condition or an early evolutionary phase, due to
  ease of access to technology
  increasing market perception of value
  Constraints on initial operations
You should anticipate an environment of multiple providers

## Slide 4: Multiple Providers
Are inevitable!
Plan for it within the areas of
  design
  policy
  business plans

## Slide 5: The Initial Model
Reselling
or
Coexistence

## Slide 6: Reselling
Purchase a service from a provider
Resell to high demand exposed markets, such as:
  commercial access
  community access
  dial-up
  school access
Reseller
Provider

## Slide 7: Reselling
Is an effective tool for Internet permeation
Increases the marketing presence
Increases purchased volumes of capacity for the upstream provider
  lowering unit price of bandwidth through increased volume

## Slide 8: Reselling
Shares the investment risk of Internet growth
Promotes rapid commercialisation of the Internet Service environment

## Slide 9: Reselling
May be counter to national regulatory environment
May be counter to funders’ requirements / constraints
May stress management function
May stress pricing structure
  fewer high volume low margin clients

## Slide 10: Reselling
Leads to direct competitive retail environment
May not be supportable within the size of the available market

## Slide 11: Reselling
For an academic Internet service provider the pressure to resell to service providers will commence on the second day!
  Cost escalation to academic clients through increased volume will be cross-subsidised by higher margins on reselling

## Slide 12: Coexistence
Multiple service providers
Each with Internet connectivity
Internet
A
B

## Slide 13: Coexistence
Independent Internet connectivity perceived as marketing advantage
Allows for Service Provider Operation to operate in a self-determined manner

## Slide 14: Independent Coexistence
Is not cost effective
Backhaul issue causes cost to both parties
Internet
A
B

## Slide 15: Independent Coexistence
Includes necessary areas of cooperative activity irrespective of link structure

## Slide 16: Areas of “Forced” Cooperation
National delegated namespace (.xx)
  structure of subdomains
  policy of subdomain creation
  inherited subdomain policy constraints
  agreed mode of operation via delegated authority
  accessibility of the domain name space as a prerequisite for Internet promulgation

## Slide 17: Cooperation (continued)
Network Address Management
  Service Provider Address Block management
  Reseller Address Block Management
  Customer switching
    address switching
    name service switching
  Reseller switching
    address block switching

## Slide 18: Cooperation (continued)
Dual Homed customers
  routing agreements
    advertisement to client
    advertisement to Internet
A
B

## Slide 19: Cooperation (continued)
Pricing policies
  competition vs collusion
Market domains
  competition v collusion
Regulatory Constraints
  data service reseller constraints
  commercial trading constraints

## Slide 20: Cooperative Coexistence
Attempts to rationalise costs to the benefit of all parties
Can be mutually cost effective
Can provide mutual failover for increased availability

## Slide 21: Cooperative Coexistence
Domestic Interconnection
Internet
A
B

## Slide 22: Exchange Structures
Layering
  layer 3 models
    multilateral policy determination!

## Slide 23: Exchange Structures
  layer 2 models (the NAP or IX)
    unilateral policy capability
    tailored bilateral policies

## Slide 24: Policy Issues
Client or Peer?
  Who determines peer status?
  How?
  Why?
How to price peering
  zero settlement only if equal perceived benefit to each party

## Slide 25: Policy Issues of Peering
risks
  leverage
  offloading
Both parties have to perceive equal benefit in order to peer

## Slide 26: Policy Issues
Internet
B
Who is an indirect party to peering?
  Transit networks
A
C

## Slide 27: Multiple Providers
Require careful consideration
Require flexibility in approach

## Slide 28: Discussion