## Slide 1: OSPF
1

## Slide 2: Today's Talk
Introduction
Distance Vector Protocol
Link State Protocol
OSPF operation
Neighbor & Adjacency
OSPF in broadcast networks
2

## Slide 3: Today’s Talk ...
Exercise-1
  simple OSPF network
Scalability
Exercise-2
  multiple areas
Redistribution
Exercise-3
  redistribution of routes
3
Notes: 4

## Slide 4
Introduction
Open Shortest First Path protocol
Preferred IGP
The myth : OSPF is hard to use
Evolved from IS-IS protocol
Link state protocol
4

## Slide 5
Distance Vector Protocols
Listen to neighboring routers
install routes in table, lowest distance wins
Advertise all routes in table
Very simple
Very stupid
5

## Slide 6
Distance Vector Protocols
6
A
B
C
D
E
F
G
H
I
A 1
B 1
C 1
G sup
H 1
A 2
B 2
C 2
D 1
E sup
F 1
G 1
H 1
I1

## Slide 7
Link State Protocols
information about adjacencies sent to all routers
each router builds a topology database
a "shortest path" algorithm is used to find best route
converge as quickly as databases can be updated
7

## Slide 8
Link State Protocols
8
A
B
C
D
E
F
G
1
2
A - 1 - G - 2 - D
H
I
3
router 1
A, B, C, G, H
router 3
H, I
router 2
D, E, F, G, I

## Slide 9
OSPF Operation
Every OSPF router sends out 'hello' packets
Hello packets used to determine if neighbor is up
Hello packets are small easy to process packets
Hello packets are sent periodically (usually short interval)
9

## Slide 10: The Hello Packet
Router priority
Hello interval
Router dead interval
Network mask
List of neighbors
FDDI
Dual Ring
Hello
Hello
Hello
10
Notes: 32
39

## Slide 11
OSPF Operation
Once an adjacency is established, trade information with your neighbor
Topology information is packaged in a "link state announcement"
Announcements are sent ONCE, and only updated if there's a change
  (or every 45mins...)
11

## Slide 12
OSPF Operation
Change occurs
Broadcast change
Run SPF algorithm
Install output into forwarding table
12

## Slide 13
Neighbor
Bi-directional OSPF communication
Result of OSPF hello packets
Need not exchange routing information
13

## Slide 14
Adjacency
Between OSPF neighbors
Exchange routing information
Point-to-point or Broadcast media
Point-to-point - neighbors are adjacent
Broadcast media - not all neighbors are
  adjacent
14

## Slide 15
Broadcast Media - problems
N neighbors - order of N square adjacency
Not optimal
Wasted bandwidth
Does not scale
15

## Slide 16
Broadcast Media
Select a neighbor - Designated Router(DR)
All routers become adjacent to DR
Exchange routing information with the DR
DR updates all the neighbors
Scales
Backup Designated Router
16

## Slide 17: Neighboring States
2-way
  Router sees itself in other Hello packets
  DR selected from neighbors in state 2-way or greater
DR
BDR
2-way
17
Notes: 35
42

## Slide 18: Neighboring States
Full
  Routers are fully adjacent
  Databases synchronized
  Relationship to DR and BDR
DR
BDR
Full
18
Notes: 36
43

## Slide 19: LSAs Propagate Along Adjacencies
LSAs acknowledged along adjacencies
DR
BDR
19
Notes: 38
45

## Slide 20: General cisco Concepts:
Ability to run multiple routing protocols in the same router
Same prefix could be learnt via more than one routing protocol
Adminstrative distance is used to discriminate between multiple source
Connected, Static and other dynamic protocols
20

## Slide 21
Exercise - 1: cisco configuration
console
‘?’ for help
command completion
‘show’ commands
‘show configuration’
‘configuration’ command
21

## Slide 22
Exercise - 1: cisco configuration
‘configure terminal’
Different modes
Example ‘interface ethernet 1’
  ‘ip address x.x.x.x m.m.m.m’
‘exit’ to exit a mode
‘show ip route’
‘show ip route x.x.x.x’
22

## Slide 23
Exercise - 1
Simple OSPF network
‘show ip route’
‘show ip ospf neighbor’
‘show ip ospf int’
‘show ip protocol’
‘show ip ospf database’
many debug commands
‘debug ip ospf ?’
23

## Slide 24
Exercise - 1
Simple OSPF network
‘network x.x.x.x m.m.m.m area <area-id>
‘m.m.m.m’ wildcard mask
‘0’ do not care bit
‘1’ check bit
‘0.0.0.0’ mask for exact match
‘network 203.167.177.10 0.0.0.0 area 0’
‘network 203.167.177.0 0.0.0.255 area 0’
24

## Slide 25
Exercise - 1
Simple OSPF network
Need to create OSPF routing process
  router configuration command
  ‘router ospf <process number>
Specify the network running ospf
Should also specify the area
25

## Slide 26
Exercise1 Verification:
26
show ip ospf
show ip ospf neighbor
show ip route
show ip route ospf
show ip ospf interface
show ip ospf database

## Slide 27
Scaling OSPF
Each link transition causes a broadcast and SPF run
OSPF can group routers to appear as one single router
OSPF areas
27

## Slide 28
OSPF areas (before)
28

## Slide 29
OSPF areas (after)
29

## Slide 30
Scaling OSPF
Rule of thumb: no more than 150 routers/area
Reality: no more than 500 routers/area
Backbone "area" is an area
Always ‘area 0’
Proper use of areas reduce bandwidth & CPU utilization
30

## Slide 31
Scaling OSPF
Route could be summarized are area
boundary
Instability is limited within each area
Divide and conquer
31

## Slide 32
Exercise - 2: OSPF with area
Use ‘network ... area <area-id> command
Each interface only in 1 area
Multiple areas per router
If more than on area, the router should be
in area 0
‘area 0’ used for inter-area traffic
32

## Slide 33
Redistribution
injecting route from other protocol
Often useful during transition
Need to be careful about feedback
Need to set metric
33