## Slide 1: packet filters using cisco access lists
Fri 19 June 97

## Slide 2
A packet filter is a set of rules that determine whether
a packet gets through an interface, or gets dropped.
permit <test 1>
deny <test 2>
deny <test 3>
permit <test 4>
(deny <everything else>)
rules are evaluated in order;
if test is true, action is taken;
if test is not true , go to next rule
Packet filters are inherently paranoid --
packets are denied if not explicitly allowed
Packet Filters

## Slide 3
Internet
Router
my net A
my net B
my net C
filters work here ...
...and here ...
Router
... in each direction, independently
in
out
Packet Filter Locations

## Slide 4
filter1 = {
deny any any any udp-port 69;
permit any any any any;
}
apply filter1 in interface 1;
apply filter1 out interface 1;
permit <src-ip, src-port> <dst-ip, dst-port>
deny <src-ip, src-port> <dst-ip, dst-port>
a packet filter rule looks like this:
to block TFTP packets:
Rules

## Slide 5
The IP Stack
Application
Transport
Internet
Network Interface
Network
Adjacent layers
Peer layers
00.00.0c.d6.d4.f7
169.222.31.42
TCP port 23
socket

## Slide 6
dst IP addr
src IP addr
Data
IP Header
169.222.30.4
169.222.31.42
IP Packet Encapsulation
src port
dst port
TCP
23
2034
IP Datagram
Packet is delivered from <src-ip, src-port> to <dst-ip, dst-port>
< 169.222.30.4 , 2034>
< 169.222.31.42 , 23>

## Slide 7
Internet
Router
my net A
my net B
my net C
block inbound packets with source IP addresses belonging to inside nets
A1.A2.A3.A4/24
B1.B2.B3.B4/29
C1.C2.C3.C4/24
filter2 = {
deny A1.A2.A3.A4/24 any any any;
deny B1.B2.B3.B4/29 any any any;
deny C1.C2.C3.C4/24 any any any;
permit any any any any;
}
apply filter2 in interface 0;
IP spoofing filters

## Slide 8
Internet
Router
my net A
my net B
my net C
A1.A2.A3.A4/24
B1.B2.B3.B4/29
C1.C2.C3.C4/24
Problem: net A can attack net B or C
Solution: Apply filters at all interfaces
But this leads to increased complexity of configuration; and
therefore increased maintenance and greater probability of
error.
IP spoofing filters (cont.)

## Slide 9
simple access-list filters
simple access lists (1-99) use only the source IP address:
permit src-ip mask
deny src-ip mask
e.g.:
access-list 1 permit 169.222.30.8
access-list 1 permit 169.222.30.9
access-list 1 permit 169.222.30.10
access-list 1 permit 169.222.30.11
access-list 1 permit 169.222.30.12
access-list 1 permit 169.222.30.13
access-list 1 permit 169.222.30.14
access-list 1 permit 169.222.30.14
access-list 1 deny any any
on the cisco documentation cd:
file:///cdrom/data/doc/software/11_1/rrout/4rip.htm#REF30724

## Slide 10
access-list 1 permit 169.222.30.9
access-list 1 permit 169.222.30.10
access-list 1 permit 169.222.30.11
access-list 1 permit 169.222.30.12
access-list 1 permit 169.222.30.13
access-list 1 permit 169.222.30.14
cisco wildcard masks
problem: access-lists must match long list of IP addresses;
too much work to type them all in:
solution: wildcard masks --
0 indicates that the corresponding bit in the address must
match the rule;
1 indicates “don’t care.”
access-list 1 permit 169.222.30.8 0.0.0.7

## Slide 11
access-list 1 permit 169.222.30.8 0.0.0.7
0000 1000
0000 0111
0000 1xxx therefore,
169.222.30.8 0.0.0.7
which includes: matches:
0000 1000 = .8 169.222.30.8
0000 1001 = .9 169.222.30.9
0000 1010 = .10 169.222.30.10
0000 1011 = .11 169.222.30.11
0000 1100 = .12 169.222.30.12
0000 1101 = .13 169.222.30.13
0000 1110 = .14 169.222.30.14
0000 1111 - .15 169.222.30.15
wildcard matching lists example

## Slide 12
more wildcard matching lists examples
169.222.30.0 0.0.0.255 matches 169.222.30.0/24
128.32.0.0 0.0.255.255. matches 128.32.0.0/16
10.0.0.0 0.0.255.255.255 matches 10.0.0.0/8
0.0.0.0 255.255.255.255 matches everything
169.222.31.42 0.0.0.0 matches 169.222.31.42

## Slide 13
extended access-list filters
extended access lists (100-199) use the source IP address,
destination IP address, protocol, destination port:
permit proto scr-ip mask op src-prt dst-ip mask op dst-port
deny proto scr-ip mask op src-prt dst-ip mask op dst-port
e.g.:
access-list 101 permit udp 169.222.30.8 0.0.0.7
169.222.31.42 0.0.0.0 eq 53
access-list 101 permit tcp 169.222.30.8 0.0.0.7
169.222.31.42 0.0.0.0 eq 53
access-list 101 deny ip 169.222.30.8 0.0.0.7
169.222.31.42 0.0.0.0
access-list 101 permit any any
on the cisco documentation cd:
file:///cdrom/data/doc/software/11_1/rrout/4rip.htm#REF24774

## Slide 14
cisco access-list filters
some shorthand notations can be used:
<ip-addr mask> = x.x.x.x 0.0.0.0
can be written as “host x.x.x.x”
so:
access-list 101 permit udp 169.222.30.8 0.0.0.7
169.222.31.42 0.0.0.0 eq 53
becomes:
access-list 101 permit udp 169.222.30.8 0.0.0.7
host 169.222.31.42 eq 53
<ip-addr mask> = x.x.x.x 255.255.255.255
can be written as “any”
so:
access-list 101 permit ip 0.0.0.0 255.255.255.255
0.0.0.0 255.255.255.255
becomes:
access-list 101 permit ip any any

## Slide 15
managing access lists
Access lists can become long; for example, more than 4
statements.
Since rules are evaluated in order, order is very important. It may
be necessary at times to change rules or re-order them.
Access lists cannot be (gracefully) edited on the router itself:
the only way to modify an existing rule is to delete it and add
the modified rule back. But deleting and adding an existing rule
has unexpected results.
Therefore, we need to edit access lists off-line, on a Unix host for
example. Later, we can copy it to the router.

## Slide 16
Access List Exercise #1 (slide 1/2)
We will create a short access list to prevent telnet from a host in
each row.
1. Select a host in your row for the exercise. Make sure you
know the host’s IP address.
2. Verify that the host can telnet to another host off the net,
i.e. a bsdi PC in a different row.
3. Telnet to the router and create the access list:
router(config)#access-list 101 deny tcp host <your-ip>
host <target-ip> eq 23
router(config)#access-list 101 permit ip any any
router(config)#^z

## Slide 17
4. Check it:
router#sho access-lists
5. Finally, apply the access-list to the router’s ethernet
interface on the row (e0).
router(config-if)#access-group 101 in
6. Verify that you can no longer telnet to the
other host.
7. To remove the access list:
router(config-if)#no access-group 101 in
Access List Exercise #1 (slide 2/2)

## Slide 18
Access List Exercise #2
We will create a short access list to prevent all telnets from a host.
1. Verify that your host can telnet to another host off the net,
i.e. a bsdi PC in a different row.
2. Telnet to the router and create the access list:
access-list 101 deny tcp host <your-ip> any eq 23
access-list 101 permit tcp any any
^z
3. Check it (think!) and apply to the router’s ethernet interface
as in the previous exercise.
4. Verify that you can no longer telnet to the other host.

## Slide 19
a more complicated example
Extended access lists allow some additional tests; see the page
on the cisco documentation cd (bottom of slide 13).
E.g. the “established” keyword tests whether the ACK or RST bit
is set in the TCP header. The first packet in a TCP open will not
match.
src
dst
SYN
SYN
ACK
ACK
ACK
DATA
ACK
ACK
DATA
ACK
ACK
DATA
ACK
ACK
FIN
ACK
FIN
ACK
open
established
close

## Slide 20
Access List Exercise #3 (slide 1/2)
We will create a short access list to prevent mail from
cyberpromo.com
access-list 111 permit tcp
205.199.212.0 0.0.0.255 any eq 25 established
access-list 111 deny tcp 205.199.212.0 0.0.0.255 any eq 25
access-list 111 permit tcp
205.199.2.0 0.0.0.255 any eq 25 established
access-list 111 deny tcp 205.199.2.0 0.0.0.255 any eq 25
access-list 111 permit ip any any
Apply access list 111 to in-bound packets on external
interface of your router. SMTP from cyberpromo is blocked,
SMTP to cyberpromo is not blocked.
Not really very effective.

## Slide 21
Access List Exercise #3 (slide 2/2)
On a PC with TFTP enabled, create a file in /tftp with these lines
(choose your own number for xxx):
access-list xxx permit tcp
205.199.212.0 0.0.0.255 any eq 25 established
access-list xxx deny tcp 205.199.212.0 0.0.0.255 any eq 25
access-list xxx permit tcp
205.199.2.0 0.0.0.255 any eq 25 established
access-list xxx deny tcp 205.199.2.0 0.0.0.255 any eq 25
access-list xxx permit ip any any
end
On your router, use copy tftp run to create the access list.
Examine the access list using show ip access-lists.
Install the access-list on the router:
router(config-if)#ip access-group xxx in

## Slide 22
other uses for access lists
- restricting route announcements
- restricting routes accepted
- controlling route redistribution between protocols
- in route-maps, for the above purposes
Access lists can be used for purposes other than packet filtering: