## Slide 1: Pricing the Internet
Geoff Huston
Notes: This presentation was formulated for the Internet Society's 1995 Workshop for Developing Countries, held in Honolulu, June 1995.
The topic covered is the architecture issues concerned with the development of national network infrastructures, focusing specifically on the issues involved with developing countries, the the issues involved with the establishment of such infrastructure activity. The presentation looks at this from a perspective of the architecture of such systems.
There are a number of non-technical issues which touch on policy formulation at a national level which enable such activity. These are briefly summarized at the end of the presentation.
It is noted that this presentation is not intended to be a specific "cookbook" for the design and implementation of a national Internet network service - this presentation will cover various aspects of this task in very general terms. In this task there is no universal "right" or "wrong" way to undertake such activity. The following are very much views derived from the personal experience of constructing a national network infrastructure within Australia over the period from 1989 until 1995, and the associated experience of working with the Internet environment globally over this same period. It is readily acknowledged that whatever attempts at "guidelines" that are proposed within this presentation will, necessarily, be extensively modified within the practical environment of a particular nation or region, and accordingly the author cautions any reader to view the following more as a set of personal observations rather than a more substantive set of objective and rigid principles.
Bio Notes:
This presentation was written by Geoff Huston, who is the Network Technical Manager of the Australian Academic and Research Network (AARNet). He is one of the co-chairs of the IEPG, the Internet Service Operators' forum, and is a participant within the IETF community. He is also a member of the Board of Trustees of the Internet Society, and is currently the Secretary of the Society.

## Slide 2: Issues Covered
Cost Identification
Pricing Policies

## Slide 3: Cost Identification
Cost elements for an Internet Service
  technical staff
  operational and support staff
  administrative overheads
  capital equipment
  data transmission costs
    domestic line leases
    international line leases
    ISP transit costs

## Slide 4: Cost Profile - non US
Typical recurrent costs
    national backbone carrier
    non-US
  staff & admin
    10%
  domestic leases
    30%
  international leases
    60%
  international transit
    <1%

## Slide 5: Cost Profile - non US

## Slide 6: Cost Profile
US profile has proportionally:
  lower international lease cost ($0!)
  lower domestic lease cost
  higher relative support staff cost

## Slide 7: Cost Profile - US
typical recurrent costs
    access provider
    non-backbone
    non US
  customer support and marketing
    50%
  access infrastructure
    20%
  domestic access to backbone
    25%

## Slide 8: Cost Profile - US

## Slide 9: Cost Profile - Backbone Net
Determining the unit cost of passing traffic over the network
  sum of unit costs for traffic over each circuit
  normalised by average end to end traffic profile

## Slide 10: Cost Profile
determining the unit cost of passing traffic over a circuit
  bidirectional or unidirectional?
  line occupancy pattern (peak to average)
  average sustainable line occupancy
Dial server usage pattern
Business usage pattern
0
12
24

## Slide 11: Cost Strategy
  avoid congestion on the circuit as a priority
    (actual unit cost of delivered data)
Average Traffic Level
Unit Cost
20%
60%
40%
80%

## Slide 12: Cost Strategy
leased circuit cost
  circuit lease cost must be fully defrayed at average circuit occupancy of 55% for a stable operating network.
  higher average occupancy is possible at the cost of peak load inefficiency
  lower average occupancy is under-subscription of the circuit resource.

## Slide 13: Worked Example
2Mbps circuit - lease cost of $150,000 per month
unit cost of data is 28.2 cents per Megabyte

## Slide 14: Worked Example
2Mbps can deliver 663,552 Mb in each direction per month
Total possible traffic level is 1,327,104 Mb in both directions
40% target line occupancy is 530,842 Mb
$150,000 divided by 530,842 is $ 0.28

## Slide 15: Worked Example
International line has double the cost
  you can’t get the other side to pay!
From previous example the unit cost of data is 56.4 cents per Megabyte

## Slide 16: Cost Profile Example
Type Proportion unit cost %total cost
of traffic
Intnl 65 1.00 89%
Dom 20 0.32 10%
Local 15 0.08 1%

## Slide 17: Cost Strategy
minimise International Lease costs
  tariff structure of decreasing unit cost with
    longer lease commitment
    higher volume circuit
  Note that the Minimum Investment Unit (MIU) of international cable systems is an E1 bearer
    major cost break leading to E1 size
    reduced cost break thereafter

## Slide 18: Cost Strategy
quantity over quality
  Frame Relay for lower speeds
quantity over diversity

## Slide 19: Cost Strategy
terminate at the cheapest useful full circuit location
  high volume termination locations are cheaper
  distance is not a significant factor
maximise useful circuit capacity
  secondary goal
  avoid the long delay pipe protocol behaviour
  use cable if marginal premium over satellite is small
  tend to cable for higher bandwidths

## Slide 20: Cost Strategy
Minimising International Lease cost is the most significant cost factor
Domestic lease cost can be significant
  similar factors apply here as with International leases

## Slide 21: International Access Costs
Connection Options
  Connect to “upstream” ISP
    Import default route
    Contract ISP to advertise your routes to Internet
    Cost highly variable
    Quality of default can be variable
    Purchase carefully!

## Slide 22: International Access Costs
Connect to an exchange point
  Can advertise your routes to all exchange peers
  Can import all announced routes to your network
This is not the same as importation of default
  You need to purchase transit at the exchange point in order to reach other exchange points
  same conditions apply

## Slide 23: Costs and Revenue
This is a growth industry
Cost containment is subsidiary to revenue growth
Effective marketing leads to
  higher revenue
  greater purchasing power
  lower unit costs

## Slide 24: Client Pricing
Objectives
  service provision
  cover costs?
  generate revenue?
  constrain / encourage use?
  competitive positioning

## Slide 25: Revenue Generation
constrained by policy objective of the network
initial revenue levels need to be offset against future growth potential within competitive environment
maintain revenue levels in line with investor expectation

## Slide 26: Constrain / Encourage Use
Must constrain use within a fixed funded or subsidised environment
  unrestricted growth of subsidised environment implies fundamental business failure within a cross-subsidised environment
Must constrain use if increased use does not generate increased funding and / or revenue

## Slide 27: Constrain / Encourage Use
Should encourage use within parameters of constant or improving
  income
  delivered quality of service
  unit cost of service provision

## Slide 28: Competitive Pricing
Must set pricing at a level which is
  comparable to competitive networks
  set by
    delivered service profile
    quality of delivered service
    investment profile
    desired return on investment
  Opportunity pricing is inherently unsafe as a longer term strategy

## Slide 29: Internet Service Pricing
Unit pricing is variable against target congestion level
The discriminent is quality
Variable perception of value of quality
price of services
service degradation

## Slide 30: Pricing Elements
  Access
  Time & Duration
  Volume
  Distance
Retail Price =
f(Access) + g(Time) + h(Volume) + j(Distance)

## Slide 31: Access Price
Normally varied by bandwidth
If used as sole price parameter then the provider relies on averaging across the client base
  Sophistication of client base implies increased usage at constant price
  Must be offset by constant growth
  ie access pricing must be offset by increased marketing costs and / or access to lower unit costs of bandwidth

## Slide 32: Access Pricing
flat fee based on bandwidth
  widely used (well, not so now)
  predictable billing for the customer
  low administrative overhead for provider
  increased marketing costs for provider
  no traffic shaping
    no incentive for shared caching to offset intnl lease costs

## Slide 33: Time-Based Pricing
only applicable to dial-up operation
scales with growth in dial-up market
widely used for dial access
  monthly access schemes are generally risk prone to over consumption
  per unit time charging difficult to market as the market matures
  monthly access plus timed overflow very common

## Slide 34: Volume Pricing
cannot measure “calls”
Sent or Received traffic?
Sent Volume
  reduces incentive to populate network with services (information provider pays to pass information to receiver)
Received Volume
  matches ftp & html usage
  poor match for email & telnet
  low incentive for cooperative infrastucture
    provider undertakes all dns, named, caches, etc

## Slide 35: Volume Pricing
Decision on Volume unit
  tens of gigabytes (virtual access bandwidth)
  megabytes (high sensitivity)
Traffic shaping by time of day
  peak / off peak pricing
  congestion / burst pricing

## Slide 36: Volume Pricing
Unit price on received gigabytes per month
Off Peak volume discount ?
increasing adoption within the Internet
scaleability
allows increasing revenue with increasing use to ensure constant delivered quality
  i.e. allows constant service integrity

## Slide 37: Distance-Based Pricing
Typically applied to volumes measured on a source to destination basis:
  local switching
  domestic transit
  international transit
requires traffic sniffing (scaling issues)
weakly manageable within the client environment

## Slide 38: Pricing Conclusions
No pricing (funding by external agencies or by multilateral client agreement) is typical starting position, but is very weak
Access Pricing is effective starting position, but is difficult to produce a stable outcome under growth pressure
Volume Pricing is stable, but requires careful positioning within current / future competitive market

## Slide 39: Discussion
Marketing Internet Services
  Cost containment vs revenue growth
  marketing as a measure to support pricing strategy
  plan ahead on demand levels, revenue and expenditure
Issues of marketing capabilities vs marketing data switching services

## Slide 40: Discussion
Pricing strategies in a competitive marketplace
What’s the objective?
What’s the regulatory position?